## Slide 1: TE4.3.1: Inter-layer SAO
Copyright © MediaTek Inc. All rights reserved.
Ximin Zhang, Shan Liu, Chih-Ming Fu and Shawmin Lei
JCTVC-L0212
Presented by Shan Liu
12th JCT Meeting in Geneva
14-23 Jan, 2013

## Slide 2: Outline
Introduction
  Inter-Layer SAO in JCTVC-K0033
Algorithm summarization
Results
Conclusions

## Slide 3: Inter-Layer SAO
Inter/Intra
Prediction
Interlayer
Prediction
-
Prediction
T/Q
IT/IQ
Reconstruction
Entropy
Coding
T/Q Residues
Inter/intra
Prediction
-
Prediction
T/Q
IT/IQ
Reconstruction
Entropy
Coding
T/Q Residues
In-loop Filter
In-loop Filter
Mode Decision
Mode Decision
Multiplex
Scalable Bitstream
Entropy
Coding
IL-SAO information
Up-Sampling
Base layer information
Enhancement Layer
Spatial
decimation
Base Layer
Input
IL-SAO

## Slide 4: Algorithm Summarization
Inter-layer SAO
  Re-use pixel classification and processing of base-layer SAO (same as SMuC0.1.1)
  A picture is divided into four regions or one picture is a region
  Each region selects one SAO type from (same as SMuC0.1.1)
    EO: 0-degree, 90-degree, 135-degree, 45-degree
    BO: starting band position
  Each SAO type signals four offsets.
  Encode IL-SAO parameters in slice header.
  Picture level on/off before the EL CTU encoding process

## Slide 5: Results (Inter-layer SAO)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -0.4% | -1.1% | -1.1% |  |  |  |  |  | 
Class B | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% |  |  | 
Overall (EL+BL) | -0.1% | -0.5% | -0.5% | -0.1% | -0.2% | -0.2% |  |  | 
Overall (EL) | -0.3% | -1.1% | -1.2% | -0.2% | -0.4% | -0.5% |  |  | 
Enc Time[%] | 100.0% |  |  | 100.2% |  |  |  |  | 
Dec Time[%] | 103.1% |  |  | 102.1% |  |  |  |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  |  |  | 
BL Match | Matched |  |  | Matched |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.6% | -1.0% |  |  |  | -0.6% | -1.0% | -1.4%
Class B | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.2% | -0.3% | -0.2%
Overall (EL+BL) | -0.2% | -0.3% | -0.4% | -0.1% | -0.2% | -0.2% | -0.3% | -0.5% | -0.5%
Overall (EL) | -0.5% | -0.6% | -0.9% | -0.2% | -0.5% | -0.4% | -0.7% | -1.3% | -1.4%
Enc Time[%] | 100.2% |  |  | 99.9% |  |  | 100.1% |  | 
Dec Time[%] | 103.8% |  |  | 101.3% |  |  | 103.6% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.8% | -1.1% |  |  |  | -0.7% | -1.2% | -1.6%
Class B | -0.2% | -0.6% | -0.5% | -0.2% | -0.6% | -0.6% | -0.5% | -1.0% | -0.9%
Overall (EL+BL) | -0.3% | -0.7% | -0.7% | -0.2% | -0.6% | -0.6% | -0.5% | -1.1% | -1.1%
Overall (EL) | -0.6% | -1.3% | -1.3% | -0.5% | -1.4% | -1.1% | -1.0% | -2.4% | -2.4%
Enc Time[%] | 100.4% |  |  | 99.7% |  |  | 100.1% |  | 
Dec Time[%] | 104.8% |  |  | 102.8% |  |  | 106.1% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
Thanks to Intel for crosscheck.

## Slide 6: Conclusion
JCTVC-K0033 proposed inter-layer SAO is implemented on SMuC0.1.1.
Results report
  Average 0.16%, 0.42% and 0.43% BD rate reduction for Y, U, V with 2x and 1.5x setting.
  Average 0.43%, 0.81% and 0.82% BD rate reduction for Y, U, V with SNR setting.
  Encoding time change is negligible, average decoding time is increased by 3%.
Recommend to support Inter-layer SAO in SMuC.

## Slide 7
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com