## Slide 1: Differential coding for RefIdx based scalability
JCTVC-L0213
Alireza Aminlou, Jani Lainema, Kemal Ugur, Miska Hannuksela

## Slide 2: Introduction
Intention
Introduce differential coding for RefIdx approach
  Add the high frequency information available on enhancement layer to base layer prediction
Maintain the ”HLS only changes” nature of RefIdx
  Do not modify the HEVC version 1 tools
  Do not add new slice level tools
  Only modify the reference picture list and buffer contructions
Approach
Put a differential picture to the reference picture buffer
Apply HEVC version 1 weighted prediction to perform the addition of differential reference picture to base layer
  ” P = B + D “

## Slide 3: Introduction

## Slide 4: Implementation
Differential reference picture contruction
Add an offset of 128 (for 8 bit video) to the differential pictures to be able to represent the differential values in between 0,255:
Di(x, y) = Clip ( Ri(x, y) – Bi(x, y) + 128 )
Reference picture list construction
Two enhancement layer references are removed from list 0 to make room for the new references (but leave at least one enhancement layer reference)
Two differential reference pictures are placed in list 0
  One corresponding to first ”normal” reference in list 0
  One corresponding to first ”normal” reference in list 1
One new base layer reference is placed in list 1

## Slide 5: Implementation
Example (POC = 4)
Example (POC = 16)
Ref pic list 0: | R0 | B4 | D0w2 | D8w2
Ref pic list 1: | R8 | R0 | B4 | B4w2
Ref pic list 0: | R8 | R6 | B16 | D8w2 |  | 
Ref pic list 1: | R8 | R6 | R4 | R0 | B16 | B16w2
Ref pic list 0: | R0 | R8 | B4 | 
Ref pic list 1: | R8 | R0 | B4 | 
Ref pic list 0: | R8 | R6 | R4 | R0 | B16 | 
Ref pic list 1: | R8 | R6 | R4 | R0 | B16 | 

## Slide 6: Implementation
Motion compensation
Performed by utilizing HEVC version 1 weighted prediction
Weight and offset setting
  Set to add the differential reference to base layer
  Set to deduct the offset added to the differential reference picture
  Could be freely selected by the encoder to optimize performance further
Basic operation: P = ( w0D + w1B + o0 + o1 ) >> 1
Selected weights: P = ( 2D + 2B -128 -128 ) >> 1
Result: P = B + ( D -128 )

## Slide 7: Results
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.2% | -2.4% | -2.5% |  |  |  | -1.1% | -2.8% | -3.1%
Class B | -0.6% | -2.4% | -2.7% | -1.0% | -2.8% | -3.0% | -1.2% | -3.0% | -3.2%
EL+BL | -0.8% | -2.4% | -2.6% | -1.0% | -2.8% | -3.0% | -1.2% | -2.9% | -3.2%
EL | -1.8% | -4.4% | -4.8% | -3.5% | -7.1% | -7.9% | -2.8% | -5.6% | -6.1%
Enc Time | 124.1% |  |  | 124.1% |  |  | N/A |  | 
Dec Time | 112.9% |  |  | 112.2% |  |  | N/A |  | 

## Slide 8: Summary
Proposed method provides tangible improvements in coding efficiency
  Average RA/EL+BL: -1.0 %
  Average RA/EL: -2.7 %
Fully compatible with the HLS RefIdx approach
  No new slice level tools
  Only modifications to reference picture list and buffer construction