## Slide 1
JCTVC-L0225: Video Sequence Characteristics Signaling in VPS and VPS Extension
Munsi Haque, Ali Tabatabai, Sachin Deshpande
Sony Electronics Sharp Labs of America

## Slide 2: Organization
Motivation for Mixed Video Sequences Signaling
VPS Extension Proposal
VPS – HEVC Version1 Proposal
Conclusion

## Slide 3: Motivation for Mixed Video Sequences Signaling
In scalable and multi-view extensions of HEVC various layers could be used to carry video sequences with mixed source characteristics in certain application scenarios.
Some possible application examples of mixed video sequences in broadcasting or network transmission:
  Frame structured video in Layer-1 and Field structured Video in Layer-2, where each video layer has its respective SPS
    Decoders can use one of the two layers based on its capability and preference
  Frame-structured video (2D) in Layer-1 and Frame-Compatible 3D video in Layer-2
    Legacy mono-view (2-D) decoder will use the Layer-1 video,
    An advanced frame-compatible 3D (3D) video decoder can use Layer-2 for 3D stereo-view video application.
VPS extension can signal information about the characteristics of such mixed video sequences
We propose to signal following mixed video sequence characteristics information about each layer in VPS extension:
  Source scan type information
  Source 2D / 3D information
  Source codec information
These proposed syntax elements can also be included in SPS of HEVC Extension

## Slide 4: Mixed Sequences Signaling Proposal (1/2)
mixed_video_present_flag syntax parameter equals 1 indicates presence of mixed video information syntax elements - source_scan_type_info_idc, source_2d_3d_info_idc, source_mixed_codec_flag, in VPS layers. If mixed_video_present_flag equals 0, no such mixed video syntax elements are present in the layers.

## Slide 5: Mixed Sequences Signaling Proposal (2/2)
source_scan_type_info_idc[i] | Video Layer Characteristics
0 | All pictures in layer i have interlaced scan type
1 | All pictures in layer i have progressive scan type
2 | Pictures in layer i have unknown scan type
3 | Pictures in layer i have a mixture of interlaced and progressive scan type
source_2d_3d_info_idc[i] | Video Layer Characteristics
0 | All pictures in layer i are 2D frames
1 | All pictures in layer i are packed in frame compatible 3D format
2 | Pictures in layer i have unknown frame packing arrangement
3 | Pictures in layer i have a mixture of frame compatible 3D and 2D frames
source_mixed_codec_flag / avc_base_codec_flag | Mixed video coding-type
0 | HEVC
1 | AVC
Note: The "source_mixed_codec_flag[i]" is set to 1 bit similar to "avc_base_codec_flag” in current VPS.
For future applications, this could be extended to more bits.

## Slide 6: Video Sequences Characteristics Signaling Proposal for VPS - for HEVC Version1
The source_scan_type_info_idc and source_2d_3d_info_idc syntax elements also can be used for the HEVC version1 in the video parameter set to signal video sequence characteristics.
The semantics of the syntax elements source_scan_type_info_idc and source_2d_3d_info_idc syntax elements are same as those of the syntax elements source_scan_type_info_idc[i] and source_2d_3d_info_idc[i] syntax elements except they apply to the base layer.
In addition to VPS the syntax elements source_scan_type_info_idc and source_2d_3d_info_idc could also be included in SPS for HEVC version1.

## Slide 7: Conclusion
We propose syntax and semantics in VPS extension to support signalling of information regarding mixed video sequences in various layers of HEVC scalable extension.
We also propose to include the source_scan_type_info_idc and source_2d_3d_info_idc syntax elements in HEVC version1, in the video parameter set to signal video sequence characteristics.
We propose adoption of the new syntax elements in VPS and VPS extension