## Slide 1
JCTVC-L0227: VPS extension with updates of profile_tier_level syntax structure
Munsi Haque
January 14, 2013

## Slide 2: On profile_tier_level syntax structure
“profile_tier_level” syntax structure contains a control (passing) parameter of “profilePresentFlag”
  In existing HEVC drafts, “profilePresentFlag = 1” for SPS, VPS and vps_extension()
This contribution has the following proposals
  A new control parameter “levelPresentFlag” together with “profilePresentFlag” to initialize all possible combinations of profile_tier and level syntax parameters
    next slide shows the merit of this new addition
  With this change, “profile_tier_level” syntax structure is used in in vps_extension() with 2 options
    for each VPS Layer
    for each Operating Point (OP)

## Slide 3: On Changes in profile_tier_level syntax structure
3
Observation:
profilePresentFlag enables restriction of profile and tier syntaxes for both general and sub-layer cases
No levelPresentFlag (current)
  No restriction on level_idc syntax possible in general cases, while sub_layer_level_present_flag restricts level_idc syntax in sub-layer cases
profilePresentFlag | sub-layer_profile_present_flag | levelPresentFlag | sub_layer_level_present_flag | Syntax parameters- General | Syntax parameters- Sub-layer
0 | - | 0 | - | - | -
0 | - | 1 | 0 | general_level_idc | -
0 | - | 1 | 1 | general_level_idc | sub_layer_level_idc
1 | 0 | 0 | - | general_profile_tier | -
1 | 1 | 0 | - | general_profile_tier | sub_layer_profile_tier
1 | 0 | 1 | 0 | general_profile_tier_level | -
1 | 1 | 1 | 1 | general_profile_tier_level | sub_layer_profile_tier_level
profilePresentFlag | sub-layer_profile_present_flag | NO levelPresentFlag | sub_layer_level_present_flag | Syntax parameters (General) | Syntax parameters (Sub-layer)
0 | - | - | 0 | general_level_idc | -
0 | - | - | 1 | general_level_idc | sub_layer_level_idc
1 | 0 | - | 0 | general_profile_tier_level | -
1 | 1 | - | 0 | general_profile_tier_level | sub_layer_profile_tier
1 | 0 | - | 1 | general_profile_tier_level | sub_layer_level_idc
1 | 1 | - | 1 | general_profile_tier_level | sub_layer_profile_tier_level
profile_tier_level( profilePresentFlag, levelPresentFlag, maxNumSubLayersMinus1 ) { | Descriptor
if( profilePresentFlag ) { | 
general_profile_space | u(2)
general_tier_flag | u(1)
general_profile_idc | u(5)
for( i = 0; i < 32; i++ ) | 
general_profile_compatibility_flag[ i ] | u(1)
general_reserved_zero_16bits [Ed. (GJS): Adjust semantics accordingly.] | u(16)
} | 
if( levelPresentFlag ) | 
general_level_idc | u(8)
for( i = 0; i < maxNumSubLayersMinus1; i++ ) { | 
if( profilePresentFlag ) | 
sub_layer_profile_present_flag[ i ] | u(1)
sub_layer_level_present_flag[ i ] | u(1)
if( profilePresentFlag && sub_layer_profile_present_flag[ i ] ) { | 
sub_layer_profile_space[ i ] | u(2)
sub_layer_tier_flag[ i ] | u(1)
sub_layer_profile_idc[ i ] | u(5)
for( j = 0; j < 32; j++ ) | 
sub_layer_profile_compatibility_flag[ i ][ j ] | u(1)
sub_layer_reserved_zero_16bits[ i ] | u(16)
} | 
if(levelPresentFlag && sub_layer_level_present_flag[ i ] ) | 
sub_layer_level_idc[ i ] | u(8)
} | 
} | 
profilePresentFlag | levelPresentFlag | Syntax parameters availability
0 | 0 | (Reference – Profile, Tier, LevelIdc)
0 | 1 | (Reference – Profile, Tier), LevelIdc
1 | 0 | Profile, Tier, (Reference – LevelIdc)
1 | 1 | Profile, Tier, LevelIdc
Use of both flags enables more flexibility in controlling parameter initialization
Observation:
levelPresentFlag (proposal)
  Allows level_idc syntax to change separately from Profile/Tier Parameter changes in general cases

## Slide 4: vps_extension update per Layer (Option-1)
JCTVC-K1007
  JCTVC-L0227: Layer-specific update
4
vps_extension( ) { | Descriptor
................ Edited .................................. | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) | 
profile_tier_level( 1, vps_max_sub_layers_minus1 ) | 
................ Edited .................................. | 
} | 
vps_extension( ) { | Descriptor
................ Edited .................................. | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) { | 
vps_profile_present_flag[ i ] | u(1)
vps_level_present_flag[ i ] | u(1)
profile_tier_level( vps_profile_present_flag[ i ], vps_level_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
if (!vps_profile_present_flag[ i ]) | 
vps_profile_ref_layer_num[ i ] | u(8)
else | 
vps_profile_ref_layer_num[ i ] = i | 
if (!vps_level_present_flag[ i ]) | 
vps_level_ref_layer_num[ i ] | u(8)
else | 
vps_level_ref_layer_num[ i ] = i | 
} | 
................ Edited .................................. | 
} | 
vps_profile_present_flag[ i ]: When this flag equal to 1 specifies the profile information for Layer i is present in the profile_tier_level( ) syntax structure; When this flag equal to 0 specifies that profile information for Layer i is not present in the profile_tier_level( ) syntax structure.
vps_profile_ref_layer_num[ i ]: When vps_profile_present_flag[ i ] equals to 0, profile information for Layer i is inferred to be equal to the profile information of the Layer indicated by vps_profile_ref_layer_num[ i ], a Layer-number used as an index to a Reference Profile-Tier-Level Look-up Table storing such information of previously sent Layers.
vps_level_present_flag[ i ]: When this flag equals to 1 specifies the level information for Layer i is present in the profile_tier_level( ) syntax structure; When this flag equals to 0 specifies that level information for Layer i is not present in the profile_tier_level( ) syntax structure.
vps_level_ref_layer_num[ i ]: When vps_level_present_flag[ i ] equals to 0, level information for Layer i is inferred to be equal to the level information of the Layer indicated by vps_level_ref_layer_num[ i ], a Layer-number used as an index to a Reference Profile-Tier-Level Look-up Table storing such information of previously sent Layers.

## Slide 5: vps_extension update per OP (Option-2)
JCTVC-K1007
  JCTVC-L0227: OP-specific update
5
vps_profile_present_flag[ i ]: When this flag equal to 1 specifies the profile information for Operation Point (OP) i is present in the profile_tier_level( ) syntax structure; When this flag equal to 0 specifies that profile information for OP i is not present in the profile_tier_level( ) syntax structure.
vps_profile_ref_op_num[ i ]: When vps_profile_present_flag[ i ] equals to 0, profile information for OP i is inferred to be equal to the profile information of the OP indicated by vps_profile_ref_op_num[ i ], a OP-number used as an index to a Reference Profile-Tier-Level Look-up Table storing such information of previously sent OPs.
vps_level_present_flag[ i ]: When this flag equal to 1 specifies the level information for OP i is present in the profile_tier_level( ) syntax structure; When this flag equal to 0 specifies that level information for OP i is not present in the profile_tier_level( ) syntax structure.
vps_level_ref_op_num[ i ]: When vps_level_present_flag[ i ] equals to 0, level information for OP i is inferred to be equal to the level information of the OP indicated by vps_level_ref_op_num[ i ], a OP-number used as an index to a Reference Profile-Tier-Level Look-up Table storing such information of previously sent OPs.
vps_extension( ) { | Descriptor
................ Edited .................................. | 
for( i = 0; i <= vps_num_op_sets_minus1; i++ ) { | 
vps_profile_present_flag[ i ] | u(1)
vps_level_present_flag[ i ] | u(1)
profile_tier_level( vps_profile_present_flag[ i ], vps_level_present_flag[ i ], vps_max_sub_layers_minus1 ) | 
if (!vps_profile_present_flag[ i ]) | 
vps_profile_ref_op_num[ i ] | u(8)
else | 
vps_profile_ref_op_num[ i ] = i | 
if (!vps_level_present_flag[ i ]) | 
vps_level_ref_op_num[ i ] | u(8)
else | 
vps_level_ref_op_num[ i ] = i | 
} | 
................ Edited .................................. | 
} | 
vps_extension( ) { | Descriptor
................ Edited .................................. | 
for( i = 1; i <= vps_max_layers_minus1; i++ ) | 
profile_tier_level( 1, vps_max_sub_layers_minus1 ) | 
................ Edited .................................. | 
} | 

## Slide 6: Conclusion
We propose new control flag addition with levelPresentFlag in profile_tier_level syntax structure
We also propose syntax and semantics for VPS extension to support profile_tier_level syntax structure with 2 possible options, either for each VPS Layer, or for each Operating Point of HEVC extensions.
We propose adoption of these new control flag and syntaxes in VPS extension design with either one of these 2 options.