## Slide 1: JCTVC-L0229 Inter-layer texture prediction for bit-depth and chroma format scalability
<number>
Do-Kyoung Kwon, Madhukar Budagavi and Minhua Zhou
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
Scalable coding tools are being evaluated using 8-bit YUV4:2:0 video in TEs
However, need to start investigating scalable coding of bit-depth and chroma resolution since
  High bit-depth video coding is already supported in HEVC version 1
  High chorma resolution video coding is studied in AHG7
In this contribution, inter-layer texture prediction (ILTP) is evaluated for the following scalable coding configurations as a starting point
  Bit-depth scalability
  Bit-depth + 1.5x spatial scalability
  Chroma scalability
  Chroma + bit-depth + 1.5x spatial scalability
Notes: <number>

## Slide 3: Inter-layer texture prediction (ILTP)
The CU-level inter-layer texture prediction turned out to be an effective tool for multi-loop scalable coding of 8-bit YUV4:2:0 sequences
Adopted in SMuC along with DCT-IF up-sampling filter
<number>
ME
MC
Intra
prediction
In-loop
Filter
Entropy
Enc.
Mode
Decision
EL bitstream
Recon for next
frame’s ME/MC
Original
EL CU
Reference
Frames
T/Q
DCT-IF
Up-sampler
Reconstructed
Base-layer Recon
Recon for next layer’s
Inter-layer intra prediction
ILP
Up-scaled
Base-layer CU
Recon
IQ/IT
- EL CU-level encoding with ILTP

## Slide 4: DCT-IF up-sampling filter in SMuC
Luma up-sampling filter
Chroma up-sampling filter
<number>
Phase shift | Luma up-sampling filter | Scaling factor
0 | { 0, 0, 0, 64, 0, 0, 0, 0} / 64 | 2x, 1.5x
1/3 | {-1, 4, -11, 52, 26, -8, 3, -1} / 64 | 1.5x
1/2 | {-1, 4, -11, 40, 40, -11, 4, -1} / 64 | 2x
2/3 | {-1, 3, -8, 26, 52, -11, 4, -1} / 64 | 1.5x
Phase shift | Chroma up-sampling filter | Horizontal, Vertical Scaling factor
0 | {0, 64, 0, 0}/64 | 2x H, 1.5x H
1/4 | {-4, 54, 16, -2}/64 | 1.5x V
1/3 | {-5, 50, 22, -3}/64 | 1.5x H
3/8 | {-6, 46, 28, -4}/64 | 2x V
1/2 | {-4, 36, 36, -4}/64 | 2x H
7/12 | {-4, 30, 43, -5}/64 | 1.5x V
2/3 | {-3, 22, 50, -5}/64 | 1.5x H
7/8 | { -2, 10, 58, -2 }/64 | 2x V
11/12 | {-1, 5, 62, -2}/64 | 1.5x V

## Slide 5: ILTP for bit-depth and chroma format scalability
ILTP with DCT-IF up-sampling filter is evaluated for bit-depth and chroma format scalability using SMuC and HM-8.0 AHG7 software as follows
<number>
Type of scalability | BL | EL | Software
Bit-depth | 1080p 8-bit YUV4:2:0 | 1080p 10-bit YUV4:2:0 | SMuC (0.1.1bf)
Bit-depth + 1.5x | 720p 8-bit YUV4:2:0 | 1080p 10-bit YUV4:2:0 | SMuC (0.1.1bf)
Chroma + Bit-depth | 1080p 8-bit YUV4:2:0 | 1080p 10-bit YUV4:2:2 | HM-8.0 AHG7
Chroma + Bit-depth + 1.5x | 720p 8-bit YUV4:2:0 | 1080p 10-bit YUV4:2:2 | HM-8.0 AHG7
- Scalable coding conditions for experiments

## Slide 6: Test sequences
1080p 10-bit YUV4:2:2 sequences
  Kimono1, ParkScene, BirdsInCage, DucksAndLegs, CrowdRun, OldTwoCross and Seeking
1080p 10-bit YUV4:2:0 sequences
  Generated by chroma down-sampling from “1080p10-bit YUV4:2:2”
1080p 8-bit YUV4:2:0 sequences
  Generated by bit shifting from “1080p 10-bit YUV4:2:0”
720p 8-bit YUV4:2:0 sequences
  Generated by spatial down-sampling from “1080p 8-bit YUV4:2:0”
<number>

## Slide 7: Up-sampling procedure
Adjust chroma scaling factors
  If there is chroma format change, chroma scaling factor is doubled
Bit-depth scaling
  If there is bit-depth change b/w BL and EL, each sample is left shifted first before spatial up-sampling
Spatial up-sampling
Adjust
chroma scaling factors
Horizontal up-sampling
Bit-depth
Scaling
Spatial
up-sampling
Vertical up-sampling
Bit-depth
Scaling
Spatial
up-sampling
<number>

## Slide 8: DCT-IF filter for chroma format scalability
Required chroma phases for up-sampling
  Horizontal and vertical 4x
    0, 1/4, 1/2 and 3/4
  Horizontal 3x
    0, 1/3 and 2/3
  Vertical 3x
    1/12, 5/12 and 3/4
<number>
2x
YUV4:2:2
YUV4:2:0
0
1/4
1/2
3/4
0
3/4
1.5x YUV4:2:2
1/12
5/12
3/4
3/4
1/12
Luma sample
Chroma sample
Upsampled luma sample
Upsampled chroma sample
Phase shift | Chroma up-sampling filter
1/12 | {-2, 62, 5, -1}/64
5/12 | {-4, 43, 30, -4}/64
3/4 | {-2, 16, 54, -4}/64

## Slide 9: Experimental results
<number>
Test 1: Bit-depth scalability, SMuC_0.1.1bf
BL – 1080p 8-bit YUV4:2:0, EL – 1080p 10-bit YUV4:2:0
 | AI HEVC BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -46.2% | -47.3% | -47.3%
Overhead over Single Layer | 4.6% | 4.0% | 4.1%
Overall (EL) | -93.2% | -96.1% | -96.2%
Enc Time[%] | 105.7% |  | 
Dec Time[%] | 104.0% |  | 
BL Match | Matched |  | 
 | RA HEVC BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -41.0% | -40.4% | -39.9%
Overhead over Single Layer | 12.9% | 18.9% | 20.5%
Overall (EL) | -83.0% | -84.8% | -84.7%
Enc Time[%] | 115.6% |  | 
Dec Time[%] | 136.1% |  | 
BL Match | Matched |  | 
 | LD-P HEVC BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -37.2% | -37.7% | -37.2%
Overhead over Single Layer | 18.6% | 22.4% | 24.5%
Overall (EL) | -76.0% | -79.8% | -79.4%
Enc Time[%] | 117.1% |  | 
Dec Time[%] | 143.8% |  | 
BL Match | Matched |  | 
Notes: <number>

## Slide 10: Experimental results
<number>
Test 2: Bit-depth + 1.5x spatial scalability, SMuC_0.1.1bf
BL – 720p 8-bit YUV4:2:0, EL – 1080p 10-bit YUV4:2:0
 | AI HEVC BitDepth + 1,5x |  | 
 | Y | U | V
Overall (EL+BL) | -35.2% | -35.5% | -35.7%
Overhead over Single Layer | 7.1% | 6.3% | 5.9%
Overall (EL) | -62.8% | -62.7% | -63.1%
Enc Time[%] | 109.0% |  | 
Dec Time[%] | 104.4% |  | 
BL Match | Matched |  | 
 | RA HEVC BitDepth + 1.5x |  | 
 | Y | U | V
Overall (EL+BL) | -26.7% | -20.3% | -19.8%
Overhead over Single Layer | 20.2% | 31.4% | 32.3%
Overall (EL) | -48.5% | -36.5% | -35.6%
Enc Time[%] | 109.3% |  | 
Dec Time[%] | 132.4% |  | 
BL Match | Matched |  | 
 | LD-P HEVC BitDepth + 1.5x |  | 
 | Y | U | V
Overall (EL+BL) | -19.8% | -15.3% | -14.5%
Overhead over Single Layer | 30.7% | 37.6% | 39.0%
Overall (EL) | -37.2% | -28.0% | -26.6%
Enc Time[%] | 109.1% |  | 
Dec Time[%] | 142.2% |  | 
BL Match | Matched |  | 
Notes: <number>

## Slide 11: Experimental results
<number>
Test 3: Chroma format + Bit-depth, HM-8,0 AHG7
BL – 1080p 8-bit YUV4:2:0, EL – 1080p 10-bit YUV4:2:2
 | AI HEVC Chroma + BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -37.3% | -41.1% | -40.3%
Overhead over Single Layer | 9.9% | 12.7% | 16.4%
Overall (EL) | -69.3% | -80.9% | -81.0%
Enc Time[%] | 101.0% |  | 
Dec Time[%] | 86.9% |  | 
BL Match | Matched |  | 
 | RA HEVC Chroma + BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -28.5% | -33.1% | -29.9%
Overhead over Single Layer | 25.4% | 32.9% | 42.6%
Overall (EL) | -54.7% | -68.3% | -63.9%
Enc Time[%] | 92.2% |  | 
Dec Time[%] | 103.3% |  | 
BL Match | Matched |  | 
 | LD-P HEVC Chroma + BitDepth |  | 
 | Y | U | V
Overall (EL+BL) | -17.3% | -28.5% | -24.8%
Overhead over Single Layer | 45.3% | 43.5% | 55.9%
Overall (EL) | -34.8% | -59.0% | -54.0%
Enc Time[%] | 94.2% |  | 
Dec Time[%] | 108.0% |  | 
BL Match | Matched |  | 
Notes: <number>

## Slide 12: Experimental results
<number>
Test 4: Chroma format + Bit-depth + 1.5x spatial, HM-8,0 AHG7
BL – 720p 8-bit YUV4:2:0, EL – 1080p 10-bit YUV4:2:2
 | AI HEVC Chroma + BitDepth + 1.5x |  | 
 | Y | U | V
Overall (EL+BL) | -29.3% | -32.5% | -32.2%
Overhead over Single Layer | 8.7% | 2.0% | 3.6%
Overall (EL) | -47.8% | -51.6% | -52.0%
Enc Time[%] | 107.8% |  | 
Dec Time[%] | 88.1% |  | 
BL Match | Matched |  | 
 | RA HEVC Chroma + BitDepth + 1.5x |  | 
 | Y | U | V
Overall (EL+BL) | -20.1% | -21.8% | -19.6%
Overhead over Single Layer | 23.8% | 19.6% | 23.8%
Overall (EL) | -34.1% | -35.1% | -31.9%
Enc Time[%] | 91.5% |  | 
Dec Time[%] | 102.4% |  | 
BL Match | Matched |  | 
 | LD-P HEVC Chroma + BitDepth + 1.5x |  | 
 | Y | U | V
Overall (EL+BL) | -12.1% | -17.2% | -14.9%
Overhead over Single Layer | 37.2% | 26.8% | 31.3%
Overall (EL) | -21.2% | -28.0% | -25.0%
Enc Time[%] | 93.5% |  | 
Dec Time[%] | 106.5% |  | 
BL Match | Matched |  | 
Notes: <number>

## Slide 13: Conclusions
<number>
Inter-layer texture prediction (ILTP) is evaluated for bit-depth and chroma format scalability
ILTP showed decent gain even for combined scalability of bit-depth, chroma format and spatial resolution
  46.2% ~ 29.3% for AI, 41.0% ~ 20.1% for RA, 37.2% ~ 12.1% for LDP
Suggest to start investigating scalable coding of bit-depth and chroma format in CE
Notes: <number>