## Slide 1: JCTVC-L0231 Inter-layer slice header syntax element prediction in SHVC
<number>
Do-Kyoung Kwon, Madhukar Budagavi and Minhua Zhou
Texas Instruments Inc.
Notes: <number>

## Slide 2: Overview
<number>
In many cases, scalable layers are coded using the same GOP structure
  Pictures at the same temporal position usually have the same slice type and temporal references
  Same RPS can be used, and WP parameter could be shared
Propose to signal in a slice header whether RPS and WP parameters are inferred from a reference layer
Notes: <number>

## Slide 3: Inter-layer RPS prediction
<number>
Propose inter_layer_rps_prediction_flag in the enhancement-layer SH
  If it is set equal to 1, RPS and reference picture list modification syntax elements are inferred from a collocated reference-layer SH
  Collocated reference-layer slice header is the SH that includes the collocated CU of the first LCU of the EL slice.
slice_header( ) { | Descriptor
…… | 
if( !IdrPicFlag ) { | 
pic_order_cnt_lsb | u(v)
inter_layer_rps_prediction_flag | u(1)
if (!inter_layer_rps_prediction_flag) | 
{ | 
short_term_ref_pic_set_sps_flag | u(1)
if( !short_term_ref_pic_set_sps_flag ) | 
short_term_ref_pic_set( num_short_term_ref_pic_sets ) | 
else | 
short_term_ref_pic_set_idx | u(v)
if( long_term_ref_pics_present_flag ) { | 
...... | 
} | 
} | 
} | 
…… | 
if( slice_type = = P ¦ ¦ slice_type = = B ) { | 
if( sps_temporal_mvp_enable_flag ) | 
slice_temporal_mvp_enable_flag | u(1)
if (!inter_layer_rps_prediction_flag) | 
{ | 
num_ref_idx_active_override_flag | u(1)
…… | 
if( lists_modification_present_flag ) | 
ref_pic_list_modification( ) | 
} | 
if( slice_type = = B ) | 
mvd_l1_zero_flag | u(1)
…… | 
} | 
…… | 
} | 
Notes: <number>

## Slide 4: Inter-layer WP param prediction
<number>
Propose inter_layer_wp_prediction_flag in the enhancement-layer SH
  If it is set equal to 1, WP parameters for all references are inferred from a collocated reference-layer SH
slice_header( ) { | Descriptor
…… | 
if( ( weighted_pred_flag && slice_type = = P) ¦ ¦ ( weighted_bipred_flag && slice_type = = B ) ) | 
{ | 
inter_layer_wp_prediction_flag | u(1)
if (!inter_layer_wp_prediction_flag) | 
pred_weight_table( ) | 
} | 
…… | 
} | 
Notes: <number>

## Slide 5: Conclusion
<number>
Pictures at the same temporal positions usually share many properties in common
Propose to signal whether RPS and WP parameters are inferred from a reference layer
  inter_layer_rps_prediction_flag and inter_layer_wp_prediction_flag
The proposed flags help reducing overhead signaling especially when scalable layers are coded using the same GOP structure, which is common
Notes: <number>