## Slide 1: AHG6: On deblocking filter and parameters signaling
JCTVC-L0232
Andrey Norkin, Kenneth Andersson, Rickard Sjöberg
Ericsson
Notes: 2010-10-07
Ericsson AB 2010
<number>

## Slide 2: Frame varying deblocking parameters AHG6 (configuration file change)
As a mandate of AHG6 (in-loop filtering) it has been proposed to determine deblocking parameters signalled for each frame in the GOP structure
The following parameters are proposed for Low Delay:
# Type POC QPoffset QPfactor tcOffsetDiv2 betaOffsetDiv2
Frame1: B 1 3 0.4624 5 0
Frame2: B 2 2 0.4624 3 0
Frame3: B 3 3 0.4624 5 0
Frame4: B 4 1 0.578 1 0

## Slide 3: Parameters proposed to random access configuration
# Type POC QPoffset QPfactor tcOffsetDiv2 betaOffsetDiv2
Frame1: B 8 1 0.442 1 0
Frame2: B 4 2 0.3536 3 0
Frame3: B 2 3 0.3536 4 0
Frame4: B 1 4 0.68 6 0
Frame5: B 3 4 0.68 6 0
Frame6: B 6 3 0.3536 4 0
Frame7: B 5 4 0.68 6 0

## Slide 4: Lambda dependence on QP (QP 27, 32, 37) Low Delay

## Slide 5: Lambda dependence on QP (QP 27, 32, 37) Random Access

## Slide 6: Decisions for HEVC strong deblocking filter
Stronger filter decisions in HEVC
Example of block boundary in Riverbed
Current strong filter is turned off here

## Slide 7: Proposed changes for strong filter decisions

## Slide 8: Proposed decision for strong filtering
Decisions allow application of strong filtering on the inclined surfaces

## Slide 9: HEVC strong filter applied to ramp
When applied to slow varying signal, e.g. ramp, HEVC strong filter creates a wave

## Slide 10: Proposed modifications to strong filter

## Slide 11: Proposed filter applied to ramp

## Slide 12: Proposed restriction on 32x32 TU in inter slices (non-normative)
However, after the proposed modification, large 32x32 intra blocks are still visible on sequences like RedKayak in the frames up in the coding hierarchy. However large transforms can also reduce overhead for the use of intra blocks.
In order to improve the subjective quality, the following restriction is introduced:
  32x32 and 16x16 TU and PU are competing in intra mode selection.
  Use of 32x32 TU and PU is penalized by scaling the number of bits.
Thus we get more frequent
use of 16x16 TU and PU on inter slices,
which improves the subjective quality.
Notes: 07/29/262011-10-19
<number>

## Slide 13: Objective results (tc_offsets)

## Slide 14: Objective results (tc_offsets + filter)

## Slide 15: Objective results (filter only)

## Slide 16: Objective results (filter only)

## Slide 17: Results (RD_penalty + tc_offsets)

## Slide 18: Results (RD_penalty + tc_offsets + filter)

## Slide 19: Subjective quality assessment
Significant reduction of blocking artifacts has been observed on sequences that contain a lot of blocking artifacts: Riverbed, West Wind Easy, China Speed with general improvement of visual quality.
Consistent visual quality improvements on common test conditions sequences (although not always as evident as for the listed sequences) that are expressed in some reduction of artifacts on ares with gradually changes intensity, e.g. shadows and similar.

## Slide 20: Summary
Blocking artifacts at large blocks in HEVC are caused by a combination of tools including the lambda parameter settings and the strong deblocking filter
It is proposed to:
  Use tc_offsets on the frame basis
  Change strong deblocking filter and the strong filter decisions
  Introduce cost penalty on 32x32 intra TU in P and B slices.

## Slide 21
Notes: 2010-10-07
Ericsson AB 2010
<number>