## Slide 1: AHG7: The performance of extended intra chroma prediction for non 4:2:0 format
J. Kim
JCTVC-L0240

## Slide 2: Introduction
Intra chroma prediction : IntraFormLuma
  For HEVC, IntraFromLuma(LM chroma) mode was adopted as one of intra chroma prediction mode
  Principle of LM chroma for 4:2:0 sampling:
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 3: Proposed Method (I)
Extended intra chroma prediction mode for non 4:2:0 sampling
  We propose to use IntraFormLuma(LM chroma) mode for non 4:2:0 sampling
  Adaptation for 4:4:4 sampling (including RGB case)
    All of luma samples are used
  Adaptation for 4:2:0 sampling
    Luma samples involved in the process are downsampled horizontally

## Slide 4: Proposed Method (I)
  4:4:4 sampling
Chroma TU
: to be predicted
Luma TU
: reconstructed

## Slide 5: Proposed Method (I)
  4:2:0 sampling
Chroma TU
: to be predicted
Luma TU
: reconstructed
Red circles indicate the locations of luma samples for prediction of chroma samples

## Slide 6: Proposed Method (II)
We propose that the parameters are calculated every CU and used for every TU in the entire CU
chroma reconstruction
for T0
Parameter
Calculation for CU
TU0
TU1
TU2
TU3
chroma reconstruction
for T1
chroma reconstruction
for T2
chroma reconstruction
for T3
chroma reconstruction
for T0
Parameter
Calculation for T0
chroma reconstruction
for T1
Parameter
Calculation for T1
chroma reconstruction
for T2
Parameter
Calculation for T2
chroma reconstruction
for T3
Parameter
Calculation for T3
<Previous design in HEVC>
<Proposed design>

## Slide 7
Experimental Results in detail (I)
Performance of extended chroma intra prediction against HM-Range-extension
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -19.7% | -17.9% | -18.7% | -15.4% | -14.4% | -15.0%
YCbCr 4:4:4 | -2.1% | -7.5% | -7.0% | -2.3% | -4.8% | -6.3%
YCbCr 4:2:2 | -2.0% | -5.9% | -4.9% | -1.7% | -3.1% | -3.1%
Overall | -8.4% | -10.8% | -10.6% | -6.9% | -7.7% | -8.5%
 | -8.4% | -10.8% | -10.6% | -6.9% | -7.9% | -8.6%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -11.1% | -9.8% | -11.8% | -7.9% | -6.3% | -8.5%
YCbCr 4:4:4 | -0.9% | -7.7% | -5.6% | -1.0% | -5.2% | -5.1%
YCbCr 4:2:2 | -0.8% | -6.4% | -4.5% | -0.7% | -2.7% | -3.0%
Overall | -4.6% | -8.1% | -7.5% | -3.4% | -4.8% | -5.6%
 | -4.6% | -8.5% | -7.4% | -3.5% | -5.7% | -6.0%
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -4.2% | -3.6% | -4.5% | -2.9% | -2.0% | -3.1%
YCbCr 4:4:4 | -0.3% | -4.0% | -2.3% | -0.3% | -2.3% | -1.9%
YCbCr 4:2:2 | -0.3% | -4.0% | -2.8% | -0.3% | -1.4% | -1.8%
Overall | -1.7% | -3.8% | -3.3% | -1.2% | -1.9% | -2.3%
 | -1.7% | -3.1% | -3.3% | -1.2% | -2.2% | -2.3%

## Slide 8
Experimental Results in detail (II)
Performance of extended chroma intra prediction with CU based parameter calculation against HM-Range-extension
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -17.7% | -16.2% | -16.8% | -13.5% | -12.9% | -13.1%
YCbCr 4:4:4 | -1.8% | -6.3% | -5.8% | -1.9% | -4.0% | -5.2%
YCbCr 4:2:2 | -1.9% | -5.8% | -4.8% | -1.7% | -3.0% | -3.1%
Overall | -7.6% | -9.7% | -9.5% | -6.0% | -6.9% | -7.4%
 | -7.6% | -9.8% | -9.5% | -6.1% | -7.1% | -7.5%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -9.4% | -8.7% | -10.3% | -6.5% | -5.5% | -7.3%
YCbCr 4:4:4 | -0.7% | -6.4% | -4.8% | -0.7% | -4.3% | -4.2%
YCbCr 4:2:2 | -0.8% | -6.3% | -4.4% | -0.7% | -2.7% | -2.9%
Overall | -3.9% | -7.2% | -6.7% | -2.8% | -4.2% | -4.9%
 | -3.9% | -7.7% | -6.6% | -2.9% | -4.9% | -5.2%
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | -3.4% | -3.1% | -3.9% | -2.4% | -1.7% | -2.6%
YCbCr 4:4:4 | -0.2% | -3.4% | -2.1% | -0.2% | -1.9% | -1.7%
YCbCr 4:2:2 | -0.3% | -3.8% | -2.8% | -0.3% | -1.3% | -1.7%
Overall | -1.4% | -3.4% | -3.0% | -1.0% | -1.7% | -2.0%
 | -1.4% | -2.9% | -3.0% | -1.0% | -1.9% | -2.0%

## Slide 9
Experimental Results in detail (III)
Performance of extended chroma intra prediction with CU based parameter calculation against HM-Range-extension with extended chroma intra prediction
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 2.9% | 2.5% | 2.9% | 2.8% | 2.1% | 2.7%
YCbCr 4:4:4 | 0.3% | 1.4% | 1.3% | 0.5% | 1.0% | 1.3%
YCbCr 4:2:2 | 0.0% | 0.2% | 0.1% | 0.0% | 0.1% | 0.1%
Overall | 1.2% | 1.4% | 1.5% | 1.2% | 1.1% | 1.4%
 | 1.1% | 1.4% | 1.5% | 1.2% | 1.1% | 1.4%
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 2.1% | 1.3% | 1.9% | 1.6% | 0.9% | 1.5%
YCbCr 4:4:4 | 0.2% | 1.5% | 0.9% | 0.2% | 1.1% | 0.9%
YCbCr 4:2:2 | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.1%
Overall | 0.8% | 1.0% | 1.0% | 0.7% | 0.7% | 0.9%
 | 0.8% | 1.0% | 1.0% | 0.7% | 0.9% | 0.9%
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  | 
 | Y | U | V | Y | U | V
RGB 4:4:4 | 0.8% | 0.5% | 0.7% | 0.5% | 0.3% | 0.5%
YCbCr 4:4:4 | 0.0% | 0.7% | 0.2% | 0.0% | 0.4% | 0.2%
YCbCr 4:2:2 | 0.0% | 0.2% | 0.0% | 0.0% | 0.1% | 0.0%
Overall | 0.3% | 0.5% | 0.3% | 0.2% | 0.2% | 0.3%
 | 0.3% | 0.3% | 0.4% | 0.2% | 0.3% | 0.3%

## Slide 10: Conclusion
We proposed including of extended intra chroma prediction (LM chroma mode) for non 4:2:0 sampling
We proposed CU-based parameter calculation to reduce total number of calculation and memory access in average.