## Slide 1: TE2-3.2.3 Infer zero motion vector when referencing co-located base layer picture
Kiran Misra, Jie Zhao, Andrew Segall
(JCTVC-L0251)

## Slide 2: Organization
Introduction
Proposed changes
Results
Conclusion

## Slide 3: Introduction
Goals:
  Minimize number of changes from base layer
SMuC 0.1.1 framework used: reference index*
  A up-sampled base layer (BL) picture is inserted at the end of the reference picture list
* Does not include encoder bug-fix JCTVC-L0167 for reference index framework

## Slide 4: Proposed changes
DESCRIPTION
Infer zero motion vector when referencing co-located BL picture

## Slide 5: Experimental Results
TE2 test conditions
Luma BD rate with HM8.1 simulcast anchors
 | EL+BL |  |  | EL only |  | 
 | 2x | 1.5x | SNR | 2x | 1.5x | SNR
All-intra | -23.0% | -32.9% |  | -35.1% | -58.8% | 
Random access | -15.3% | -25.6% | -18.6% | -23.7% | -46.6% | -29.5%
Low delay P | -12.5% | -22.4% | -13.3% | -19.9% | -41.7% | -21.4%
This represents the following increase in BD rate for reference index framework with HM8.1 simulcast anchors
 | EL+BL |  |  | EL only |  | 
 | 2x | 1.5x | SNR | 2x | 1.5x | SNR
All-intra | -0.1% | -0.2% |  | -0.2% | -0.3% | 
Random access | -0.2% | -0.1% | -0.2% | -0.3% | -0.2% | -0.3%
Low delay P | -0.4% | -0.3% | -0.3% | -0.5% | -0.4% | -0.5%

## Slide 6: Experimental Results (with changes)
  BD rate for proposed infer zero MV method with HM 8.1 simulcast anchors
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -27.1% | -26.5% | -27.3% |  |  |  |  |  | 
Class B | -21.3% | -20.4% | -20.2% | -32.9% | -33.0% | -33.2% |  |  | 
Overall (EL+BL) | -23.0% | -22.1% | -22.2% | -32.9% | -33.0% | -33.2% |  |  | 
Overall (EL) | -35.1% | -34.0% | -34.3% | -58.8% | -58.5% | -58.9% |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -17.6% | -5.4% | -6.8% |  |  |  | -20.5% | -9.2% | -8.1%
Class B | -14.4% | -5.8% | -3.9% | -25.6% | -18.9% | -17.0% | -17.9% | -6.2% | -1.7%
Overall (EL+BL) | -15.3% | -5.7% | -4.8% | -25.6% | -18.9% | -17.0% | -18.6% | -7.0% | -3.5%
Overall (EL) | -23.7% | -9.0% | -7.8% | -46.6% | -36.0% | -32.8% | -29.5% | -12.5% | -7.4%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -13.7% | -1.5% | -2.7% |  |  |  | -14.0% | -6.7% | -5.7%
Class B | -12.0% | -5.7% | -3.9% | -22.4% | -16.9% | -15.1% | -13.0% | -5.6% | -1.6%
Overall (EL+BL) | -12.5% | -4.5% | -3.5% | -22.4% | -16.9% | -15.1% | -13.3% | -5.9% | -2.8%
Overall (EL) | -19.9% | -7.1% | -5.8% | -41.7% | -32.3% | -29.0% | -21.4% | -11.2% | -6.8%

## Slide 7: Experimental Results (without changes)
  BD rate for reference index framework with HM 8.1 simulcast anchors
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -26.9% | -26.2% | -27.1% |  |  |  |  |  | 
Class B | -21.2% | -20.1% | -20.0% | -32.8% | -32.9% | -33.1% |  |  | 
Overall (EL+BL) | -22.8% | -21.9% | -22.0% | -32.8% | -32.9% | -33.1% |  |  | 
Overall (EL) | -34.8% | -33.7% | -33.9% | -58.5% | -58.2% | -58.7% |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -17.3% | -4.6% | -6.1% |  |  |  | -20.3% | -8.3% | -7.3%
Class B | -14.2% | -5.2% | -3.3% | -25.4% | -18.8% | -16.9% | -17.7% | -5.8% | -1.2%
Overall (EL+BL) | -15.1% | -5.1% | -4.1% | -25.4% | -18.8% | -16.9% | -18.5% | -6.5% | -2.9%
Overall (EL) | -23.4% | -8.0% | -6.9% | -46.4% | -35.9% | -32.7% | -29.2% | -11.7% | -6.5%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -13.3% | -1.1% | -2.3% |  |  |  | -13.7% | -6.4% | -5.4%
Class B | -11.6% | -5.6% | -3.9% | -22.1% | -16.9% | -15.2% | -12.7% | -5.7% | -1.8%
Overall (EL+BL) | -12.1% | -4.3% | -3.5% | -22.1% | -16.9% | -15.2% | -13.0% | -5.9% | -2.9%
Overall (EL) | -19.4% | -6.8% | -5.7% | -41.2% | -32.1% | -29.1% | -20.9% | -11.2% | -6.9%

## Slide 8: Experimental Results (difference)
  BD rate improvement for reference index framework with HM 8.1 simulcast anchors
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | -0.2% | -0.2% |  |  | 
Class B | -0.1% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1%
Overall (EL+BL) | -0.1% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1%
Overall (EL) | -0.2% | -0.3% | -0.3% | -0.3% | -0.3% | -0.2%
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.3% | -0.8% | -0.7% |  |  |  | -0.1% | -0.8% | -0.8%
Class B | -0.2% | -0.6% | -0.6% | -0.1% | -0.1% | -0.1% | -0.2% | -0.4% | -0.5%
Overall (EL+BL) | -0.2% | -0.6% | -0.6% | -0.1% | -0.1% | -0.1% | -0.2% | -0.5% | -0.6%
Overall (EL) | -0.3% | -0.9% | -0.9% | -0.2% | -0.1% | -0.1% | -0.3% | -0.8% | -0.8%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.4% | -0.3% |  |  |  | -0.3% | -0.3% | -0.3%
Class B | -0.3% | -0.1% | 0.0% | -0.3% | -0.1% | 0.1% | -0.3% | 0.1% | 0.3%
Overall (EL+BL) | -0.4% | -0.2% | -0.1% | -0.3% | -0.1% | 0.1% | -0.3% | 0.0% | 0.1%
Overall (EL) | -0.5% | -0.3% | -0.1% | -0.4% | -0.1% | 0.1% | -0.5% | -0.1% | 0.1%

## Slide 9: Conclusion
Zero motion vector is inferred when referencing co-located base layer picture.
The proposed approach achieves the following average luma BD rate improvements with HM-8.1 simulcast anchors: 23.0% /32.9% (AI 2x/AI 1.5x), 15.3%/25.6%/18.6% (RA 2x/RA 1.5x/RA SNR), 12.5%/22.4%/13.3% (LD-P 2x/ LD-P 1.5x/LD-P SNR).
The proposed approach achieves an additional BD rate improvement of 0.1% to 0.4% for the SMuC 0.1.1 reference index framework with HM 8.1 simulcast anchors.