## Slide 1: JCT-VC L0252: Non-TE4: Adaptive upsampling of base layer picture using bilateral filters
Jie Zhao, Kiran Misra, Andrew Segall
Presenter: Kiran Misra

## Slide 2: Outline
Introduction
Algorithms
  Use of Bilateral filtering in inter layer prediction
  Proposed Adaptive upsampling syntax
Performance
Summary

## Slide 3: Introduction
Idea:
  To improve upsampled based layer used for inter layer prediction by using non-linear and content adaptive “bilateral” filters.
  The “bilateral” filter is an adaptive filter that is asserted to preserve edges while smoothing texture and noise.
  Adaptively select upsampler on CU basis when INTRA_BL mode is selected.

## Slide 4: Algorithm
When INTRA_BL mode is on, there are two versions of upsampled base layer pictures available for inter layer prediction
  Fixed upsampler of SMuC 0.1.1,
  Performing bilateral filtering on the first upsampled base layer picture.
Upsampler index is signaled at CU level when INTRA_BL mode is selected.
Encoder side: decided in checkRDCostIntraBL by RD decision.
B-Layer
E-Layer
upsampled
Base Layer
Bilateral
Filtered
upsampled
Base Layer
Fig. Example of 2 upsampled
BL picture in Spatial scalability

## Slide 5: Algorithm
Output(x,y) is weighted average within a window. (e.g. a 5x5 window below).
Weight is related to both the gradient of a pixel at (a,b) to the input pixel at (x,y) and related to the distance to the input pixel.
function f() maps the spatial distance and gradient information to a weight value.
G(a,b) denotes the gradient of the input at (a,b) relative to input at (x,y).
sigmaR is a control parameter to adjust the weight based on the Gradient.
K(a,b) denotes a spatial kernel, which is typically a Gaussian kernel, to adjust the weight based on the distance of location (a,b) to the input location (x,y)
f() is implemented as a LUT to reduce computational complexity
 | (a,b) |  |  | 
 |  | (x,y) |  | 

## Slide 6: Example Syntax
Parameters of bilateral filters can be signaled in bitstream.
At high level, signal the number of filters and filter indices.

## Slide 7: Example Syntax
CU level signaling when INTRA_BL mode is selected.
If supporting a large number of upsamplers, upsampler index may be predicatively coded from a most probable upsample index. E.g.
  Use a mapping of the indices
  Or use distance to a most probable upsampler

## Slide 8: Experiment
SMuC0.1.1 TE4 test configuration. Used 1 fixed upsampler and 1 bilteral filter.
Performed two tests by whether including an SMuC0.1.1 bug fix or not.
  Relative to SMuC0.1, SMuC0.1. 1 has a bug fix to include the INTRA_BL bit count in the RD decision ( in function xAddSymbolBitsInter). However, the bug fix caused 0.1% RD performance drop for random access.
  Since our upsampling index is coded together with the INTRA_BL flag, we conducted two tests with and without this bug fix.
Test 1:
Without this bug fix. i.e. not including the INTRA_BL and upsampler Index bits in xAddSymbolBitsInter. We denote this test as SHARP_ENCODER_RATE_MODIFY 1.
Test 2:
Leave this bug fix on. We denote this test as SHARP_ENCODER_RATE_MODIFY 0.

## Slide 9: Result
Test 1:
With SHARP rate modification
Average 1.4% rate reduction for 2X case.
0.6% to 0.9% rate reduction for 1.5X and SNR cases.

## Slide 10: Result
Test 2:
Without SHARP rate modification
Average 1.3% to 1.4% rate reduction for 2X scalability.
0.5% to 0.9% rate reduction for 1.5X and SNR cases.

## Slide 11: Cross-Check
Result are cross checked by Samsung, (cross check report JCTVC-L0361).
Timing data in the result tables are from our cross checker, which ran the jobs on Linux cluster with uniform computing nodes.
Our filter tool is similar to Samsung’s de-ringing filter tool proposed in L0195.

## Slide 12: Summary
Proposed a non-linear and content adaptive bilateral filtering process
Relative large gain (1.4% rate reduction) is observed for 2X spatial scalability, 0.5%-0.9%. rate reduction for 1.5x and SNR scalabilities.
Proposed further study of the method in a TE/CE.