## Slide 1: JCTVC-L0254 AHG 9: On RPS derivation & marking process for long-term reference pictures
The 12th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
For signaling LTRP in RPS, MSB cycle is not mandated if there is two or more reference pictures that have the same POC LSB
There might be an issue with marking process for LTRP
  When an LTRP is supposed to be removed from DPB but not
    An LTRP is marked as unused for reference at a picture that can be removed from bitstream without affecting decodability of other pictures.
  For next picture, there is another ref pic with same POC LSB with the LTRP
  Decoder may choose wrong reference picture in such situation.
Proposal: two options are offered to fix this issue.
  Option 1: mandate to always signal delta MSB cycle for all LTRP
    Cost: bit count for always signalling delta MSB
  Option 2: modify marking process such that marking of LTRP to be unused for reference shall not be in picture with non-referenced type NALU and TemporalId not equal 0.
    Cost: delay in removing LTRP from DPB

## Slide 3: Example of case
At pic 266, there are two ref pics with the same POC LSB (Ref pic 0 as LTRP and Ref pic 256 as STRP)
At pic 267, Ref pic 0 is not needed for reference anymore
At pic 268, Ref pic 256 is marked as LTRP
Problem: If pic 267 is not decoded, then Ref pic 0 will exists in DPB for Pic 268
According to current spec, Ref pic 0 will be marked as LTRP and Ref pic 256 will be marked as unused for reference
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {256, 264}
Pic 264
TRAIL_R NAL Unit
POC LSB is signaled by using 8 bits
…
PocLtCurr = {}
PocStCurrBefore = {256, 264, 266}
MSB Info for LT is NOT signaled
PocLtCurr = {0}
PocStCurrBefore = {264, 266}
…
Pic 265
TRAIL_N NAL Unit
Pic 267
TRAIL_N NAL Unit
Pic 266
TRAIL_R NAL Unit
Pic 268
TRAIL_R NAL Unit
Discarded!

## Slide 4: Options for solution (1)
Option 1: mandate that delta MSB cycle to be signaled for all LTRP
  (+) LTRP can be marked as unused for reference as soon as it is not needed
  (-) Overhead bit count for signaling delta MSB cycle
    NOTE: Delta MSB cycle is not always needed
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {256, 264}
Pic 264
TRAIL_R NAL Unit
POC LSB is signaled by using 8 bits
…
PocLtCurr = {}
PocStCurrBefore = {256, 264, 266}
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {264, 266}
…
Pic 265
TRAIL_N NAL Unit
Pic 267
TRAIL_N NAL Unit
Pic 266
TRAIL_R NAL Unit
Pic 268
TRAIL_R NAL Unit
Discarded!

## Slide 5: Options for solution (2)
Option 1: modify marking process such that marking of LTRP to be unused for reference shall not be in picture with non-referenced type NALU and TemporalId not equal 0
  (+) No need to signal delta MSB cycle when it is not really needed
  (-) Possible delay to remove LTRP from DPB when it is not needed anymore
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {256, 264}
Pic 264
TRAIL_R NAL Unit
POC LSB is signaled by using 8 bits
…
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {256, 264, 266}
MSB Info for LT is signaled
PocLtCurr = {0}
PocStCurrBefore = {264, 266}
…
Pic 265
TRAIL_N NAL Unit
Pic 267
TRAIL_N NAL Unit
Pic 266
TRAIL_R NAL Unit
Pic 268
TRAIL_R NAL Unit
Discarded!

## Slide 6: Text modification
See contribution document

## Slide 7: Remarks & Conclusion
Current RPS derivation and reference picture marking process has issue
  Possible wrong marking when removal of LTRP from DPB is signaled in unreferenced picture and / picture with temporalId higher than 0
Two possible solutions are offered
  Option 1: mandate to always signal delta MSB cycle for all LTRP
  Option 2: modify marking process such that marking of LTRP to be unused for reference shall not be in picture with non-referenced type NALU and TemporalId not equal 0.
The authors recommend option 2
  Preserves the concept of signaling delta MSB cycle only when it is really needed.