## Slide 1: JCTVC-L0255 AHG 9: On dependent slice segment signaling
The 12th JCT-VC Meeting
LG Electronics

## Slide 2: Overview
For system level app, it is beneficial to be able to differentiate dependent and non-dependent slice segment [JCTVC-K0184]
  Dropping and aggregating NAL units
In last meeting, flags for dependent slice segment have been moved to earlier position but there might be issues:
  Complicated parsing the flags as there are several conditions to checks
  Required additional memory at system level app to store PPS
    picture_parameter_set_id
    dependent_slice_segments_enabled_flag
Proposals to avoid the above issues
  Option 1: move dependet_slice_segment_flag to earlier position (i.e., before pic_parameter_set_id)
  Option 2: assign a new NAL unit for dependent slice segment

## Slide 3: Parsing of dependent_slice_segment_flag
There at least three conditions to be checked when parsing the flag
  First slice in pic?
  RAP?
  Dependent slice segments allowed?
The last condition requires checking it other place since it is not directly available in the same slice header
slice_segment_header( ) { | Descriptor
first_slice_segment_in_pic_flag | u(1)
if( RapPicFlag ) | 
no_output_of_prior_pics_flag | u(1)
pic_parameter_set_id | ue(v)
if( !first_slice_segment_in_pic_flag ) { | 
if(dependent_slice_segments_enabled_flag ) | 
dependent_slice_segment_flag | u(1)
slice_segment_address | u(v)
} | 
… | 

## Slide 4: Additional memory to store PPS and enabled flag
Dependent slice segment can be used only if ‘dependent_slice_segments_enabled_flag’ in PPS is set
There can be many PPS in a bitstream so that the enabled flag can change frequently.
Consequently, system level app needs to keep track of PPS or at least an array of PPSId and the enabled flag

## Slide 5: Considerations
Implementing dependent slice segment does not add much addition burden
  There is no real benefit of turning it on / off.
  It is supported in main profile
  The benefit of turning it off is only saving 1 bit in slice header.
There is no real benefit to have the value of dependent_slice_segments_enabled_flag changes within bitstream.

## Slide 6: Proposals
Option 1 -- Move dependent_slice_segment_flag to earlier position
  Before pic_parameter_set_id
  No need to check enabled flag in PPS
  Benefits:
    No need to keep array of pps id and enabled flag
Option 2 – Assign a new NAL unit type
  No complicated parsing process
  No need to keep array of pps id and enabled flag

## Slide 7: Remarks & Conclusion
Being able to identify dependent slice segment at system level is beneficial
However, current signalling of dependent slice segment may have issues
  Complicated parsing as there are at least three condition checks
  Requires additional memory to store PPS
Considerations:
  Implementing dependent slice segment does not add much addition burden
  There is no real benefit to have the value of dependent_slice_segments_enabled_flag changes within bitstream
Proposals
  Option 1: move dependent_slice_segment_flag to earlier position than its current
  Option 2: assign a new NAL unit type for dependent slice segment