## Slide 1: JCTVC-L0258 Inter-layer prediction indication flags and pictures management
The 12th JCT-VC Meeting
LG Electronics & Texas Instruments Inc.

## Slide 2: Overview
Two flags are proposed to be signaled in slice header to indicate the use of inter-layer prediction (ILP)
  ilp_flag – specifies whether or not current picture is used for ILP
  ilp_ref_flag – specifies whether or not current picture is used for inter prediction by other picture(s) whose ilp_flag equals 1.
Originally proposed in JCTVC-K0264
  Result of further study on this topic is proposed here
Benefits of having those two flags:
  Easy to determine whether or not a picture in a non-target layer needs to be delivered / to be decoded
  Enable a single RPS to be used for multiple layers when their temporal structure are the same
  Enable to limit the required DPB size when decoding any target layer

## Slide 3: Ilp_flag and ilp_rev_flag (1)
Not every pictures are needed for ILP.
  In example shown in next slice -- only pictures in Tid 0 & 1 in BL are needed for ILP
In non-target layer, pictures that are not directly / indirectly needed for ILP do not have to be decoded
  Ilp_flag & ilp_rev_flag help to determine which pictures can be discarded.
Required DPB size may be different for a layer when it is a target and non-target.
  We may need multiple RPS for each layer
  In a layer, RPS when it is target layer and RPS when it is not target layer

## Slide 4: Ilp_flag and ilp_rev_flag (2)

## Slide 5: Ilp_flag and ilp_rev_flag (3)
ilp_flag indicates that current slice may be used for inter-layer prediction. It is requirement of the bitstream that the value of this flag shall be the same in all slice segment headers of a coded picture.
ilp_ref_flag indicates that current slice may be referred / used for inter prediction by other picture(s) that are needed for inter-layer prediction. It is requirement of the bitstream that the value of this flag shall be the same in all slice segment headers of a coded picture.
There are reserved, undetermined flag(s) in current slice header, however, we propose to discuss whether the above two flags should be signal differently
  May have effect on decoding process
  May have effect on reference picture list construction
slice_segment_header( ) { | Descriptor
… | 
ilp_flag | u(1)
ilp_ref_flag | u(1)
… | 
} | 

## Slide 6: ilp_flag, ilp_rev_flag, and decoding process
Let LayerID denotes layer id & TargetLayer denotes the target layer for decoding / display.
Given a particular TargetLayer, reconstructed picture of coded picture shall not be kept in memory if all the following are true:
  Its LayerID < TargetLayer, and
  ilp_flag is false, and
  ilp_ref_flag is false
Given a particular TargetLayer, after decoding of a picture with POC poc_curr and LayerID curr_layer_id (i.e., curr_layer_id ≤ TargetLayer), any reference picture in memory shall be removed if all the following is true:
  POC of the reference picture is the same as poc_curr, and
  LayerID of the reference picture is less than curr_layer_id, and
  ilp_ref_flag of the reference picture is false

## Slide 7: ilp_flag, ilp_rev_flag, and RPL construction (1)
Given that pictures not needed for ILP (directly / indirectly) in non-target layer may not be decoded
  RPS for each layer may be different when the layer is target and non-target layer.
  Consequently, multiple copies of RPS are needed
With the two flags, multiple copies of RPS are not needed.
Modify current ref pic list (RPL) construction to incorporate the two flags.

## Slide 8: ilp_flag, ilp_rev_flag, and RPL construction (2)
If ilp_flag of a slice equals 0, the reference picture lists for the slice are constructed based on RPS only. That is, no change to the current reference picture lists construction.
If the ilp_flag of the slice equals 1, the reference picture lists for the slice are constructed by including reference pictures that:
  Have ilp_ref_flag equals 1, and
  Are included in the RPS for that slice

## Slide 9: Text modification
See contribution document

## Slide 10: Remarks & Conclusion
Further study on the need for inter-layer prediction indication for each coded picture has been done
  Proposed flags: ilp_flag and ilp_ref_flag
The two flags can offer the following benefits
  Determine whether a picture in a non-target layer needs to be delivered / to be decoded
  Use single RPS for multiple layers
  Limit the required DPB size when decoding any target layer
Areas where the two flags should be used
  Decoding process
  Reference picture list construction
Recommend to discuss these two flags and to adopt them.