## Slide 1: TE5 Subset 1: Inter-layer Intra Mode Prediction
JCTVC-L0259
Presented by Mei Guo
12th JCT-VC Meeting in Geneva
14-23 Jan., 2013
Mei Guo, Shan Liu, Shawmin Lei (MediaTek Inc.) Joonyoung Park, Jungsun Kim, Byeongmoon Jeon (LG)

## Slide 2: Outline
Algorithm description
Experimental results
Conclusions

## Slide 3: Algorithm Description
Use collocated BL Intra mode as MPM in EL Intra mode coding.
  The center 4x4 block A in the current EL PU is projected to BL.
EL Intra mode coding
  Luma: 33 angular modes (remove DC and Planar)
    1 MPM (BL, Left, Top, V)
      If Left or Top is INTRA_BL, the collocated BL intra mode of Left or Top neighbor is used.
    32 remaining modes FLC
  Chroma: 3 modes (DM, H, V)

## Slide 4: Experimental Results (1/2)
Anchor – SMuC-0.1.1
Thank Nokia for cross verifying our results (L0125).
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.3% | -0.1% | 0.0% |  |  | 
Class B | -0.3% | -0.2% | -0.2% | -0.2% | 0.1% | 0.0%
Overall (EL+BL) | -0.3% | -0.2% | -0.2% | -0.2% | 0.1% | 0.0%
Overall (EL) | -0.6% | -0.3% | -0.3% | -0.4% | 0.2% | 0.1%
Enc Time[%] | 98.1% |  |  | 98.5% |  | 
Dec Time[%] | 100.5% |  |  | 100.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 5: Experimental Results (2/2)
Remove parsing dependency by disabling MDCS.
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.2% | 0.0% | 0.1% |  |  | 
Class B | -0.2% | 0.0% | 0.1% | -0.2% | 0.1% | 0.1%
Overall (EL+BL) | -0.2% | 0.0% | 0.1% | -0.2% | 0.1% | 0.1%
Overall (EL) | -0.4% | 0.0% | 0.1% | -0.4% | 0.2% | 0.2%
Enc Time[%] | 97.5% |  |  | 97.9% |  | 
Dec Time[%] | 100.5% |  |  | 100.6% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 6: Conclusions
Reported the results of TE5.1.1.
Improved the efficiency of intra mode coding at EL by exploiting the correlation between intra modes from different layers.
Experimental Results:
  BD-rate reduction of 0.3% and 0.2% for AI2x and AI1.5x
  Encoding time decreases by around 2%
Recommend to be adopted in SHVC.

## Slide 7
Thank you!