## Slide 1: JCTVC-L0262 Signaling of required DPB size in VPS
The 12th JCT-VC Meeting
LG Electronics & Texas Instruments Inc.

## Slide 2: Overview
Related to contribution JCTVC-L0258
Required DPB size for decoding process at a particular layer can be different
  Target layer / non-target layer
The information is useful for decoder in session negotiation to determine the highest layer the decoder can handle.
Currently, no syntax element in VPS / VPS extension conveys the intended information
vps_max_dec_pic_buffering[ i ] is only for each sub layer / temporal layer.

## Slide 3: Proposed syntax
vps_max_dec_pic_buffering_target[ i ] specifies the required size of the decoded picture buffer in units of picture storage buffers when HighestLayerId is equal to i. When i is greater than 0, vps_max_dec_pic_buffering_target[ i ] shall be greater than or equal to vps_max_dec_pic_buffering_target[ i − 1 ].
vps_max_dec_pic_buffering_nontarget[ i ] specifies the required size of the decoded picture buffer in units of picture storage buffers for decoding only pictures whose layerID equals i.
ue(v) can also be replace with fixed-length bits (i.e., u(5)?)
vps_extension( ) { | Descriptor
… | 
for( i = 0; i <= vps_max_num_layers_minus1; i++ ) { | 
vps_max_dec_pic_buffering_target[ i ] | ue(v)
vps_max_dec_pic_buffering_nontarget[ i ] | ue(v)
} | 
… | 
} | 

## Slide 4: Motivation
Signal in VPS extension the total number of required DPB size to decode a particular (target) layer so that
Level- compliant scalable decoder can choose a target layer depending on the DPB size it can support
Example: Profile/Level on total DPB size for scalable HEVC decoder
  …
  Level -3: DPB size = 9
  Level -4: DPB size = 12
  …
  Suppose that a decoder is compliant to Level-3, i.e. DPB size = 9

## Slide 5: Example: scalable bitstream
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
EL2
02
12
22
32
42
52
62
72
82
92
102
112
122
132
142
152
162
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
EL1
01
11
21
31
41
51
61
71
81
91
101
111
121
131
141
151
161
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
BL
00
10
20
30
40
50
60
70
80
90
100
110
120
130
140
150
160
DPBBL2 = 6
DPBEL1 = 6
DPBBL = 6

## Slide 6: Example: target layer decoding - BL
When BL is a target layer,
  Total DPB size is 6
  Level-3 compliant decoder can decode BL
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
BL
00
10
20
30
40
50
60
70
80
90
100
110
120
130
140
150
160
DPBBL,target = 6

## Slide 7: Example: target layer - EL1
When EL1 is a target layer,
  Total DPB size is 9
  Level-3 compliant decoder can decode EL1
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
EL1
01
11
21
31
41
51
61
71
81
91
101
111
121
131
141
151
161
L0
L0
L0
L1
L1
BL
00
40
80
120
160
DPBtarget= 9
DPBBL,non-target = 3

## Slide 8: Example: target layer - EL2
  When EL2 is a target, Level-3 compliant decoder CANNOT decode EL2
L0
L0
L0
L1
L1
L2
L2
L2
L2
L3
L3
L3
L3
L3
L3
L3
L3
EL2
02
12
22
32
42
52
62
72
82
92
102
112
122
132
142
152
162
L0
L0
L0
L1
L1
L2
L3
L3
EL1
01
41
81
121
161
L0
L0
L0
L1
L1
BL
00
40
80
120
160
DPBEL2, target= 12
DPBEL1, non-target = 3
DPBBL, non-target = 3

## Slide 9: Remarks & Conclusion
It is proposed for each scalable layer to signal DPB sizes when the layer is target and non-target layer
Decoder know how many decoded picture buffers are necessary to decode a particular target layer
Therefore, decoder can select a target layer depending on the total DPB size it can support