## Slide 1: On interpolation filter for Generalized Residual Prediction (JCTVC-L0265)
JCT-VC 12th Meeting in Geneva, CH, 14– 23 Jan. 2013
Takeshi Tsukuba, Tomoyuki Yamamoto, Tomohiro Ikai
SHARP Corporation

## Slide 2: Overall summary
Motivation
  Variants of Generalized Residual Prediction(GRP) were proposed in the last meeting.
  GRP can effectively reduce the redundancy between base-layer and enhancement-layer while the complexity of interpolation process and the memory band increased.
  It is necessary to simplify the interpolation process.
Proposal:
  To apply simple interpolation filters to Base-layer motion compensation for generating residual instead of classical DCT-IF filters:8-tap for luma, 4-tap for chroma
    Interpolation filters are selected depending on the slice type
      B-slice : 2-tap filter for luma and chroma
      P-slice : 4-tap filter for luma and 2-tap filter for chroma
  The proposed method is implemented on TE3 4.6.3 software[1] provided by Nokia.
Experimental results
  “EL+BL” bdrate gain :
    2.1 % to 3.6% compared to SMuC-0.1.1
    0.1 % to 0.9% except LP SNR scalability ( 0.5% loss) compared to TE3 4.6.3
  Cross-checked results are provided by Nokia
  [1] J. Lainema, K Ugur, “TE3: Results of test 4.6.3 on base enhanced motion compensated prediction,” JCTVC-L0038, Geneva, CH, Jan. 2013.

## Slide 3: Overview of Generalized Residual Prediction
GRP proposed in [1] is summarized as follows:
  Generate residual by subtracting base layer MC result with enhancement layer motion parameters from base layer reconstruction
  Add the regular prediction and the weighted residual to get final prediction
  Signal the weight on PU level
Generating residual process
R = UP ( RecBL) – MC ( UP(RefBL), MVEL ) - (eq.1)
Adding weighted residual process to the regular prediction
PEL ’= PEL + w * R - (eq.2)
The original proposal(BEMCP) uses classical DCT-IF filters for residual generation in eq.1.
  8-tap for luma
  4-tap for chroma
It is desirable to simplify the interpolation process in eq. 1 so as to reduce the complexity
MVEL
MVEL
Enhancement layer
Base layer
UP
UP
PEL’
PEL= MC( RefEL, MVEL)
w
R
curPic
RefEL
RefBL
RecBL
-
PBL= MC(UP(RefBL), MVEL)
UP(RecBL)
Example of uni-prediciton with residual prediction
  [1] J. Lainema, K Ugur, “TE3: Results of test 4.6.3 on base enhanced motion compensated prediction,” JCTVC-L0038, Geneva, CH, Jan. 2013.

## Slide 4: Proposal
To apply simple interpolation filters to Base-layer motion compensation for generating residual in eq. 1
R = UP ( RecBL) – MC ( UP(RefBL), MVEL ) - (eq.1)
Interpolation filters are selected depending on the slice type
  B-slice : 2-tap filter for luma and chroma
  P-slice : 4-tap filter for luma and 2-tap filter for chroma
Table.1: Interpolation filter selection for each slice type
Phase offset | Filter coefficients
0/4 | [ 0, 64, 0, 0 ] // 64
1/4 | [-4, 54, 16, -2 ] // 64
2/4 | [-4, 36, 36, -4 ] // 64
3/4 | [-2, 16, 54, -4 ] // 64
Phase offset | Filter coefficients
0/4 | [ 64, 0 ] // 64
1/4 | [48, 16] // 64
2/4 | [32, 32] // 64
3/4 | [16, 48] // 64
Phase offset | Filter coefficients
0/8 | [ 64, 0 ] // 64
1/8 | [ 56, 8 ] // 64
2/8 | [ 48, 16] // 64
3/8 | [ 40, 24] // 64
4/8 | [ 32, 32] // 64
5/8 | [ 24, 40] // 64
6/8 | [ 16, 48] // 64
7/8 | [ 8, 56] // 64
Table.1 : Interpolation filter for luma in P-slice
Table.2 : Interpolation filter for luma in B-slice
Table.3 : Interpolation filter for chroma in P/B-slice

## Slide 5: Experimental results
The proposal was implemented on top of TE3 4.6.3 software provided by Nokia (JCTVC-L0038)
BD-rate gain : 2.1 % to 3.6% compared to SmuC0.1.1

## Slide 6: Experimental results
The proposal was implemented on top of TE3 4.6.3 software provided by Nokia (JCTVC-L0038)
BD-rate gain : 0.1 % to 0.9% except LP SNR scalability (0.5% loss) compared to TE3 4.6.3

## Slide 7: Conclusion
Proposal:
  To apply simple interpolation filters to Base-layer motion compensation for generating residual instead of classical DCT-IF filters:8-tap for luma, 4-tap for chroma
    Interpolation filters are selected depending on the slice type
      B-slice : 2-tap filter for luma and chroma
      P-slice : 4-tap filter for luma and 2-tap filter for chroma
  The proposed method is implemented on TE3 4.6.3 software provided by Nokia.
Experimental results
  “EL+BL” bdrate gain:
    2.1 % to 3.6% compared to SMuC-0.1.1
    0.1 % to 0.9% except LP SNR scalability ( 0.5% loss) compared to TE3 4.6.3
Recommendation … investigate the proposal in CE / TE in the candidate tools of SHVC
Many thanks to Nokia for cross-checking this contribution (JCTVC-Lxxxx)