## Slide 1: Non-TE4: Inter-layer SAO
JCTVC-L0283
Presented by Shan Liu
12th JCT Meeting in Geneva
14-23 January 2013
Zhenzhong Chen, Shan Liu, Ximin Zhang,
Shih-Ta Hsiang, Chih-Ming Fu, Shawmin Lei

## Slide 2: Inter-layer SAO
JCTVC-K0033 proposed inter-layer SAO.
JCTVC-L0212 implemented on SMuC0.1.1.

## Slide 3: Method 1
Decide the SAO type and calculate the offset by using the inter-layer SAO method (JCTVC-K0033) iteratively.
  In each iteration
    A picture is split into four regions or one picture is a region.
    Each region selects one SAO type
      EO: 0-degree, 90-degree, 135-degree, 45-degree
      BO: band position
    Each SAO type signals four offsets.
    Picture level on/off before the EL CTU encoding process
  The corresponding SAO parameters are sent in slice header.
SAO_Type
SAO_Parameters
SAO_Type
SAO_Parameters
SAO_Type
SAO_Parameters
...
1st iteration
2nd iteration
Nth iteration

## Slide 4: Method 2
Calculate the offset for each SAO type one by one.
  For each SAO type
    A picture is split into four regions or one picture is a region.
    Each SAO type signals four offsets.
    SAO Type on/off at picture level.
  The SAO type is implemented in order
    EO: 0-degree, 90-degree, 135-degree, 45-degree then BO.
    One type is calculated on the output of the previous type.
  The corresponding SAO parameters are sent in slice header in the predefined order.
Parameters
Parameters
Parameters
Parameters
Parameters
EO1 On/Off
EO2 On/Off
EO3 On/Off
EO4 On/Off
BO On/Off

## Slide 5: Method 1 Results (Anchor: SMuC0.1.1)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -1.3% | -2.3% | -2.5% |  |  |  |  |  | 
Class B | -0.1% | -0.5% | -0.6% | -0.1% | -0.3% | -0.3% |  |  | 
Overall (EL+BL) | -0.5% | -1.0% | -1.1% | -0.1% | -0.3% | -0.3% |  |  | 
Overall (EL) | -1.1% | -2.2% | -2.4% | -0.2% | -0.6% | -0.7% |  |  | 
Enc Time[%] | 101.5% |  |  | 101.7% |  |  |  |  | 
Dec Time[%] | 107.7% |  |  | 103.4% |  |  |  |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  |  |  | 
BL Match | Matched |  |  | Matched |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.4% | -1.1% | -1.5% |  |  |  | -1.0% | -1.4% | -2.1%
Class B | -0.2% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% | -0.3% | -0.6% | -0.4%
Overall (EL+BL) | -0.6% | -0.5% | -0.6% | -0.1% | -0.2% | -0.2% | -0.5% | -0.8% | -0.9%
Overall (EL) | -1.2% | -1.1% | -1.3% | -0.3% | -0.5% | -0.3% | -1.1% | -2.0% | -2.1%
Enc Time[%] | 100.5% |  |  | 100.1% |  |  | 99.9% |  | 
Dec Time[%] | 107.4% |  |  | 101.9% |  |  | 104.3% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.4% | -1.6% | -2.0% |  |  |  | -1.3% | -2.2% | -3.0%
Class B | -0.4% | -1.1% | -0.9% | -0.3% | -1.0% | -0.9% | -0.8% | -2.0% | -1.7%
Overall (EL+BL) | -0.7% | -1.2% | -1.2% | -0.3% | -1.0% | -0.9% | -0.9% | -2.0% | -2.0%
Overall (EL) | -1.5% | -2.4% | -2.4% | -0.7% | -2.2% | -1.7% | -1.8% | -4.3% | -4.3%
Enc Time[%] | 100.3% |  |  | 100.2% |  |  | 100.3% |  | 
Dec Time[%] | 113.4% |  |  | 105.9% |  |  | 110.8% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 

## Slide 6: Method 2 Results (Anchor: SMuC0.1.1)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -1.3% | -2.2% | -2.4% |  |  |  |  |  | 
Class B | -0.1% | -0.5% | -0.6% | -0.1% | -0.2% | -0.3% |  |  | 
Overall (EL+BL) | -0.5% | -1.0% | -1.1% | -0.1% | -0.2% | -0.3% |  |  | 
Overall (EL) | -1.1% | -2.1% | -2.3% | -0.2% | -0.5% | -0.5% |  |  | 
Enc Time[%] | 99.6% |  |  | 99.6% |  |  |  |  | 
Dec Time[%] | 109.4% |  |  | 106.0% |  |  |  |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  |  |  | 
BL Match | Matched |  |  | Matched |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.7% | -1.0% | -1.5% |  |  |  | -1.1% | -1.3% | -1.8%
Class B | -0.2% | -0.3% | -0.2% | -0.1% | -0.2% | -0.1% | -0.3% | -0.5% | -0.3%
Overall (EL+BL) | -0.7% | -0.5% | -0.6% | -0.1% | -0.2% | -0.1% | -0.5% | -0.7% | -0.7%
Overall (EL) | -1.4% | -1.0% | -1.2% | -0.2% | -0.4% | -0.3% | -1.0% | -1.7% | -1.8%
Enc Time[%] | 99.9% |  |  | 99.5% |  |  | 99.7% |  | 
Dec Time[%] | 111.0% |  |  | 103.8% |  |  | 106.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.9% | -1.6% | -2.1% |  |  |  | -1.4% | -2.1% | -2.8%
Class B | -0.5% | -1.0% | -0.8% | -0.3% | -0.8% | -0.7% | -0.8% | -1.8% | -1.5%
Overall (EL+BL) | -0.9% | -1.2% | -1.1% | -0.3% | -0.8% | -0.7% | -1.0% | -1.9% | -1.9%
Overall (EL) | -1.8% | -2.3% | -2.2% | -0.7% | -1.8% | -1.2% | -1.9% | -4.0% | -3.9%
Enc Time[%] | 99.8% |  |  | 99.3% |  |  | 99.6% |  | 
Dec Time[%] | 116.2% |  |  | 105.3% |  |  | 112.3% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 

## Slide 7: Conclusion
Two implementations of IL-SAO are presented.
Results are reported compared with SMuC0.1.1 anchor.
  Method 1 BD rate reduction for Y, U, V
    Average 0.38%, 0.72% and 0.73% for spatial scalability.
    Average 0.73%, 1.42% and 1.44% for SNR scalability.
    Encoding time change is negligible, average decoding time is increased by 6.85%.
  Method 2 BD rate reduction for Y, U, V
    Average 0.42%, 0.65% and 0.65% for spatial scalability.
    Average 0.75%, 1.39% and 1.30% for SNR scalability.
    Encoding time change is negligible, average decoding time is increased by 8.81%.
Recommend to further study the proposed methods in related TE (CE).

## Slide 8
www.mediatek.com