## Slide 1: TE2: Results of Test 3.1.1 on Inter-layer Texture Prediction Signaling (JCTVC-L0284)
Liwei Guo, Vadim Seregin, Jianle Chen, Marta Karczewicz

## Slide 2: Introduction
TE2 – Inter-layer texture prediction signaling
This contribution reports the results of test 3.1.1 in TE2 which includes:
  Intra-BL Skip flag signaling
  Deblocking BS setting for Intra-BL Skip

## Slide 3: Intra-BL Skip Flag Signaling
coding_unit( x0, y0, log2CbSize ) { | Descriptor
CurrCbAddrTS = MinCbAddrZS[ x0 >> Log2MinCbSize ][ y0 >> Log2MinCbSize ] | 
intra_bl_skip_flag[ x0 ][ y0 ] | ae(v)
if( !intra_bl_skip_flag[ x0 ][ y0 ] ) { | 
if( slice_type != I ) { | 
skip_flag[ x0 ][ y0 ] | ae(v)
} | 
intra_bl_flag | ae(v)
…… | 
} | 
Intra-BL Skip Flag
  If this flag is equal to 1, the CU is reconstructed by copying the reconstructed base layer pixel values (may need up-sampling).

## Slide 4: Deblocking BS setting
For Intra-BL Skip, no deblocking is applied
Deblocking BS settings:
  For neighboring two blocks
    If at least one is Intra, BS = 2, otherwise
    If at least one is Intra-BL, BS =1 for Luma and BS =2 for Chroma, otherwise
    If both are Intra-BL Skip, BS = 0 (no deblocking), otherwise

## Slide 5: Simulation
Anchor: HM 8.1 Simulcast
Settings: Test conditions defined in TE 2
Two tests
  Test A: DCT used for Intra-BL 4x4
  Test B: DST used for Intra-BL 4x4
Avg. AI BD-rate (2X, 1.5X) |  |  |  |  |  | Avg. RA/LDP BD-rate (2X, 1.5X) |  |  |  | 
 | Y | U | V | Enc. Time | Dec. Time | Y | U | V | Enc. Time | Dec.Time
Test A | -27.99% | -28.06% | -28.23% | 115.20% | 101.09% | -19.29% | -12.62% | -11.47% | 108.80% | 130.78%
Test B | -28.03% | -28.05% | -28.22% | 116.38% | 102.91% | -19.31% | -12.61% | -11.47% | 110.89% | 132.02%
SMuC 0.1.1 | -27.67% | -27.96% | -27.99% | 113.73% | 105.88% | -19.17% | -12.90% | -11.69% | 109.28% | 136.86%

## Slide 6
Thank you!