## Slide 1: Non-TE5: Inter-layer motion data inheritance
Wenhao Zhang, Yi-jen Chiu
Intel Corporation
JCTVC-L0291

## Slide 2: Introduction
  Apply an inter-layer motion data inheritance (MDI) mode to improve coding efficiency of SHVC.
  Features of proposed MDI:
    Partition the 2Nx2N PU into 4 NxN sub-blocks
    BL MV prediction and motion compensation are processed at sub-block level..
  Performance:
    1.78% average BD-rate reduction if uncompressed BL mv is used.
    Enc/dec coding time is reduced.
  Thanks to Huawei and Qualcomm for crosscheck (JCTVC-L0413, JCTVC-L0411).

## Slide 3: Algorithm
  Partition 2Nx2N PU into 4 NxN sub-blocks.
  Each sub-block copies a BL MV. Center position (c3) is used to derive the collocated BL block.
  MV is scaled based on the spatial ratio between EL and BL.
  If the collocated is unavailable, use IntraBL instead.
Collocated BL block
Motion data inherit
A 2Nx2N PU in EL

## Slide 4: Algorithm
  Related syntax
prediction_unit_EL( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
mdi_flag | ae(v)
if( MaxNumMergeCand > 1 && !mdi_flag) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
merge_flag[ x0 ][ y0 ] | ae(v)
if( merge_flag[ x0 ][ y0 ] ) { | 
if (PartMode = = PART_2Nx2N) | 
mdi_flag | ae(v)
if( MaxNumMergeCand > 1 && !mdi_flag) | 
merge_idx[ x0 ][ y0 ] | ae(v)

## Slide 5: Algorithm
  Compared to the motion candidate based inter-layer motion prediction,
    No change to Merge/AMVP candidate list building process.
    EL can reuse BL’s candidate list building module.
  Compared to the 4x4/8x8 granular inter-layer motion inheritance,
    The proposed method avoids partitioning the large PU (64x64, 32x32) into small blocks, so will not harm the memory bandwith efficiency of motion compensation for large blocks.

## Slide 6: Simulation and results
  Two cases are tested.
    Case 1: smallest sub-block size is 4x4.
    Case 2: smallest sub-block size is 8x8.
      For 8x8 CU, no partitioning is performed and only one BL MV is fetched.
 | Case 1 | Case 2
64x64 | 4 32x32 sub-PUs, 4 MVs | 4 32x32 sub-PUs, 4 MVs
32x32 | 4 16x16 sub-PUs, 4 MVs | 4 16x16 sub-PUs, 4 MVs
16x16 | 4 8x8 sub-PUs, 4 MVs | 4 8x8 sub-PUs, 4 MVs
8x8 | 4 4x4 sub-PUs, 4 MVs | 1 8x8 PU, 1 MV

## Slide 7: Simulation and results
  Case 1 (without the limit to 8x8)
    Average: 1.88% (uncompressed BL MV)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.5% | -5.4% | -5.2% |  |  |  | -2.9% | -7.4% | -7.7%
Class B | -2.0% | -3.5% | -3.6% | -2.2% | -3.9% | -4.1% | -2.3% | -4.3% | -4.5%
Overall (EL+BL) | -2.1% | -4.0% | -4.1% | -2.2% | -3.9% | -4.1% | -2.5% | -5.2% | -5.4%
Enc Time[%] | 98.0% |  |  | 96.4% |  |  | 99.1% |  | 
Dec Time[%] | 91.3% |  |  | 93.3% |  |  | 95.2% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.6% | -3.2% | -3.1% |  |  |  | -2.7% | -5.0% | -5.1%
Class B | -1.1% | -2.0% | -2.0% | -1.2% | -2.1% | -2.2% | -1.8% | -2.8% | -2.9%
Overall (EL+BL) | -1.2% | -2.4% | -2.3% | -1.2% | -2.1% | -2.2% | -2.1% | -3.4% | -3.5%
Enc Time[%] | 99.6% |  |  | 98.4% |  |  | 100.5% |  | 
Dec Time[%] | 93.1% |  |  | 94.5% |  |  | 96.2% |  | 

## Slide 8: Simulation and results
  Case 2 (with the limit to 8x8)
    Average: 1.78% (uncompressed BL MV)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.5% | -5.4% | -5.2% |  |  |  | -2.6% | -6.5% | -6.8%
Class B | -2.0% | -3.5% | -3.6% | -2.1% | -3.6% | -3.9% | -2.2% | -4.0% | -4.2%
Overall (EL+BL) | -2.1% | -4.0% | -4.1% | -2.1% | -3.6% | -3.9% | -2.3% | -4.7% | -4.9%
Enc Time[%] | 98.1% |  |  | 96.5% |  |  | 99.3% |  | 
Dec Time[%] | 93.7% |  |  | 93.8% |  |  | 96.2% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.6% | -3.2% | -3.1% |  |  |  | -2.2% | -4.1% | -4.2%
Class B | -1.1% | -2.0% | -2.0% | -1.1% | -1.9% | -2.0% | -1.6% | -2.5% | -2.6%
Overall (EL+BL) | -1.2% | -2.4% | -2.3% | -1.1% | -1.9% | -2.0% | -1.8% | -2.9% | -3.1%
Enc Time[%] | 99.7% |  |  | 98.5% |  |  | 100.5% |  | 
Dec Time[%] | 94.0% |  |  | 94.8% |  |  | 96.4% |  | 

## Slide 9: Comparison to TE5.3.1 (Qualcomm)
  The basic idea is quite similar
      Partition CU into sub-blocks to do BL motion prediction and motion compensation.
      Use IntraBL when BL collocated is unavailable.
  Difference:
    Sub-block size is 8x8 in TE5.3.1, and NxN in the proposed method.
  Coding results (uncompressed BL MV)
 | Y-RA-2x | Y-RA-1.5x | Y-RA-SNR | Y-LDP-2x | Y-LDP-1.5x | Y-LDP-SNR | Y-average | Enc time | Dec time
TE5.3.1 | -2.20 | -1.96 | -2.37 | -1.34 | -1.01 | -1.84 | -1.79 | 102% | 101%
the proposed | -2.12 | -2.08 | -2.28 | -1.25 | -1.10 | -1.82 | -1.78 | 99% | 95%

## Slide 10: Conclusion
  A inter-layer motion data inheritance method is proposed, by partitioning the 2Nx2N PUs into NxN sub-blocks to preform BL MV prediction and MC.
  A trade off between coding gain and implementation efficiency
    Do not worsen the worst case of MC memory access (case 2)
    Decoupled from the Merge/AMVP candidate list building.
    Keep the memory access efficiency and parallel performance of MC for large PUs.
  Performance (case 2):
    1.78% average BD-rate reduction if uncompressed BL MV is used.
    ~1.15% average BD-rate reduction is estimated if compressed BL MV is used.
    Enc/dec running time is reduced.
  Thanks to Huawei and Qualcomm for crosscheck (JCTVC-L0413, JCTVC-L0411).

## Slide 11: Back up

## Slide 12: Simulation and results
  Case 1 (without the limit to 8x8 PU)
    Average: 1.15% (compressed BL MV)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.8% | -1.8% | -1.7% |  |  |  | -1.8% | -4.1% | -4.3%
Class B | -1.2% | -2.1% | -2.1% | -1.6% | -2.7% | -2.8% | -1.8% | -3.2% | -3.3%
Overall (EL+BL) | -1.1% | -2.0% | -2.0% | -1.6% | -2.7% | -2.8% | -1.8% | -3.4% | -3.6%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.3% | -0.7% | -0.6% |  |  |  | -1.2% | -2.2% | -2.2%
Class B | -0.5% | -0.9% | -1.0% | -0.7% | -1.3% | -1.2% | -1.2% | -1.8% | -1.9%
Overall (EL+BL) | -0.5% | -0.9% | -0.9% | -0.7% | -1.3% | -1.2% | -1.2% | -1.9% | -2.0%