## Slide 1: Non-TE5: Inter-layer motion data inheritance
Wenhao Zhang, Yi-jen Chiu
Intel Corporation
JCTVC-L0291

## Slide 2: Introduction
  Apply an inter-layer motion data inheritance (MDI) mode to improve coding efficiency of SHVC.
  Features of proposed MDI:
    Only apply to the 2Nx2N PU.
    Divide the MDI PU into NxN sub-PUs to copy the BL MVs and do MC.
    Do not harm the memory access efficiency and parallel performance of large PUs.
    Do not worsen the worst case of MC memory access of EL.
  BD-rate gain:
    2.1%/2.1%/2.3% BD-rate gain for RA_2x/RA_1.5x/RA_SNR
    1.2%/1.2%/2.1% BD-rate gain for LP_2x/LP_1.5x/LP_SNR.
  Thanks to Huawei and Qualcomm for crosschecking (JCTVC-L0413, JCTVC-L0411).

## Slide 3: Algorithm
  Partition 2Nx2N PU into four NxN sub-PUs.
  Each sub-PU copies a BL MV. Center position (c3) is used to derive the collocated BL block.
  MV is scaled based on the spatial ratio between EL and BL.
  If the collocated is unavailable, use IntraBL.
  A flag is added after merge/skip flag.
Collocated BL block
Motion data inherit
A 2Nx2N PU in EL

## Slide 4: Algorithm
  Compared to the motion candidate based inter-layer motion prediction,
    The proposed method doesn’t change the logic of Merge/AMVP candidate list building process. It means the EL can reuse BL’s motion candidate list building logic module.
  Compared to the 4x4/8x8 granular inter-layer motion inheritance,
    The proposed method avoids fragmentation of large PU, so it doesn’t harm the memory access efficiency and parallel performance of large PU’s MC process.

## Slide 5: Simulation and results
  Two cases are simulated.
    Case 1 divides all 2Nx2N PUs into 4 NxN sub-PUs.
    Case 2 only copies one BL MV for 8x8 PU, instead of splitting a 8x8 PU into 4 4x4 sub-PUs. Test 2 doesn’t worsen the worst case of MC memory access.
MDI PU size | Case 1 | Case 2
64x64 | 4 32x32 sub-PUs, 4 MVs | 4 32x32 sub-PUs, 4 MVs
32x32 | 4 16x16 sub-PUs, 4 MVs | 4 16x16 sub-PUs, 4 MVs
16x16 | 4 8x8 sub-PUs, 4 MVs | 4 8x8 sub-PUs, 4 MVs
8x8 | 4 4x4 sub-PUs, 4 MVs | 1 8x8 PU, 1 MV

## Slide 6: Simulation and results
  Case 1 (without the limit to 8x8 PU)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.5% | -5.4% | -5.2% |  |  |  | -2.9% | -7.4% | -7.7%
Class B | -2.0% | -3.5% | -3.6% | -2.2% | -3.9% | -4.1% | -2.3% | -4.3% | -4.5%
Overall (EL+BL) | -2.1% | -4.0% | -4.1% | -2.2% | -3.9% | -4.1% | -2.5% | -5.2% | -5.4%
Enc Time[%] | 98.0% |  |  | 96.4% |  |  | 99.1% |  | 
Dec Time[%] | 91.3% |  |  | 93.3% |  |  | 95.2% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.6% | -3.2% | -3.1% |  |  |  | -2.7% | -5.0% | -5.1%
Class B | -1.1% | -2.0% | -2.0% | -1.2% | -2.1% | -2.2% | -1.8% | -2.8% | -2.9%
Overall (EL+BL) | -1.2% | -2.4% | -2.3% | -1.2% | -2.1% | -2.2% | -2.1% | -3.4% | -3.5%
Enc Time[%] | 99.6% |  |  | 98.4% |  |  | 100.5% |  | 
Dec Time[%] | 93.1% |  |  | 94.5% |  |  | 96.2% |  | 

## Slide 7: Simulation and results
  Case 2 (with the limit to 8x8 PU)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.5% | -5.4% | -5.2% |  |  |  | -2.6% | -6.5% | -6.8%
Class B | -2.0% | -3.5% | -3.6% | -2.1% | -3.6% | -3.9% | -2.2% | -4.0% | -4.2%
Overall (EL+BL) | -2.1% | -4.0% | -4.1% | -2.1% | -3.6% | -3.9% | -2.3% | -4.7% | -4.9%
Enc Time[%] | 98.1% |  |  | 96.5% |  |  | 99.3% |  | 
Dec Time[%] | 93.7% |  |  | 93.8% |  |  | 96.2% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.6% | -3.2% | -3.1% |  |  |  | -2.2% | -4.1% | -4.2%
Class B | -1.1% | -2.0% | -2.0% | -1.1% | -1.9% | -2.0% | -1.6% | -2.5% | -2.6%
Overall (EL+BL) | -1.2% | -2.4% | -2.3% | -1.1% | -1.9% | -2.0% | -1.8% | -2.9% | -3.1%
Enc Time[%] | 99.7% |  |  | 98.5% |  |  | 100.5% |  | 
Dec Time[%] | 94.0% |  |  | 94.8% |  |  | 96.4% |  | 

## Slide 8: Conclusion
  A inter-layer motion data inheritance method is proposed, by partitioning the 2Nx2N PUs into NxN sub-PUs to copy BL MV and perform MC.
  A trade off between coding gain and implementation efficiency
    Do not worsen the worst case of MC memory access
    Decoupled from the Merge/AMVP candidate list building.
    Keep the memory access efficiency and parallel performance of MC for large PUs.
  Achieve 2.1% ~ 2.3% BD-rate gain for RA cases, 1.1% ~ 1.8% BD-rate gain for LP cases.
  It is suggested the case 2 (limit to 8x8) is considered for adoption into the reference software.
  Thanks to Huawei and Qualcomm for crosschecking (JCTVC-L0413, JCTVC-L0411).

## Slide 9: Back up

## Slide 10: Simulation and results
  Two additional cases were tested.
    Case 3 divides all 2Nx2N PUs into 4 NxN sub-PUs, and copy compressed BL MV.
    Case 4 only copies one BL MV for all 2Nx2N PUs.
MDI PU size | Case 3 | Case 4
64x64 | 4 32x32 sub-PUs, 4 MVs, compressed BL MV | 1 64x64 PU, 1 MV, uncompressed BL MV
32x32 | 4 16x16 sub-PUs, 4 MVs, compressed BL MV | 1 32x32 PU, 1 MV, uncompressed BL MV
16x16 | 4 8x8 sub-PUs, 4 MVs, compressed BL MV | 1 16x16 PU, 1 MV, uncompressed BL MV
8x8 | 4 4x4 sub-PUs, 4 MVs, compressed BL MV | 1 8x8 PU, 1 MV, uncompressed BL MV

## Slide 11: Simulation and results
  Case 3 (without the limit to 8x8, copy compressed BL MV)
    Reference: SMuC0.1.1
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.8% | -1.8% | -1.7% |  |  |  | -1.8% | -4.1% | -4.3%
Class B | -1.2% | -2.1% | -2.1% | -1.6% | -2.7% | -2.8% | -1.8% | -3.2% | -3.3%
Overall (EL+BL) | -1.1% | -2.0% | -2.0% | -1.6% | -2.7% | -2.8% | -1.8% | -3.4% | -3.6%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.3% | -0.7% | -0.6% |  |  |  | -1.2% | -2.2% | -2.2%
Class B | -0.5% | -0.9% | -1.0% | -0.7% | -1.3% | -1.2% | -1.2% | -1.8% | -1.9%
Overall (EL+BL) | -0.5% | -0.9% | -0.9% | -0.7% | -1.3% | -1.2% | -1.2% | -1.9% | -2.0%

## Slide 12: Simulation and results
  Case 4 (limit all 2Nx2N PUs inherit only one BL MV)
    Reference: Our TE5.2.4 with uncompressed MV
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.4% | 0.7% | 0.7% |  |  |  | 0.4% | 0.8% | 0.8%
Class B | 0.3% | 0.5% | 0.5% | 0.3% | 0.3% | 0.3% | 0.4% | 0.5% | 0.5%
Overall (EL+BL) | 0.4% | 0.6% | 0.6% | 0.3% | 0.3% | 0.3% | 0.4% | 0.6% | 0.6%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | 0.2% | 0.6% | 0.4% |  |  |  | 0.5% | 0.6% | 0.9%
Class B | 0.2% | 0.5% | 0.6% | 0.2% | 0.2% | 0.2% | 0.4% | 0.3% | 0.6%
Overall (EL+BL) | 0.2% | 0.5% | 0.6% | 0.2% | 0.2% | 0.2% | 0.4% | 0.4% | 0.6%