## Slide 1: TE5: Results of test 5.2.9 on inter-layer motion prediction
Kiran Misra, Jie Zhao, Andrew Segall
(JCTVC-L0297)

## Slide 2: Organization
Introduction
Proposed changes
  Description
  Characteristics
Results
Conclusion

## Slide 3: Introduction
Goals:
  Use base layer motion information for predicting enhancement layer motion information
  Minimize number of changes from base layer
SMuC 0.1.1 framework used: Intra BL

## Slide 4: Proposed changes
DESCRIPTION
Inclusion of one base layer based merge list candidate after the temporal candidate
Inclusion of a primary motion vector predictor based on base layer motion

## Slide 5: Proposed changes
CHARACTERISTICS
One base layer motion information fetch mechanism for merge/AMVP
One motion vector scaling mechanism
No modification of the base layer pruning and redundancy checks for merge list
The pixel location used in fetching the base layer motion information is the same as that used for the temporal candidate

## Slide 6: Experimental Results
TE5 test conditions
BD rate with SMuC 0.1.1 anchors
 | Y-RA-2x | Y-RA-1.5x | Y-RA-SNR | Y-LDP-2x | Y-LDP-1.5x | Y-LDP-SNR
Merge only | -1.9% | -2.0% | -2.0% | -1.1% | -1.1% | -1.3%
AMVP only | -1.3% | -1.3% | -1.3% | -0.8% | -0.7% | -0.8%
Merge+AMVP | -2.1% | -2.2% | -2.2% | -1.2% | -1.2% | -1.4%

## Slide 7: Detailed experimental results – Merge only
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.9% | -3.3% | -3.3% |  |  |  | -1.9% | -3.5% | -3.8%
Class B | -1.9% | -2.8% | -2.9% | -2.0% | -2.7% | -3.0% | -2.0% | -2.9% | -3.1%
Avg. EL+BL | -1.9% | -3.0% | -3.0% | -2.0% | -2.7% | -3.0% | -2.0% | -3.1% | -3.3%
Avg. EL | -3.4% | -5.3% | -5.5% | -5.0% | -6.7% | -7.2% | -3.9% | -5.7% | -6.2%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.1% | -1.9% | -1.8% |  |  |  | -1.3% | -2.0% | -2.0%
Class B | -1.1% | -1.4% | -1.6% | -1.1% | -1.4% | -1.5% | -1.3% | -1.6% | -1.8%
Avg. EL+BL | -1.1% | -1.6% | -1.7% | -1.1% | -1.4% | -1.5% | -1.3% | -1.7% | -1.9%
Avg. EL | -1.8% | -2.6% | -2.7% | -2.4% | -2.9% | -3.2% | -2.2% | -2.8% | -3.0%

## Slide 8: Detailed experimental results – AMVP only
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.4% | -2.3% | -2.4% |  |  |  | -1.3% | -2.3% | -2.6%
Class B | -1.3% | -1.8% | -1.9% | -1.3% | -1.6% | -1.9% | -1.3% | -1.9% | -2.0%
Avg. EL+BL | -1.3% | -1.9% | -2.0% | -1.3% | -1.6% | -1.9% | -1.3% | -2.0% | -2.2%
Avg. EL | -2.3% | -3.4% | -3.6% | -3.4% | -3.8% | -4.4% | -2.6% | -3.6% | -4.0%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.9% | -1.4% | -1.4% |  |  |  | -0.9% | -1.4% | -1.3%
Class B | -0.7% | -1.0% | -1.0% | -0.7% | -0.9% | -1.1% | -0.8% | -1.0% | -1.1%
Avg. EL+BL | -0.8% | -1.1% | -1.1% | -0.7% | -0.9% | -1.1% | -0.8% | -1.1% | -1.2%
Avg. EL | -1.3% | -1.8% | -1.8% | -1.6% | -1.9% | -2.2% | -1.4% | -1.8% | -1.9%

## Slide 9: Detailed experimental results – Merge+AMVP
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -2.2% | -3.8% | -3.8% |  |  |  | -2.1% | -4.0% | -4.3%
Class B | -2.0% | -3.1% | -3.3% | -2.2% | -3.0% | -3.2% | -2.2% | -3.2% | -3.4%
Avg. EL+BL | -2.1% | -3.3% | -3.4% | -2.2% | -3.0% | -3.2% | -2.2% | -3.4% | -3.7%
Avg. EL | -3.7% | -5.9% | -6.1% | -5.5% | -7.2% | -7.8% | -4.2% | -6.3% | -6.8%
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.3% | -2.0% | -2.0% |  |  |  | -1.4% | -2.1% | -2.1%
Class B | -1.1% | -1.5% | -1.6% | -1.2% | -1.5% | -1.6% | -1.3% | -1.7% | -1.8%
Avg. EL+BL | -1.2% | -1.7% | -1.7% | -1.2% | -1.5% | -1.6% | -1.4% | -1.8% | -1.9%
Avg. EL | -1.9% | -2.8% | -2.9% | -2.5% | -3.0% | -3.3% | -2.2% | -2.9% | -3.0%

## Slide 10: Conclusion
The proposed changes exploit the base layer motion information without significant modifications to single layer scheme
No modification of the base layer pruning and redundancy checks for merge list
One base layer motion information fetch and scaling mechanism