## Slide 1
AHG8: P2M based dual-coder Extension of HEVC
JCTVC-L0303
14 Jan. – 23 Jan. 2013
Tao Lin

## Slide 2
Screen picture has two types of content
  Continuous-tone content + Discontinuous-tone content
Hybrid coding is not discontinuous-tone oriented
  Even 444 has bad quality (due to high QP) at low bit-rate
Pseudo-2D-matching coder can do a much better job
  2D pixel data oriented dictionary-like coder
  Using a super-large searching-window
Motivation

## Slide 3
P2M coder
LCU
m
LCU
0
LCU
1
LCU
2
LCU
h
LCU
h+1
LCU
h+2
1st matched string (red) has 42 samples=14 pixels
2nd matched string (blue) has 33 samples
3rd matched string (green) has 45 samples
LCU
h-1
LCU
2h-1

## Slide 4
seq_parameter_set_rbsp( ) { | Descriptor
video_parameter_set_id | u(4)
<snip ……> | 
dual_coder_mode | ue(v)
log2_max_pic_order_cnt_lsb_minus4 | ue(v)
<snip ……> | 
rbsp_trailing_bits( ) | 
} | 
P2M coder

## Slide 5
P2M coder
coding_tree_unit( x0, y0, log2CbSize ) { | Descriptor
xCtb = ( CtbAddrRS % PicWidthInCtbsY ) << Log2CtbSizeY | 
yCtb = ( CtbAddrRS / PicHeightInCtbsY ) << Log2CtbSizeY | 
CtbAddrInSliceSeg = CtbAddrInRS − slice_segment_address | 
if( slice_sao_luma_flag ¦ ¦ slice_sao_chroma_flag ) | 
sao( xCtb >> Log2CtbSizeY, yCtb >> Log2CtbSizeY ) | 
if(dual_coder_mode = = 0) | 
coding_quadtree( xCtb, yCtb, Log2CtbSizeY, 0 ) | 
else { | 
ctu_coded_by_p2m_coder_flag | ae(v)
if(cu_coded_by_p2m_coder_flag = = 0) //HYBRID_CODER | 
coding_quadtree( xCtb, yCtb, Log2CtbSizeY, 0 ) | 
else | 
p2m_coder( x0, y0, Log2CtbSizeY ) | 
} | 
} | 

## Slide 6
P2M_coder( x0, y0, log2CtbSizeY ) { | Descriptor
decoded_sample_count = 0 | 
NumSamplesInCTU = (3 << (log2CtbSizeY << 1)) | 
while(decoded_sample_count < NumSamplesInCTU) { | 
matching_string_flag | ae(v)
if(matching_string_flag = = 1) { | 
matching_string_distance_use_recent_8_flag | ae(v)
if(matching_string_distance_use_recent_8_flag = = 1) { | 
matching_string_distance_recent_8_idx | ae(v)
matching_string_distance_minus1 = Recent8Distances[matching_string_distance_recent_8_idx] | 
for( i = matching_string_distance_recent_8_idx; i > 0; i-- ) | 
Recent8Distances[i] = Recent8Distances[i-1] | 
Recent8Distances[0] = matching_string_distance_minus1 | 
} | 
else { | 
matching_string_distance_minus1 | ae(v)
for( i = 7; i > 0; i-- ) | 
Recent8Distances[i] = Recent8Distances[i-1] | 
Recent8Distances[0] = matching_string_distance_minus1 | 
} | 
matching_string_length_minus2 | ae(v)
decoded_sample_count += (matching_string_length_minus2 + 2) | 
} | 
else { | 
unmatchable_sample_residual_abs | ae(v)
unmatchable_sample_residual_sign | ae(v)
decoded_sample_count += 1 | 
} | 
} | 
} | 
P2M coder

## Slide 7
24 AHG8 test sequences
Experimental Results
 |  |  | AI_main |  |  | LP_main |  | 
 |  |  | BD-rate (cubic) |  |  | BD-rate (cubic) |  | 
 |  | level | Y | U | V | Y | U | V
Class F (YUV420) | BasketballDrillText | level_4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | ChinaSpeed | level_4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | SlideEditing | level_4 | -0.4% | -0.6% | -0.6% | -0.6% | -0.9% | -0.9%
 | SlideShow | level_4 | -1.3% | -0.8% | -0.7% | -0.4% | -0.1% | -0.3%
SC (YUV444) | VenueVu | level_4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | cad-waveform | level_1 | -66.9% | -68.1% | -69.1% | -61.2% | -62.0% | -62.1%
 | cad-waveform | level_4 | -75.8% | -76.7% | -78.0% | -71.3% | -72.1% | -72.2%
 |  | level_7 | -81.1% | -81.9% | -83.1% | -77.0% | -77.8% | -78.1%
 | pcb-layout | level_1 | -70.2% | -71.3% | -73.2% | -58.5% | -59.4% | -60.3%
 | pcb-layout | level_4 | -78.5% | -79.4% | -80.8% | -67.9% | -68.6% | -69.5%
 |  | level_7 | -78.8% | -79.7% | -81.0% | -68.4% | -69.2% | -70.0%

## Slide 8
24 AHG8 test sequences
Experimental Results
SC(YUV444) | ppt-doc-xls | level_1 | -44.9% | -44.7% | -46.9% | -35.5% | -36.3% | -38.7%
 | ppt-doc-xls | level_4 | -52.1% | -52.0% | -54.1% | -43.2% | -44.0% | -46.1%
 |  | level_7 | -60.5% | -60.2% | -61.9% | -50.3% | -51.0% | -52.7%
 | vc-doc-sharing | level_1 | -38.8% | -41.6% | -41.2% | -39.3% | -44.4% | -42.5%
 | vc-doc-sharing | level_4 | -55.6% | -57.8% | -57.5% | -58.4% | -63.1% | -61.8%
 |  | level_7 | -83.2% | -84.4% | -84.1% | -70.1% | -74.2% | -73.2%
 | web-browsing | level_1 | -39.1% | -44.6% | -40.7% | -17.9% | -19.8% | -16.7%
 | web-browsing | level_4 | -64.3% | -69.3% | -66.8% | -48.2% | -50.3% | -46.9%
 |  | level_7 | -91.0% | -93.0% | -92.3% | -60.6% | -63.0% | -60.0%
 | cg_twist_tunnel | level_4 | -18.8% | -28.0% | -27.9% | -3.4% | -15.9% | -16.0%
 | wordEditing | level_4 | -13.1% | -13.1% | -13.2% | -4.1% | -4.7% | -4.6%
 |  | level_7 | -60.8% | -59.8% | -59.9% | -8.5% | -9.9% | -9.8%
 | map | level_4 | -7.9% | -13.5% | -16.7% | -2.1% | -5.3% | -8.2%
 | programmming | level_4 | -12.4% | -13.2% | -13.9% | -4.2% | -5.4% | -6.3%

## Slide 9
24 AHG8 test sequences
Experimental Results
SC (GBR444) | VenueVu | level_4 | 1.1% | 1.5% | 1.1% | 0.0% | 0.0% | 0.0%
 | cad-waveform | level_4 | -76.0% | -76.2% | -76.7% | -72.1% | -73.0% | -72.7%
 | pcb-layout | level_4 | -84.5% | -84.7% | -85.6% | -72.9% | -73.0% | -73.6%
 | ppt-doc-xls | level_4 | -59.2% | -59.2% | -59.1% | -54.1% | -54.4% | -54.7%
 | vc-doc-sharing | level_4 | -61.6% | -61.5% | -62.5% | -64.8% | -65.0% | -66.7%
 | web-browsing | level_4 | -67.3% | -68.1% | -67.7% | -53.8% | -54.0% | -54.1%
 | cg_twist_tunnel | level_4 | -52.0% | -51.9% | -52.1% | -29.7% | -29.5% | -29.5%
 | wordEditing | level_4 | -33.7% | -31.9% | -32.2% | -13.1% | -13.0% | -13.1%
 | map | level_4 | -28.0% | -25.0% | -25.1% | -13.7% | -13.7% | -14.1%
 | programmming | level_4 | -32.4% | -29.5% | -28.7% | -6.8% | -7.1% | -6.8%
 | Average of 24 | level_4 | -35.0% | -35.6% | -36.0% | -27.4% | -28.5% | -28.7%
 |  | Enc Time | 110% | Dec Time | 66% | 99% | Dec Time | 88%

## Slide 10
Conclusions
P2M based dual-coder is a straightforward yet very effective extension of HEVC for SCC
Basically just adding three new syntax elements in LCU
Significant BD-rate reduction and subjective improvement
  AI-main: 0% to 85% with an average of 35%
  LP-main: 0% to 73% with an average of 27%
After 4 complete meeting cycles, quite mature now
Propose to adopt the P2M based dual-coder extension

## Slide 11
THANK YOU