## Slide 1
YUV444 and RGB screen content test sequences
JCTVC-L0313
14 Jan. – 23 Jan. 2013
Tao Lin

## Slide 2
Traditional video: relatively smooth edges, complicated textures, and thick lines with virtually unlimited colors
Screen content video: very sharp edges, simple shapes, and thin lines with few colors, even one-pixel-wide single-color lines
Screen contents seen in daily activities:
  Web browsing
  Video conferencing with document sharing
  Office document editing
  Engineering drawing
  Hardware design engineering
  Software programming
  Gaming
  Map navigating and address direction searching
Motivation

## Slide 3
Sequence Name | sc_cad_waveform sc_pcb_layout sc_ppt_doc_xls | sc_web_browsing sc_video_conferencing_doc_sharing sc_cg_twist_tunnel
Resolution | 1920 × 1080p | 1280 × 720p
Frame rate | 20 fps, progressive | 30 fps, progressive
Bit depth | 8 | 8
Color format | planar RGB and YUV 4:4:4 | planar RGB and YUV 4:4:4
Duration | 10 seconds (200 frames) | 10 seconds (300 frames)
Screen Content Sequences

## Slide 4
Screen Content Sequences
No | File name | Brief description | Features
1 | sc_cad_waveform_1920x1080_20_200_8bit | CAD waveform | Typical digital circuit design waveform with code and schematic windows One pixel thin lines with many colors Scrolling Zooming
2 | sc_pcb_layout_1920x1080_20_200_8bit | PCB layout windows | Typical PCB layout window Display of multiple layers with different colors Component footprint display One pixel diagonal, horizontal, vertical lines and curves with different colors Enabling/disabling display of some layers Moving around Zooming in and out
3 | sc_ppt_doc_xls_1920x1080_20_200_8bi | Ppt, doc, and xls windows | Text, graph, chart Copy and paste between ppt, doc, and xls windows One pixel thin lines and curves Zooming chart and graph
4 | sc_web_browsing_1280x720_30_300_8bit | Web browsing | Browsing different webpages
5 | sc_video_conferencing_doc_sharing_1280x720_30_300_8bit | Video conferencing with doc sharing | A video conferencing window A document sharing window Switching between excel sheets with texts or plots Excel sheet scrolling and panning
6 | sc_cg_twist_tunnel_1280x720_30_8bit | 3D computer graphics | Fast spinning twist Fast moving tunnel Texture-mapped and light-shaded (using Gouraud shading) rendering Underneath wireframe rendering

## Slide 6
Conclusions
Total 14 AHG8 test sequences with different contents
  4 class F
  4 Huawei/MERL
  6 TJ
cover a variety of different screen contents
Propose to adopt these sequences for the study and improvement of HEVC for screen content coding

## Slide 7
THANK YOU