## Slide 1: Comparison of Compression Performance of HEVC Draft 9 with AVC High Profile and Performance of HM9.0 with Temporal Scalability Characteristics
University of Science and Technology of China
Microsoft Corp.

## Slide 2: Comparison between HM-9.0 and JM-18.4
Similar as previous proposals
Update to HM-9.0 and JM-18.4
  All Intra case: 22% bit saving
  Random Access case: 34% bit saving
  Low Delay case: 37% bit saving

## Slide 3: HM-9.0 with temporal scalability
Use the following GOP structure for RA case
 | RA-Main |  |  | RA-HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 1.0% | 0.1% | −0.1% | 1.0% | 0.2% | −0.1%
Class B | 0.3% | −0.1% | −0.1% | 0.4% | 0.2% | 0.2%
Class C | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2%
Class D | −0.1% | −0.1% | −0.1% | −0.1% | 0.2% | −0.2%
Overall | 0.3% | 0.0% | −0.1% | 0.3% | 0.2% | 0.0%
Class F | 0.3% | 0.2% | 0.3% | 0.2% | 0.2% | 0.2%
Enc. T. | 98% |  |  | 98% |  | 
Dec. T. | 101% |  |  | 101% |  | 

## Slide 4: HM-9.0 with temporal scalability (Cont.)
Average 0.3% loss
  Best average among several kinds of GOP structure setting
Most loss cause by the two 10-bit sequences in Class A
Encoding time decrease
  Only 2 reference pictures are used at temporal level 0

## Slide 5: Temporal scalability for LD cases
Performance loss due to not using the nearest picture as reference
  About 8% ~ 9% performance loss
Three temporal layers are supported

## Slide 6: Experimental Results
 | LB-Main |  |  | LB-HE10 |  | 
 | Y | U | V | Y | U | V
Class B | 9.4% | 5.0% | 3.7% | 9.9% | 7.1% | 5.6%
Class C | 10.5% | 9.2% | 9.0% | 10.7% | 10.0% | 9.4%
Class D | 7.5% | 5.3% | 3.8% | 7.7% | 7.1% | 5.4%
Class E | 8.0% | 5.1% | 3.5% | 8.9% | 8.8% | 8.1%
Overall | 8.9% | 6.1% | 5.0% | 9.4% | 8.2% | 7.0%
Class F | 19.1% | 19.8% | 20.8% | 19.1% | 19.5% | 19.5%
Enc. T. | 98% |  |  | 98% |  | 
Dec. T. | 100% |  |  | 100% |  | 
 | LP-Main |  |  | LP-HE10 |  | 
 | Y | U | V | Y | U | V
Class B | 7.8% | 3.5% | 2.1% | 7.9% | 4.8% | 4.1%
Class C | 9.1% | 7.6% | 7.2% | 9.1% | 8.1% | 7.6%
Class D | 7.0% | 5.4% | 3.0% | 6.8% | 6.2% | 5.4%
Class E | 6.9% | 5.3% | 3.5% | 7.8% | 7.9% | 7.7%
Overall | 7.7% | 5.3% | 3.9% | 7.9% | 6.6% | 5.9%
Class F | 17.8% | 18.6% | 19.0% | 17.7% | 18.8% | 18.7%
Enc. T. | 100% |  |  | 100% |  | 
Dec. T. | 101% |  |  | 100% |  | 

## Slide 7
Thank you!