## Slide 1
SPECIFICATION OF ACTIVE REFERENCE INDICES AND DECODED PICTURE BUFFER JCTVC-L0323
Zhijie Yang, Brian Heng and Wade Wan
Broadcom Corporation

## Slide 2: DECODED PICTURE BUFFER (DPB)
H.264/AVC
  Current picture stored in separate buffer from DPB
  Max number of reference frames = DPB size
Current HEVC text
  Current picture directly stored in DPB
  Max number of reference frames = DPB size – 1
Difference causes some values that were valid in H.264/AVC to no longer be valid or consistent for HEVC
Concern: Encoders incorrectly use “one too many” reference frames
Proposal:
  Reduce max number of active reference indices from 16 to 15
  Increase min size of decoded picture buffer from 0 to 1
  Reduce max number of all types of reference pictures by 1
Notes: <number>

## Slide 3: MAX NUMBER OF ACTIVE REFERENCE INDICES
Max DPB size = 16 and max num of reference pictures = 15
But max num of active reference indices = 16
Although reference picture list could be filled up using duplicate reference pictures, suggest change to so specification is clearer and more consistent with convention in H.264/AVC
Proposal:
  Reduce max number of active reference indices from 16 to 15
  More specifically, changing max value for these parameters from 15 to 14:
    num_ref_idx_l0_default_active_minus1
    num_ref_idx_l1_default_active_minus1
    num_ref_idx_l0_active_minus1
    num_ref_idx_l1_active_minus1

## Slide 4: DECODED PICTURE BUFFER SIZE
max_dec_picture_buffering allowed to be 0 in text
But the DPB includes the current decoded picture so it shall always have at least one picture buffer
Proposal:
  Increase min size of decoded picture buffer from 0 to 1
  More specifically, changing min value for these parameters from 0 to 1:
    vps_max_dec_pic_buffering
    sps_max_dec_pic_buffering

## Slide 5: NUMBER OF ALL TYPES OF REFERENCE PICTURES
To be consistent with other changes, reduce max number of all types of reference pictures by 1
Proposal:
  More specifically, add -1 to the equations for:
    num_negative_pics
    num_positive_pics
    num_long_term_sps
    num_long_term_pics