## Slide 1: JCT-VC L0334: Color Gamut Scalable Video Coding
Louis Kerofsky, Seung-Hwan Kim, Kiran Misra and Andrew Segall
Presenter: Andrew Segall

## Slide 2: Reminder
We previously proposed Color Gamut Scalable Video Coding in last meeting (JCTVC-K0241)
Key Differences between L0334 and K0241
  Tool ported to TMuC software
  Support for combined spatial and color gamut scalability
  Results using wider gamut material
Color Gamut Scalability required by MPEG parent body
  M24484 – “Requirements for the scalable enhancement of HEVC” (S-2.10)
    The scalability extension shall support a base and enhancement layer with different color spaces
    The scalability extension shall support a combination of color space scalability and spatial scalability.
    The scalability extension shall support tristimulus values in the enhancement layer that can not be represented in the base layer color space.

## Slide 3: Outline
Motivation
  BT.709 vs. BT.2020
Proposed Color gamut Scalable Video Coding
  Scalable coding system supporting color space prediction
  Color predictor parameter design (Bit increment/Gain offset)
Results
Conclusions

## Slide 4: Motivation
Upcoming deployment of UHDTV devices and content will use a different color gamut
  HD uses the BT.709 recommendation [1]
  UHDTV will use the BT.2020 recommendation [2]
Color gamut of UHDTV is significantly larger than HD as shown in Figure 1
Recent recommendation BT.2020 for UHDTV
  Resolutions 3840x2160 or 7680x4320 (4K and 8K)
  Primaries differ from BT.709 much wider gamut white point still D65
  Luma and chroma definitions some what differ but similar
  Quantization Bit-depth 10, 12 (no 8-bit)
Figure 1. Gamut of UHDTV significantly larger in both green and red primaries. Identical white point used for each D65.
[1] ITU-R Recommendation BT.709 “Parameter values for the HDTV standards for production and international programme exchange” Dec. 2010.
[2] ITU-R Recommendation BT.2020 “Parameter values for UHDTV systems for production and international programme exchange” April 2012.

## Slide 5: Proposed Color Gamut Scalability
Supports a change in bit-depth between BL and EL
  Motivated by the definition of BT.2020 as either a 10-bit or 12-bit color gamut, as compared to the common use of 8-bit BT.709 in consumer applications
Supports “color gamut scalability” which is different from the idea of “color format scalability”
  The previous work [3] is concerned with the change in the chroma subsampling format, or resolution rather than the color gamut
Proposed color space scalable coder shown in Figure 2
  Apply designed/developed color predictor
  Estimate enhancement layer data from a given BT.709 (BL) information
Input
BT.709
Input
BT.2020
Base Layer
Encoding Loop
Enhancement Layer
Encoding Loop
Base Layer
Reference
Bitstream
Multiplex
Enhancement Layer
Reference
Color Space
Predictor
Upsampling
[3] H. Schwarz, D. Marpe, and T. Wiegand, “Overview of the Scalable Video Coding extension of the H.264/AVC standard,” IEEE Trans.
Circuits Syst. Video Technol., vol. 17, no. 9, pp. 1103–1120, Sept. 2007.
Figure 2. Color Space Scalable Coder

## Slide 6: Color Gamut Predictors
We propose support for two prediction methods
  Gain-Offset
  Bit-increment
Features
  Approximation of color gamut conversion without explicit calculation
    YCbCr to R’G’B’ conversion using the matrix of BT.709
    R’G’B’ to RGB using the nonlinearity of BT.709, (gamma)
    RGB to XYZ using primary chromaticity values from BT.709
    XYZ to RGB using primary chromaticity values from BT.2020 (UHDTV)
    RGB to R’G’B’ using the nonlinearity of BT.2020 (UHDTV)
    R’G’B’ to YCbCr conversion using matrix of BT.2020 (UHDTV)
  Color channels processed independently
Gain-Offset parameters designed off-line or on-line (sequence adaptive or fixed)
 | Bit Increment | Gain Offset
YUHDTV | Y709 <<2 | g1 ·Y709 + o1
UUHDTV | U709 <<2 | g2 ·U709 + o2
VUHDTV | V709 <<2 | g3 ·V709 + o3
Side Information | No parameters to send | 6 parameters
Table 1. Two color predictors (BI vs. GO)

## Slide 7: Proposal Details
Syntax
color_prediction_model | Name
0 (BI) | Bit Increment
1 (GO-NA) | Fixed Gain Offset
2 (GO-SA) | Gain Offset Picture Adaptive
pps_extension_flag
if( pps_extension_flag )
use_color_prediction
if(use_color_prediction)
color_pred_data ( )
rbsp_trailing_bits( )
color_prediction_model
if(color_prediction_model==2) {
numFractionBits
for( I = 0; I < 3; i++ ){
color_predictor_gain [ I ]
color_predictor_offset [ I ]
}
}
Prediction defined by
Pred[c][x][y] = (gain[c]*In[x][y] + (1<<(numFractionBits-1))>> numFractionBits + offset[c]

## Slide 8: Why Gain-Offset?
Motivation for Gain-Offset
  Analysis shows linear approximation is well motivated for related BT.709 and BT.2020.

## Slide 9: Color Space scalable tests
Performance
  Two scenarios:
    BT.709 input sequences (converted to BT.2020 for enhancement layer)
    BT.2020 input sequences (converted to BT.709 for base layer)
  Test conditions
    AI-2X and RA-2X (same rate points as TE)
    AI-CGS and RA-CGS (no resolution change)
    QP scaling enabled when coding BT.2020 layers to normalize scaling with BT.709

## Slide 10: Color Space scalable tests
Performance
  First Scenario
    Use common test sequences
BT.709 BL data (presented as BT.709)
BT.2020 EL data (presented as BT.709)

## Slide 11: Chromaticity of SWG-1 to SWG-5 content
Performance
  Second Scenario
    BT.2020 sequences (internal)
    HD and 4K source
    Natural content and professionally captured
    Out of gamut colors projected to BT.709 boundary for baselayer creation; CfP downsamplers used.

## Slide 12: Simulcast Comparison Example (Traffic)
The single layer is compared to the Base Layer + Enhancement Layer in terms of BD rate. The RD performance of the gain offset model compared to the bit increment model is seen in all color channels but largest in the V channel.

## Slide 13: Enhancement Layer Comparison Example (Traffic)
The Enhancement Layers are compared, the Bit-Difference and the NonAdaptive and Sequence Adaptive Gain Offset

## Slide 14: Performance Comparison (EL only)
 |  | AI HEVC 2x |  |  | AI HEVC CGS |  | 
 |  | Y | U | V | Y | U | V
 | BI | -43.5% | -47.2% | -44.8% | -91.0% | -90.8% | -90.3%
Class A | GO-NA | -42.8% | -47.1% | -46.6% | -94.1% | -94.0% | -94.4%
 | GO-SA | -46.2% | -49.7% | -49.7% | -95.7% | -95.7% | -95.9%
 | BI | -29.0% | -32.6% | -29.0% | -86.9% | -86.4% | -85.3%
Class B | GO-NA | -28.6% | -33.1% | -30.5% | -91.1% | -90.8% | -91.0%
 | GO-SA | -33.0% | -36.7% | -34.7% | -93.1% | -93.0% | -93.1%
 | BI | -22.4% | -25.7% | -23.5% | -49.8% | -48.6% | -47.8%
SWG | GO-NA | -28.6% | -32.4% | -31.2% | -60.3% | -59.5% | -59.4%
 | GO-SA | -29.7% | -33.2% | -32.2% | -62.2% | -60.8% | -61.0%
 |  | RA HEVC 2x |  |  | RA HEVC CGS |  | 
 |  | Y | U | V | Y | U | V
 | BI | -31.2% | -26.2% | -15.9% | -81.5% | -80.0% | -72.3%
Class A | GO-NA | -29.1% | -25.3% | -25.9% | -85.6% | -84.5% | -85.4%
 | GO-SA | -34.0% | -27.8% | -26.1% | -90.3% | -89.5% | -90.2%
 | BI | -20.6% | -20.1% | -14.5% | -76.3% | -73.9% | -66.4%
Class B | GO-NA | -20.0% | -20.2% | -16.9% | -81.0% | -79.1% | -80.2%
 | GO-SA | -24.6% | -23.0% | -20.0% | -86.3% | -84.6% | -85.2%
 | BI | -13.3% | -14.4% | -10.0% | -37.1% | -34.4% | -32.4%
SWG | GO-NA | -17.3% | -17.7% | -12.5% | -44.5% | -39.3% | -38.3%
 | GO-SA | -17.9% | -18.0% | -13.0% | -46.5% | -40.7% | -39.7%

## Slide 15: Performance Comparison (BL+EL)
 |  | AI HEVC 2x |  |  | AI HEVC CGS |  | 
 |  | Y | U | V | Y | U | V
 | BI | -25.10% | -29.60% | -26.90% | -45.40% | -45.00% | -41.70%
Class A | GO-NA | -24.20% | -29.40% | -29.00% | -47.10% | -46.80% | -49.80%
 | GO-SA | -26.90% | -31.40% | -31.60% | -47.60% | -48.20% | -51.00%
 | BI | -17.10% | -21.30% | -17.50% | -43.30% | -42.50% | -38.10%
Class B | GO-NA | -16.60% | -21.70% | -19.00% | -45.40% | -44.90% | -46.50%
 | GO-SA | -19.80% | -24.00% | -22.10% | -46.20% | -46.40% | -47.80%
 | BI | -12.10% | -16.00% | -13.50% | -24.70% | -23.60% | -22.40%
SWG | GO-NA | -15.60% | -20.20% | -18.80% | -29.80% | -29.20% | -29.30%
 | GO-SA | -16.10% | -20.70% | -19.40% | -30.90% | -29.60% | -29.90%
 |  | RA HEVC 2x |  |  | RA HEVC CGS |  | 
 |  | Y | U | V | Y | U | V
 | BI | -16.60% | -10.40% | 1.30% | -40.80% | -35.30% | -8.50%
Class A | GO-NA | -14.70% | -9.90% | -11.00% | -42.90% | -37.10% | -41.60%
 | GO-SA | -18.30% | -10.50% | -8.70% | -44.60% | -38.70% | -43.30%
 | BI | -11.60% | -11.30% | -5.10% | -38.10% | -32.70% | -11.80%
Class B | GO-NA | -10.80% | -11.30% | -7.70% | -39.20% | -35.20% | -39.00%
 | GO-SA | -14.00% | -12.40% | -9.20% | -42.40% | -36.10% | -38.80%
 | BI | -7.80% | -9.10% | -4.60% | -20.40% | -17.40% | -14.90%
SWG | GO-NA | -10.40% | -10.90% | -5.40% | -24.50% | -17.90% | -16.60%
 | GO-SA | -10.80% | -10.90% | -5.80% | -26.20% | -18.70% | -17.20%

## Slide 16: Conclusions
Scalable video coding is beneficial to support both full HD and UHDTV content.
In addition to resolution, BT.2020 also includes a color gamut and bit-depth transition.
The proposed method of color prediction gives improvement in the ability to predict BT.2020 data from BT.709 data represented in different color spaces.
Adaptive Gain Offset model provides low complexity while improving the results scalable coding results compared to bit shift approach.
Cross check in JCVC-L0145 (Thanks to SONY)
We propose adopting the gain offset based color prediction tool into future scalable HEVC design. General gain offset parameters are carried in the PPS and the color prediction is applied following any up sampling if present.

## Slide 17: JCT-VC L0334: Color Gamut Scalable Video Coding
Louis Kerofsky, Seung-Hwan Kim, Kiran Misra and Andrew Segall
Presenter: Andrew Segall