## Slide 1: JCTVC-L0336: Non-TE5: on motion mapping in SHVC Jianle Chen, Vadim Seregin, Liwei Guo, Marta Karczewicz,
Notes: Preparation for the 8-th JCT-VC meeting
Possible topics to look into (JS)

## Slide 2: Summary of the proposed method
In the current reference software, motion field of Interlayer reference (ILR) picture is missing.
Motion field mapping is necessary to enable TMVP on ILR without low level modification
  For each 16x16 EL block
    Copy collocated MV and prediction mode
    Aligned to motion compression method of HEVC
  Using compressed base-layer motion field

## Slide 3: Experimental results
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.7% | -2.4% | -2.6% |  |  |  | -1.6% | -3.9% | -4.5%
Class B | -1.2% | -2.7% | -3.1% | -1.7% | -3.0% | -3.4% | -2.1% | -4.0% | -4.5%
Overall (EL+BL) | -1.1% | -2.6% | -3.0% | -1.7% | -3.0% | -3.4% | -2.0% | -4.0% | -4.5%
Overall (EL) | -2.1% | -4.7% | -5.3% | -4.4% | -7.1% | -8.2% | -3.8% | -7.2% | -8.1%
Enc Time[%] | 91.0% |  |  | 86.7% |  |  | 89.6% |  | 
Dec Time[%] | 88.3% |  |  | 84.8% |  |  | 89.5% |  | 
Enc Mem[%] | 107.3% |  |  | 106.4% |  |  | 105.3% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.2% | -0.6% | -0.6% |  |  |  | -1.0% | -1.6% | -1.7%
Class B | -0.2% | -0.5% | -0.5% | -0.4% | -0.6% | -0.7% | -0.7% | -1.1% | -1.2%
Overall (EL+BL) | -0.2% | -0.6% | -0.5% | -0.4% | -0.6% | -0.7% | -0.8% | -1.2% | -1.4%
Overall (EL) | -0.4% | -1.0% | -1.0% | -0.9% | -1.2% | -1.6% | -1.3% | -2.0% | -2.2%
Enc Time[%] | 86.9% |  |  | 82.1% |  |  | 87.0% |  | 
Dec Time[%] | 87.6% |  |  | 83.0% |  |  | 87.7% |  | 
Enc Mem[%] | 108.8% |  |  | 107.7% |  |  | 106.4% |  | 
BL Match | Matched |  |  | Matched |  |  | Matched |  | 
Average gain: Y -1.03%, U -2.01%, V -2.24%

## Slide 4
Thanks