## Slide 1: Non-CE1: Square transform blocks for 4:2:2
J. Sole, R. Joshi, M. Karczewicz (Qualcomm)
A. Gabriellini, M. Mrak (BBC)

## Slide 2: Motivation
HEVC Range Extensions Core Experiment 1 tests the usage of two square transforms instead of one rectangular transform
Test 3 only replaces one rectangular transform by two square transforms (JCTVC-L0333)
  Signaling of two cbf and invoking residual coding twice
  No need for the 32-point transform in the chroma path
  No reconstruction after intra prediction as in HEVC version 1
  Intra prediction applied on rectangular blocks (intra angles modified with respect to HEVC version 1)

## Slide 3: Method 1
Based on CE1 test 3, JCTVC-L0333
Included upper square transform block reconstruction prior to the intra prediction of the lower square block
Removed the QP increase by 3 associated to the rectangular transforms
Removed the scaling lists associated to the rectangular transforms
Removed the intra prediction modification for planar modes specific for rectangular blocks
Removed the intra prediction modification for angular modes specific for rectangular blocks

## Slide 4: Method 2: intra angle clip
Like method 1, but keeping the rectangular intra agnular prediction
Since the intra prediction reference array size depends on the block size, largest angles get out of boundary
Proposal: clip intra angle values to 32
Luma Block
Hor Intra Pred
IntraPredAngle=21
IntraPredAngle=42
Chroma 4:2:2 Block Hor Intra Pred
Chroma 4:2:2 Square Blocks Hor Intra Pred
No Clipping With Clipping
IntraPredAngle=42
IntraPredAngle=32

## Slide 5: Performance
Method 1 | Main Tier |  |  | High Tier |  | 
 | Y | U | V | Y | U | V
All Intra HE | 0.8% | 3.6% | 5.0% | 0.6% | 1.9% | 2.3%
Random Acc HE | 0.4% | 4.5% | 5.6% | 0.3% | 2.4% | 3.6%
Low Delay B HE | 0.2% | 4.0% | 5.0% | 0.0% | 2.3% | 3.4%
Method 2 | Main Tier |  |  | High Tier |  | 
 | Y | U | V | Y | U | V
All Intra HE | 0.2% | 2.9% | 4.3% | 0.1% | 1.5% | 1.9%
Random Acc HE | 0.2% | 3.8% | 5.0% | 0.0% | 2.1% | 3.3%
Low Delay B HE | 0.0% | 3.5% | 4.6% | -0.1% | 2.2% | 3.2%
BD-rate using HEVC range extensions common conditions

## Slide 6
Method 2 vs Method 1 | Main Tier |  |  | High Tier |  | 
 | Y | U | V | Y | U | V
All Intra HE | -0.6% | -0.6% | -0.7% | -0.5% | -0.4% | -0.4%
Random Acc HE | -0.3% | -0.6% | -0.5% | -0.2% | -0.3% | -0.3%
Low Delay B HE | -0.1% | -0.5% | -0.4% | -0.1% | -0.2% | -0.2%
Method 1 vs L0331 | Main Tier |  |  | High Tier |  | 
 | Y | U | V | Y | U | V
All Intra HE | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1%
Random Acc HE | 0.0% | 0.2% | 0.2% | 0.0% | 0.0% | 0.1%
Low Delay B HE | 0.0% | 0.3% | 0.3% | 0.0% | 0.0% | 0.1%
JCTVC-L0333 (CE1 test 3) replaces rectangular transform by two square transforms
Performance

## Slide 7: Conclusions
Luma BD-rate reflects changes in bit-rate; in average that is 0.1%, 0.0% and -0.1% for AI, RA and LD, respectively
Chroma BD-rate reflects changes in PSNR for chroma
  Average 0.06 dB for each component, compared to non-square anchors
This contribution shows the best results using square transforms in 4:2:2 chroma format