## Slide 1: AHG7: In-loop color-space transformation of residual signals for range extensions
K. Kawamura, T. Yoshino, S. Naito
KDDI Corp. (KDDI R&D Labs. Inc.)

## Slide 2: Overview
Additional coding tool for only 4:4:4 format
  Reduce colour space redundancy for each CU
  Target is residual signals of intra/inter pred.
  No additional syntax and No coding structure change
  YUV BD-rate 14.3%/14.6%/13.4% (AI/RA/LD) for average of YUV and RBG 4:4:4
Recommend to adopt the proposal to HM-RExt

## Slide 3: Motivation & Solution
Motivation
  Reduce inter-plane redundancy
Proposed solution: in-loop ACST
  Three planes are transformed into that in no correlated space.
  Prediction error signals are transformed.
  Transform matrix is based on singular-value-decomposition for each CU.

## Slide 4: Proposed architecture
Intra Prediction
Inter Prediction
Color space transform.
FDCT/FDST
Q
IQ
IDCT/IDST
Color space inverse transform.
In-loop filters
Frame buffer
Local decoded image
Original image
Matrix derivation

## Slide 5: Colour space transform
Forward transform
Inverse transform

## Slide 6: Matrix derivation –reference–
Intra block case
  Coded pixels
Inter block case
  Reference blocks of MC
Target block
Reference
pixels
Reference
frame
Target frame
Reference
block
Target
block

## Slide 7: Matrix derivation –algorithm–
Covariance matrix
  Average is subtracted for each plane
  For example, [3x32][32x3]t=[3x3]
Simplified singular-value-decomposition
  Algorithm: Jacobi method
  Arithmetic: Integer multiplication and shift operation only

## Slide 8: Experimental Results
Implemented on HM9.0-Rext

## Slide 9: Conclusion
Additional coding tool for only 4:4:4 format
  YUV BD-rate 14.3%/14.6%/13.4% (AI/RA/LD) for average of YUV and RBG 4:4:4
  Inter frame can provide coding grain.
  Additional decoding runtime is practical.
Recommend to adopt the proposal to HM-RExt