## Slide 1: Supporting document for CANNB comments on the Frame packing arrangement SEI message
Comment provided as part of the vote on HEVC - m27994

## Slide 2: CANNB comment
It is our understanding that the frame_packing_arrangement_type equal to 7, corresponding to figure D12 as inherited from AVC, is needlessly complicated in HEVC. The use case is to permit carriage of side-by-side non-sub-sampled 3D pictures in 720p, as inherited from AVC. The current HEVC specification does not require fancy decompositions and permits a side-by-side full frame 720p sequence. As such, the extra complexity is redundant with the current core specification and not required for a system that contains this feature from the outset.

## Slide 3: FPA type 7

## Slide 4: When can a level support a type-7 FPA but not two side-by-side non-subsampled views?
A picture size for a level is allowed when:
  PicSizeInSamplesY = pic_width_in_luma_samples * pic_height_in_chroma_samples
  PicSizeInSamplesY <= MaxLumaPS
  pic_width_in_luma_samples <= Sqrt( MaxLumaPS * 8 )
  pic_height_in_luma_samples <= Sqrt( MaxLumaPS * 8 )
Assuming a 2D picture of size width * height,
  A 3D type-7 FPA is allowed when:
    2 * width * height < MaxLumaPS
  A side-by-side arrangement (which has the same PicSizeInSamplesY as the type-7 case) is not allowed when:
    2 * width > Sqrt( MaxLumaPS * 8 )
Therefore, the problem occurs when both of these conditions are true.

## Slide 5: Result: it never happens
Level: |  |  |  |  | 1 | 2 | 2.1 | 3 | 3.1 | 4 | 4.1 | 5 | 5.1 | 5.2 | 6 | 6.1 | 6.2
Max luma picture size (samples): |  |  |  |  | 36864 | 122880 | 245760 | 552960 | 983040 | 2228224 | 2228224 | 8912896 | 8912896 | 8912896 | 35651584 | 35651584 | 35651584
Max luma sample rate (samples/sec) |  |  |  |  | 552960 | 3686400 | 7372800 | 16588800 | 33177600 | 66846720 | 133693440 | 267386880 | 534773760 | 1069547520 | 1069547520 | 2139095040 | 4278190080
Sqrt( MaxLumaPS * 8 ) |  |  |  |  | 543.1 | 991.5 | 1402.2 | 2103.3 | 2804.3 | 4222.1 | 4222.1 | 8444.1 | 8444.1 | 8444.1 | 16888.2 | 16888.2 | 16888.2
Format nickname |  | Luma width | Luma height | Luma picture size |  |  |  |  |  |  |  |  |  |  |  |  | 
SQCIF |  | 128 | 96 | 16384 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QCIF |  | 176 | 144 | 36864 | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QVGA |  | 320 | 240 | 81920 | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
525 SIF |  | 352 | 240 | 98304 | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CIF |  | 352 | 288 | 122880 | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
525 HHR |  | 352 | 480 | 196608 | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
625 HHR |  | 352 | 576 | 221184 | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Q720p |  | 640 | 360 | 245760 | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
VGA |  | 640 | 480 | 327680 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
525 4SIF |  | 704 | 480 | 360448 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
525 SD |  | 720 | 480 | 393216 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4CIF |  | 704 | 576 | 405504 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
625 SD |  | 720 | 576 | 442368 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
480p (16:9) |  | 864 | 480 | 458752 | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
SVGA |  | 800 | 600 | 532480 | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
QHD |  | 960 | 540 | 552960 | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
XGA |  | 1024 | 768 | 786432 | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
720p HD |  | 1280 | 720 | 983040 | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
4VGA |  | 1280 | 960 | 1228800 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
SXGA |  | 1280 | 1024 | 1310720 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
525 16SIF |  | 1408 | 960 | 1351680 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
16CIF |  | 1408 | 1152 | 1622016 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
4SVGA |  | 1600 | 1200 | 1945600 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
1080 HD |  | 1920 | 1080 | 2088960 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
2Kx1K |  | 2048 | 1024 | 2097152 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
2Kx1080 |  | 2048 | 1080 | 2228224 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
4XGA |  | 2048 | 1536 | 3145728 | - | - | - | - | - | - | - | 0 | 0 | 0 | 0 | 0 | 0
16VGA |  | 2560 | 1920 | 4915200 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
3616x1536 (2.35:1) |  | 3616 | 1536 | 5603328 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
3672x1536 (2.39:1) |  | 3680 | 1536 | 5701632 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
3840x2160 (4*HD) |  | 3840 | 2160 | 8355840 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
4Kx2K |  | 4096 | 2048 | 8388608 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
4096x2160 |  | 4096 | 2160 | 8912896 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
4096x2304 (16:9) |  | 4096 | 2304 | 9437184 | - | - | - | - | - | - | - | - | - | - | 0 | 0 | 0
7680x4320 |  | 7680 | 4320 | 33423360 | - | - | - | - | - | - | - | - | - | - | - | - | -
8192x4096 |  | 8192 | 4096 | 33554432 | - | - | - | - | - | - | - | - | - | - | - | - | -
8192x4320 |  | 8192 | 4320 | 35651584 | - | - | - | - | - | - | - | - | - | - | - | - | -

## Slide 6: Proposal
simplify the definition of frame_packing_arrangement_type equal to 7, such that there are only two regions of equal size, or
remove the definition of frame_packing_arrangement_type equal to 7 from the HEVC specification and provide a flag that specifies if up-sampling is required for display of unpacked frames using frame_packing_arrangement_type 0—4 inclusive.

## Slide 7: The issue
Document K382-v2 was agreed in Shanghai meeting with some related decision on display/crop window. It reflects the JCT-VC agreement on the FPA.
  FPA type 1 to 5
SoDIS version 10 and further versions contains document K382-v2 but also contains additional types of FPA (6 and 7) that correspond to the latest AVC profiles and SEI amd (which is not ratified).
Those AVC SEIs were under ballot (DAM1) when the DIS was issued; and remain waiting for final FDAM approval
They were not part of the DIS.
They were not proposed nor agreed in HEVC
JCT-VC experts and NB had no chance to discuss, and little to review them.
The CANNB believes that at least one of those new types is not relevant in HEVC.
It was further pointed out at this meeting that one of those type is not working properly with the cropping/display window.

## Slide 8: FPA types 0 to 2 and cropping window

## Slide 9: The proposal
Fix type 0 to 2
Evaluate the CANNB comment on profile constraints (next slide)

## Slide 10: CANNB comment on profile constraints.
As a specification is under development for 3D HEVC, it seems desirable to constrain the values of the Frame packing arrangement in the main profile and main 10 profile. It would be beneficial that product implementing the HEVC 3D specification rather than a hook specified as an SEI message above the current HEVC specification.
It is proposed that the frame_packing_arrangement_type values would be limited to [5], [simplified 7 as per “comment 2 on Frame packing SEI message”], [modified 3, modified 4 as per “comment 2 on Frame packing SEI message”] in the main and main 10 profiles