## Slide 1
On secondary transforms for Intra_BL
residue
JCTVC-M0033
Ankur Saxena and Felix Fernandes
Samsung Electronics, Co. Ltd.
Dallas R & D Research Center

## Slide 2: Motivation and Prior Work
DCT is not necessarily the optimal transform for Intra_BL residue
Prior Work :
L. Guo, M. Karczewicz, J. Sole, and J. Chen, JCTVC-K0321
L. Guo, M. Karczewicz, and J. Chen, JCTVC-L0330
  Full size 8x8, 16x16 and 32x32 additional transforms were proposed there.
  Gains of around 1.7% and 1.5% were obtained for AI 2x and AI 1.5x scenario.
Since additional transforms are expensive to implement at larger sizes, e.g., 32x32, we propose to use secondary transforms.

## Slide 3: Overview (1)
Currently in SHM 1.0,
  For Luma Intra_BL 4x4 Residue: DST is used.
  For 8x8 and larger Luma Intra_BL residue, DCT is used
Proposal: Apply 8x8 secondary transform to low-frequency DCT coefficients for Intra_BL residue at TU size 8x8 and larger (Luma only)
  No changes to Chroma and 4x4 Intra_BL TU’s
  Gains of 1.4 % and 0.9 % obtained for AI 2x and AI 1.5x scenarios.
Trigger Conditions
Decoder Operations
Inverse DCT
Inverse Quantizer
Inverse Secondary Transform
TU >=8 ; Mode == Intra_BL ; Text_Luma;
and useSecTransFlag ==1
Inverse DCT
Inverse Quantizer

## Slide 4: Overview (2)
Fast factorization/implementation of secondary transforms also proposed.
  Proposed 8x8 Secondary Transform requires 22 mults and 58 adds
  Note : A full 8x8 transform implementation via matrix multiplication requires 64 mults and 56 adds.
  A low-complexity ROTation transform requiring only 20 mults and 12 adds is also presented.

## Slide 5: Improvements over secondary transforms proposed for HEVC
Fast implementation of secondary transforms
  Only 22 mults as compared to 64 mults for full 8x8 matrix multiplication.
  Low complexity secondary transform can even have 15 mults
In HEVC, gains were around 0.7 %. Gains now are upto 1.4 % for (EL+BL)
In HEVC, the smaller blocks were providing more gains: e.g., 8x8.
In S-HEVC, in EL the larger blocks, e.g., 32x32 are providing larger gains
  So we can avoid applying secondary transform on 8x8 blocks (worst-case), and still get most of the gains.

## Slide 6: Different Tests
Case 1: At CU level, perform a R-D search to choose between:
(a) DCT
(b) DCT + Secondary Transform 1
Case 2: At CU level, perform a R-D search to choose between:
(a) DCT
(b) DCT + Secondary Transform 1
(c) DCT + Secondary Transform 2
Transmit a flag for transform choice per CU.

## Slide 7: Algorithm Description: Decoder
Trigger Conditions
Decoder Operations
Inverse DCT
Inverse Quantizer
Inverse Secondary Transform
TU >=8 ; Mode == Intra_BL ; Text_Luma;
and useSecTransFlag ==1
Inverse DCT
Inverse Quantizer

## Slide 8: Secondary Transform Matrices
Secondary Transform matrices.
The two matrices differ in sign change for a few coefficients only.
Fast factorization with 22 mults and 58 adds as compared to 64 mults, and 56 adds for 8x8 matrix multiplication
1st Secondary Transform Matrix
2nd Secondary Transform Matrix
120 | 39 | -20 | -4 | -9 | -4 | -4 | -2
-33 | 114 | 37 | -29 | -1 | -11 | -2 | -3
26 | -26 | 116 | 22 | -33 | -2 | -10 | -1
-9 | 29 | -14 | 119 | 4 | -33 | -2 | -7
14 | -6 | 27 | -3 | 120 | -15 | -30 | -3
-1 | 16 | 0 | 26 | 8 | 118 | -33 | -22
8 | 2 | 14 | 6 | 26 | 20 | 114 | -45
4 | 9 | 7 | 13 | 14 | 27 | 36 | 118
120 | -39 | -20 | 4 | -9 | 4 | -4 | 2
33 | 114 | -37 | -29 | 1 | -11 | 2 | -3
26 | 26 | 116 | -22 | -33 | 2 | -10 | 1
9 | 29 | 14 | 119 | -4 | -33 | 2 | -7
14 | 6 | 27 | 3 | 120 | 15 | -30 | 3
1 | 16 | 0 | 26 | -8 | 118 | 33 | -22
8 | -2 | 14 | -6 | 26 | -20 | 114 | 45
-4 | 9 | -7 | 13 | -14 | 27 | -36 | 118

## Slide 9: Low-complexity Secondary Transform ROT Matrix
Sparse matrix. Implementation in 20 mults and 12 adds
The second secondary matrix is simply the transpose of ROT matrix above
Operations can be further reduced via lifting implementations (JCTVC-C096, JCTVC-G304) to 15 mults.
87 | -93 | 12 | 0 | 0 | 0 | 0 | 0
91 | 79 | -44 | 0 | 0 | 0 | 0 | 0
25 | 38 | 120 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 118 | -50 | -5 | 0 | 0
0 | 0 | 0 | -50 | -118 | -13 | 0 | 0
0 | 0 | 0 | 1 | 14 | -128 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 128 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 128

## Slide 10: Summary of Results
Test Number | # of secondary Transforms tested | Type of Secondary Transform | TU sizes on which secondary transform applied | AI 2x Y | AI 1.5x Y | Average Luma gain | Average Encoding Time | Average Decoding Time
1 | 1 | SecTrans | 8 to 32 | -1.0% | -0.6% | -0.8% | 112% | 103%
2 | 2 | SecTrans | 8 to 32 | -1.4% | -0.9% | -1.2% | 125% | 104%
3 | 1 | ROT | 8 to 32 | -0.8% | -0.4% | -0.6% | 111% | 101%
4 | 2 | ROT and Transpose | 8 to 32 | -1.1% | -0.6% | -0.9% | 124% | 102%
Thanks to Qualcomm for cross-checking the proposal in JCTVC-M0307.
Additional encoding complexity (times) can be halved by using a fast search as in JCTVC-L0330.

## Slide 11: Complexity: Operation Counts
 |  |  |  |  | Worst Case | Worst Case | Average Case | Average Case
 |  | Operations for 2-d DCT | Proposed Sec Trans | Proposed ROT | % increase for Sec Trans | % increase for ROT | % increase for Sec Trans | % increase for ROT
TU Size |  | SHM 1.0 DCT |  |  |  |  |  | 
4x4 | Mults | 48 | N/A | N/A | N/A | N/A | N/A | N/A
 | Adds | 96 | N/A | N/A | N/A | N/A | N/A | N/A
8x8 | Mults | 352 | 352 | 320 | 100% | 91% | 50% | 45%
 | Adds | 576 | 928 | 192 | 161% | 33% | 81% | 17%
16x16 | Mults | 2752 | 352 | 320 | 13% | 12% | 6% | 6%
 | Adds | 3712 | 928 | 192 | 25% | 5% | 13% | 3%
32x32 | Mults | 21888 | 352 | 320 | 2% | 1% | 1% | 1%
 | Adds | 25856 | 928 | 192 | 4% | 1% | 2% | 0%

## Slide 12: Summary of Results (2)
Test Number | # of secondary Transforms tested | Type of Secondary Transform | TU sizes on which secondary transform applied | AI 2x Y | AI 1.5x Y | Average Luma gain | Average Encoding Time | Average Decoding Time
1 | 1 | SecTrans | 8 to 32 | -1.0% | -0.6% | -0.8% | 112% | 103%
2 | 2 | SecTrans | 8 to 32 | -1.4% | -0.9% | -1.2% | 125% | 104%
3 | 1 | ROT | 8 to 32 | -0.8% | -0.4% | -0.6% | 111% | 101%
4 | 2 | ROT and Transpose | 8 to 32 | -1.1% | -0.6% | -0.9% | 124% | 102%
5 | 2 | SecTrans | 16 and 32 | -0.9% | -0.5% | -0.7% | 123% | 102%
6 | 2 | ROT | 16 and 32 | -0.8% | -0.4% | -0.6% | 123% | 102%
Additional encoding complexity (times) can be halved by using a fast search as in JCTVC-L0330.
Notes: Additional encoding complexity (times) can be further reduced to half by using a fast search as in JCTVC-L0330.

## Slide 13: Conclusions
Proposed secondary transform provides upto 1.4 % and 0.9 % gain for All Intra 2x and 1.5x cases respectively.
Presented fast factorization for secondary transforms.
Additional decoding complexity is marginal.
Recommend to adopt proposed secondary transform, or test in a Core Experiment for Transforms/Intra_BL residue.

## Slide 14
Back-Up

## Slide 15: Derivation of the Secondary Transform Matrices
No training to derive the secondary transforms
In JCTVC-L0330, it was proposed to choose between
DCT Type-2 (C2)
DCT Type-3 (C3)
DST Type-3 (S3)
Derivation for secondary transform (size 8x8):
C3 = C2 * (C2 ) T * C3
= C2 * M
(DCT followed by secondary transform M)
ROTation transform was obtained for Intra residues even before HEVC CfP.

## Slide 16: Results forJCTVC-L0330 and this Proposal
Test Number | # of Transforms tested | Type of Transform | AI 2x Y | AI 1.5x Y | Average Luma gain | Average Encoding Time | Average Decoding Time
M-0033 | 1 | SecTrans | -1.0% | -0.6% | -0.8% | 112% | 103%
M-0033 | 2 | SecTrans | -1.4% | -0.9% | -1.2% | 125% | 104%
L-0030 | 1 | Full-Size Trans | -1.1% | -1.0% | -1.0% | 105% | 99%
L-0030 | 2 | Full-Size Trans | -1.7% | -1.5% | -1.6% | 110% | 99%