## Slide 1: JCTVC-M0040: AHG9: Using SHVC for adaptive resolution change and efficient trick mode
K. Ugur, H. Lavasani, M. M. Hannuksela
Nokia

## Slide 2: Summary
Adaptive Resolution Change (ARC): Dynamically changing the resolution within the video sequence without using IDR pictures.
  ARC was earlier proposed for HEVC v1, but functionality was not included, mostly due to the need to include “resampling” process in v1.
Efficient trick mode: For trick mode, using downsampled pictures, instead of IRAP pictures of the main video track to have low bitrate trick mode. IRAP pictures of EL can be predicted from low-resolution trick mode pictures for improved coding efficiency.
SHVC inherently supports resolution change and inter-layer prediction, it can effectively support ARC and trick mode use-cases with small high-level changes.
Proposal:
We propose sequence level indications for SHVC to indicate above operations for SHVC.
  This was first proposed at the Geneva meeting (JCTVC-L0119) but was requested to evaluate after the WD text was available.

## Slide 3: ARC - Background
Benefits of ARC (JCTVC-F158)
Better network adaptation and error resilience: For better adaptation to changing network requirements for different content, it is desired to be able to change both the temporal / spatial resolution in addition to quality.
Fast start: The start-up time of the session could be increased by first sending a low resolution frame and then increasing the resolution.
  More important in HEVC due to intra frames taking relatively higher bitrate compared to earlier standards
Conference compose: When the person starts speaking, his/her corresponding resolution is increased. Doing this with an IDR frame causes a “blip” in the quality as IDR frames need to be coded at a relatively low quality so the delay is not increased.
BL0-BL1-BL2-BL3-EL3-EL4

## Slide 4: ARC
Illustration of how ARC reduces the bitrate compared to using IDR picture
Complete results in the contribution and in JCTVC-L0119

## Slide 5: Efficient trick mode
Coding efficiency of HEVC is improved more for P- and B- pictures compared to that of I- pictures.
It was argued earlier that this phenomenon poses a problem for streaming trick mode pictures as the bitrate for trick mode will be relatively higher in HEVC compared to that of earlier standards.
  JCTVC-J0293 indicated that one way to solve this problem is “Explore a simplified SVC extension of HEVC where the layers below the top layer consist only of occasional lower-resolution I-frames, while the main bitstream contains a near-constant sequence of P and B-frames at full resolution”.

## Slide 6
...
...
0
1
2
3
4
5
6
7
8
TR0
TR4
TR8
...
...
0
1
2
3
4
5
6
7
8
...
...
0
1
2
3
4
5
6
7
8
TR0
TR4
TR8
Trick mode pictures (red) are the IRAP pictures of the video track
Trick mode pictures (red) are downsampled pictures of the video track
Trick mode pictures (red) are downsampled pictures of the video track. The IRAP pictures of EL can utilize the trick mode pictures

## Slide 7: Proposal
We propose the following high level feature so that SHVC could be used with the use-cases described above:
  A coded video sequence constrained to perform the ARC operation is signaled in VPS (single_layer_for_non_irap_flag), specifically indicating:
    except for IRAP pictures in enhancement layer, each AU in the sequence contains a single picture from a single layer (which may or may not be BL picture)
    Access units containing IRAP picture of EL include pictures from two layers and inter-layer scalability tools may be used.
The motivation for this flag
  Decoder need not to perform multi-loop for decoding the bitstream.
  Decoder becomes aware that the base layer might not be present for all access units (and hence not decode the bitstream if it cannot decode the EL resolution)

## Slide 8: Spec. text
vps_extension( ) { | Descriptor
… | 
single_layer_for_non_irap_flag | u(1)
} | 
single_layer_for_non_irap_flag equal to 1 indicates either that all the VCL NAL units of an access unit have the same nuh_layer_id value or that two nuh_layer_id values are used by the VCL NAL units of an access unit and the picture with the greater nuh_layer_id value is an IRAP picture. single_layer_for_non_irap_flag equal to 0 indicates that nuh_layer_id values may or may not be constrained beyond constraints specified in other parts of this Recommendation | International Standard.

## Slide 9: Conclusion
SHVC inherently supports inter-layer prediction and resolution change
  ARC and efficient trick mode comes for free.
We proposed high level flag so SHVC could be used for these use-cases.