## Slide 1: SCE4.2.5: Switchable De-ringing Filter for Inter-layer Prediction (JCTVC – M0055)
Z. Ma, F. Fernandes
Samsung Electronics

## Slide 2: Motivation
Ringing artifacts occur due to
  Re-sampling error
  Quantization error
Proposed solution: reduce the ringing artifacts so as to improve the up-sampled base layer reconstruction and inter-layer coding efficiency

## Slide 3: Proposal
3x3 based 2D Switchable De-ringing filter for intraBL
2x | W_luma_2x = {{w(-4), w(-3), w(-2)}, {{ 3, 4, 3 }, {w(-1), w( 0), w( 1)}, = { 4, 5, 4 }, {w( 2), w( 3), w( 4)}} { 3, 4, 3 }}
1.5x/SNR | W_luma_15x = {{w(-4), w(-3), w(-2)}, {{ 1, 2, 1 }, {w(-1), w( 0), w( 1)}, = { 2, 8, 2 }, {w( 2), w( 3), w( 4)}} { 1, 2, 1 }}
g[65] = { 32, 30, 27, 22, 16, 11, 7, 4, 2, 1,
0, 0 0, 0, … … , 0 };

## Slide 4: CU level switchable de-ringing filter (SDRF)
A new flag drfFlag is introduced
  When the block is coded using intraBL or intraBL skip, this drfFlag is encoded to indicate whether this block is using upsampled BL or filtered up-sampled BL.

## Slide 5: Division implementation using LUT
A = 1 << 16
A/Wd as the LUT (initial design with 897 entries for 2x, and 385 entries for 1.5x)

## Slide 6: Experimental Results (DIV)
Anchor SHM1.0
Thanks for the cross-check from MediaTek
AI 2x |  |  | AI 1.5x |  | 
-1.0% | -1.5% | -1.6% | -0.3% | -0.7% | -0.7%
RA 2x |  |  | RA 1.5x |  |  | RA SNR |  | 
-0.9% | -0.8% | -0.8% | -0.2% | -0.3% | -0.2% | -0.5% | -0.5% | -0.3%
LDP 2x |  |  | LDP 1.5x |  |  | LDP SNR |  | 
-1.1% | -1.3% | -1.3% | -0.6% | -0.7% | -0.7% | -0.9% | -1.0% | -0.8%
LD 2x |  |  | LD 1.5x |  |  | LD SNR |  | 
-1.1% | -1.3% | -1.3% | -0.6% | -0.7% | -0.7% | -0.9% | -1.0% | -0.8%

## Slide 7: Experimental Results (LUT)
Anchor SHM1.0
Thanks for the cross-check from MediaTek
AI 2x |  |  | AI 1.5x |  | 
-0.7% | -0.8% | -0.9% | -0.2% | -0.6% | -1.0%
RA 2x |  |  | RA 1.5x |  |  | RA SNR |  | 
-0.7% | -0.2% | -0.4% | -0.1% | -0.4% | -0.7% | -0.4% | -0.6% | -1.1%
LDP 2x |  |  | LDP 1.5x |  |  | LDP SNR |  | 
-0.9% | -0.7% | -0.9% | -0.4% | -0.8% | -0.8% | -0.7% | -0.9% | -1.2%
LD 2x |  |  | LD 1.5x |  |  | LD SNR |  | 
-0.6% | -0.5% | -0.7% | -0.1% | -0.5% | -0.5% | -0.4% | -0.7% | -1.0%

## Slide 8: Complexity Measurement

## Slide 9: Conclusion
SDRF with division provides average gain of -0.7%, -0.8%, -0.8% (Y/U/V)
SDRF with LUT provides average gain of -0.5% -0.6% -0.8% (Y/U/V)
We recommend adoption of SDRF.