## Slide 1: Non-SCE3: Inter-layer residual prediction with motion prediction
Wenhao Zhang, Zhipin Deng Yi-jen Chiu
Intel Corporation
JCTVC-M0062

## Slide 2: Introduction
  A H.264/SVC-like inter-layer residual prediction for SHVC
  Features:
    inter-layer residual prediction + inter-layer motion prediction
    Bilinear filter is used to upsample BL residual
    Only apply to inter 2Nx2N PUs of EL.
    No new syntax is introduced.
  Compared to SHM1.0, it provides 0.94% BD-rate gain on average for RA/LD-P/LD-B cases, with marginal increase of runtime and implementation complexity.
  Thanks Huawei to crosschecking in JCTVC-M0319.

## Slide 3: Algorithm
  Encoder
    ResEL = OrigEL – PredEL – UP{Res’BL}
    ResEL: input of trans./quant. of EL
    OrigEL: original video of EL
    PredEL: inter predicted signal of EL
    UP{Res’BL}: reconstructed residual signal of the collocated BL, which is upsampled by bilinear filter
Encoder diagram

## Slide 4: Algorithm
  Decoder
    RecEL = Res’EL + PredEL + UP{Res’BL}
    Res’EL: reconstructed residual of EL
    PredEL: inter predicted signal of EL
    UP{Res’BL}: reconstructed residual signal of the collocated BL, which is upsampled by bilinear filter
Decoder diagram

## Slide 5: Algorithm
  Bound IL residual pred and IL motion pred together
    Consistent motion = higher cross-layer correlation for residual
  For a EL PU, if the BL merge candidate is used, inter-layer residual prediction is applied
Bool bInterLayerResidualPred = merge_flag && merge_idx == 0 && bAvailMotionBL; if ( bInterLayerResidualPred ) { performInterLayerResidualPred(); }

## Slide 6: Simulation results (vs. SHM1.0)
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.8% | -0.8% |  |  |  | -0.4% | -1.0% | -1.2%
Class B | -0.7% | -1.4% | -1.8% | -0.9% | -1.8% | -2.2% | -0.8% | -1.7% | -2.2%
Overall (Test vs Ref) | -0.6% | -1.2% | -1.5% | -0.9% | -1.8% | -2.2% | -0.7% | -1.5% | -1.9%
Enc Time[%] | 99.0% |  |  | 98.3% |  |  | 99.1% |  | 
Dec Time[%] | 122.0% |  |  | 125.9% |  |  | 108.2% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.4% | -0.7% | -0.8% |  |  |  | -0.5% | -0.8% | -0.9%
Class B | -0.9% | -1.3% | -1.5% | -1.1% | -1.7% | -2.0% | -1.0% | -1.2% | -1.6%
Overall (Test vs Ref) | -0.8% | -1.1% | -1.3% | -1.1% | -1.7% | -2.0% | -0.9% | -1.1% | -1.4%
Enc Time[%] | 98.8% |  |  | 97.6% |  |  | 99.3% |  | 
Dec Time[%] | 121.0% |  |  | 128.3% |  |  | 107.0% |  | 
 | LD-B HEVC 2x |  |  | LD-B HEVC 1.5x |  |  | LD-B HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -0.6% | -1.0% | -1.1% |  |  |  | -0.7% | -1.0% | -1.2%
Class B | -1.2% | -1.8% | -2.1% | -1.5% | -2.4% | -2.6% | -1.2% | -1.7% | -2.0%
Overall (Test vs Ref) | -1.0% | -1.6% | -1.8% | -1.5% | -2.4% | -2.6% | -1.0% | -1.5% | -1.8%
Enc Time[%] | 98.4% |  |  | 96.2% |  |  | 99.3% |  | 
Dec Time[%] | 122.1% |  |  | 128.7% |  |  | 115.0% |  | 
  Average of RA/LD-P: -0.81%, 98.7%, 119.8%
  Average of RA/LD-P/LD-B: -0.94%, 98.4%, 119.8%
  If the decoder implement the upsampling at block level, the increase of decoding time will be reduced a lot.

## Slide 7: Complexity assessment
  Additional buffer is needed to store BL residual
    But it’s with BL picture size and not in reference pic buffer
  Lower memory bandwidth
    Only access residual buffer of the collocated BL block once
  Less operations
    2D separable bilinear upsampling
 | 8b/8b | 64b/256b | 64b/512b | Mults | Adds
RA | 115% | 117% | 118% | 107% | 104%
LD-P | 122% | 124% | 125% | 109% | 105%
LD-B | 116% | 118% | 119% | 107% | 104%
All | 118% | 120% | 121% | 108% | 104%
Complexity assessment

## Slide 8: Conclusion
  Visible gain is achieved among all the inter coding tests
    0.94% (EL+BL) BD-rate gain on average
  Marginal increase of implementation complexity
  Thanks Huawei to crosschecking in JCTVC-M0319.

## Slide 9: Back up