## Slide 1: JCTVC-M0086: AHG-17: complexity and performance analysis of SHM1.0 compare to HM8.1 simulcast
Elena Alshina
Alexander Alshin
Samsung Electronics, Ltd

## Slide 2: Tools in SHM1.0
IntraBL
  Inter-layer texture prediction
    enabled on CU level
  MV prediction from BL
RefIDx
  Inter-layer texture prediction
    enabled on PU level
  MV prediction from BL (MV mapping)
  Simplest combined prediction
    (IL_Pred +MCEL_Pred+1)>>1

## Slide 3: Performance comparison
Frame-work | All Intra tests |  |  |  | Test scenarios with MC (RA, LD-P) |  |  |  |  | 
 | Luma, BD-rate | Chroma, BD-rate | Enc. Time | Dec. Time | Luma, BD-rate | Chroma, BD-rate |  | Enc. Time |  | Dec. Time
IntraBL | -27,1% | -26,9% | 114% | 80% | -18,5% | -8,8% |  | 104% |  | 96%
RefIdx | -26,8% | -26,5% | 114% | 82% | -18,0% | -8,3% |  | 101% |  | 97%
difference between two |  |  |  |  |  |  |  |  |  | 
IntraBL vs RefIdx | 0,3% | 0,5% | 99% | 103% | 0,7% | 0,6% | 98% |  | 101% | 

## Slide 4: Complexity comparison
Frame-work | All Intra tests |  |  |  | Test scenarios with MC (RA, LD-P) |  |  | 
 | Pure | DDR-2 | DDR-3 | Mults | Pure | DDR-2 | DDR-3 | Mults
IntraBL | INF | INF | INF | INF | 94% | 96% | 96% | 96%
RefIdx | INF | INF | INF | INF | 93% | 94% | 94% | 97%
RefIdxPic | INF | INF | INF | INF | 134% | 117% | 116% | 149%
difference between two |  |  |  |  |  |  |  | 
IntraBL vs RefIdx | 91% | 89% | 89% | 98% | 99% | 98% | 98% | 101%
The worst case complexity vs HEVC
Memory band-width, mults / adds | 
IntraBL | 100%
RefIdx (MV = 0 for IL predicted Pus) | 100%

## Slide 5: I-slices
Only Inter-layer texture prediction is the subject for memory access evaluation
RefIdx vs IntraBL | Pure | DDR-2 | DDR-3 | Mults | #IL Precited samples
 | 91% | 89% | 89% | 98% | 87%

## Slide 6: Conclusion
In average computational complexity and memory access of SHM1.0 is 4-7% lower than for HM8.1 simulcast single layer coding, while 18% Luma BD-rate reduction is achieved in motion compensation test scenarios.
The motion vector in inter-layer predicted blocks in RefIdx framework shall be normatively restricted to be 0. This restriction guarantees the worst case memory bandwidth of SHVC will not exceed HEVC limit.
Complexity assessment by AhG17 tool shows negligible difference between IntraBL and RefIdx frameworks (1-2% in motion compensation test scenarios), while IntraBL branch outperforms RefIdx framework 0.7% in terms of Luma BD-rate (0,6% in terms of Chroma BD-rate).