## Slide 1: SCE4: De-noising filter for SNR scalability
Elena Alshina
Alexander Alshin
Samsung Electronics, Ltd

## Slide 2: SCE4: De-noising filter for SNR scalability
Test 4.1.1 | Y-BD rate | Enc Time | Dec Time | The worst case |  | Actual | 
 |  |  |  | Memory | Comp. | Memory | Comp.
vs IntraBL | -2,1% | 102% | 103% | 100% | 100% | 101% | 106%
vs RefIdx | -1,4% | 100% | 127% | 100% | 100% | 102% | 108%
*M0273 | -2,1% | 100% | 127% | 100% | 100% | 102% | 106%
5 taps
4 bits precision
2D separable filter
{ -1,3,12,3,-1}/16
CU on/off for Intra BL
Enabled for all IL predicted PUs in RefIdx

## Slide 3: Complexity assessment details
 | RA HEVC SNR |  |  | 
 | Pure | DDR-2 | DDR-3 | Mults
Class A | 102% | 100% | 100% | 106%
Class B | 101% | 100% | 100% | 103%
Overall | 101% | 100% | 100% | 104%
LD-P HEVC SNR |  |  |  | 
 | Pure | DDR-2 | DDR-3 | Mults
Class A | 104% | 101% | 101% | 112%
Class B | 103% | 101% | 101% | 107%
Overall | 103% | 101% | 101% | 109%
LD-B HEVC SNR |  |  |  | 
 | Pure | DDR-2 | DDR-3 | Mults
Class A | 102% | 100% | 100% | 107%
Class B | 101% | 100% | 100% | 103%
Overall | 101% | 100% | 100% | 104%
RA HEVC SNR |  |  |  |  | 
 | Pure |  | DDR-2 | DDR-3 | Mults
 | 102% |  | 100% | 100% | 107%
 | 102% |  | 102% | 102% | 105%
 | 102% |  | 101% | 101% | 106%
LD-P HEVC SNR |  |  |  |  | 
 | Pure |  | DDR-2 | DDR-3 | Mults
 | 103% |  | 100% | 100% | 112%
 | 104% |  | 102% | 102% | 110%
 | 103% |  | 102% | 101% | 110%
LD-B HEVC SNR |  |  |  |  | 
 |  | Pure | DDR-2 | DDR-3 | Mults
 |  | 102% | 100% | 100% | 108%
 |  | 103% | 102% | 102% | 107%
 |  | 102% | 101% | 101% | 107%
IntraBL
RefIdx
We would like to thank Inter Digital for careful and comprehensive cross-check of presented test data

## Slide 4: Up-date compare to JCTVC-L0087

## Slide 5: Conclusion
Based on test results:
Average Luma BD-rate gain:
  2.1% (IntraBL) and 1.4% (RefIdx)
Average Memory access:
  101% (IntraBL) and 102% (RefIdx)
Samsung proposes adoption of 2D separable de-noising filter into next SHVC Test Model and reference software.

## Slide 6: Fixed coefficients vs Adaptive
 | ×2 |  | ×1,5 |  | SNR | 
 | Y gain | Ch gain | Y gain | Ch gain | Y gain | Ch gain
Intra BL |  |  |  |  |  | 
8AUF | -0,35% | -0,49% | -0,46% | -0,80% | -0,21% | -0,88%
6AUF | -0,31% | -0,48% | -0,34% | -0,59% | -0,05% | -0,87%
RefIdx |  |  |  |  |  | 
8AUF | -0,33% | -0,43% | -0,42% | -0,69% | -0,23% | -0,94%
6AUF | -0,31% | -0,42% | -0,37% | -0,56% | -0,13% | -1,00%
Anchor:
SHM1.0 for x2 and x1,5  no filtering of int-pel
SCE4.1.1(IBL)/M0373(RefIDx) SNR  fixed 2D sep. filter for of int-pel, CU/PU;
Luma only
Test:
Adaptive up-sampling filter for both Luma and Chroma