## Slide 1: JCTVC-M0089: Non SCE4: simplified design of cross-color inter-layer (test 4.2.4)
Elena Alshina
Alexander Alshin
Yongjin Cho
Samsung Electronics, Ltd

## Slide 2: Cross-color inter-layer filter
List of changes:
Modification A:
S = 16 (fixed not signaled)
  helps implementation
|Q|≤1023  |Q|≤1024; Q≠0
  Q=0 is equivalent to disabling tool (duplicated functionality with slice level flag)
  Modification B:
Refer to Reconstructed Base Layer instead Up-sampled Base Layer
  Remove latency

## Slide 3: Modification A Slice header syntax
cross_color_filter_cb_flag | u(1)
if (cross_color_filter_cb _flag) { | 
cb_ cross_color _filter_ mult_abs | u(10)
for( k = 0; k < 12; k++ ) | 
cb_ cross_color _filter_coeff_plus8[k] | u(4)
if (cb_ cross_color _filter_ mult_abs){ | 
cb_ cross_color _filter_ mult_sign | u(1)
cb_ cross_color _filter_ shift | u(5)
} | 
} | 
cross_color_filter_cr_flag | u(1)
if (cross_color_filter_cr _flag) { | 
cr_ cross_color _filter_ mult_abs | u(10)
for( k = 0; k < 12; k++ ) | 
cr_ cross_color _filter_coeff_plus8[k] | u(4)
if (cr_ cross_color _filter_ mult_abs){ | 
cr_ cross_color _filter_ mult_sign | u(1)
cr_ cross_color _filter_ shift | u(5)
} | 
} | 
cross_color_filter_cb_flag | u(1)
if (cross_color_filter_cb _flag) { | 
cb_ cross_color _filter_no_zero_mult | u(11)
for( k = 0; k < 12; k++ ) | 
cb_ cross_color _filter_coeff_plus8[k] | u(4)
} | 
cross_color_filter_cr_flag | u(1)
if (cross_color_filter_cr flag) { | 
cr_ cross_color _filter_no_zero_mult | u(11)
for( k = 0; k < 12; k++ ) | 
cr_ cross_color_filter _filter_coeff_plus8[k] | u(4)
} | 
Tested in SCE4
Proposed

## Slide 4: Modification B
RecBL Y
RecBL Cr&Cb
Up-sampled Y
Up-sampled Cr&Cb
Cross-color filter
Inter Layer Texture
Prediction
***Latency
RecBL Y
RecBL Cr&Cb
Up-sampled Y
Up-sampled Cr&Cb
Cross-color filter
Inter Layer Texture
Prediction
Tested in SCE4
Proposed

## Slide 5: Performance summary
Tool | All Luma | All Chroma | AI Luma | AI Chroma | MC Luma | MC Chroma | SNR Luma | SNR Chroma
RefIdx framework |  |  |  |  |  |  |  | 
SCE4 4.2.4 v1 | -0,40% | -8,14% | -0,79% | -8,31% | -0,25% | -8,73% | -0,28% | -6,79%
Modification A | -0,39% | -7,80% | -0,76% | -7,84% | -0,26% | -8,29% | -0,29% | -6,77%
Modification A&B | -0,32% | -6,57% | -0,61% | -6,02% | -0,19% | -6,75% | -0,29% | -6,77%
Modification A&B | -0,41% | -8,00% | -0,80% | -8,02% | -0,28% | -8,60% | -0,29% | -6,77%
Complexity assessment for both SCE4 4.2.4 v1, Modification A and Modification A&B results in same numbers in average
Thanks million times to the cross-checker for bug fix provided!

## Slide 6: Conclusion
Based on show results:
  0,4% average Luma BD-rate gain
  8,0% (RefIdx) average Chroma BD-rate gain
  No latency on decoder side
  Inter-layer texture prediction can be done for Luma and Chroma in parallel
  Constant de-scaling shift
  Simplified compare to original version syntax in slice-header
Samsung suggests adoption of cross-color inter-layer filter to the next version for SHVC test model with proposed simplifications A&B.