## Slide 1: JCTVC-M0090: Low-pass filter for Combined Inter Prediction
Alexander Alshin
Elena Alshina
Samsung Electronics, Ltd

## Slide 2: Inter-layer texture prediction
Original signal Inter layer texture prediction

## Slide 3: Combined prediction
SCE3, tests 3.1 or 3.2
  ComibedPredEL=(PredBL+ PredEL +1)>>1
Proposed
  ComibedPredEL =clip(( PredBL+ PredEL
  +Â·[PredBL - PredEL] +1)>>1 )
  ComibedPredEL =( (I+ Â)·[PredBL] + (I- Â)·[PredEL] +1)>>1
  Â·[ ] - 2D separable low-pass 5-taps filter:
  { 11, 13, 16, 13, 11}/64

## Slide 4: Combined predictions

## Slide 5: Performance summary
Test | Luma, BD-rate | Chroma, BD-rate | EncTime | DecTime
SCE3 test3.2 | -1,24% | -5,16% | 114% | 100%
M0090 (full) | -1,74% | -7,93% | 115% | 102%
Test | Luma, BD-rate | Chroma, BD-rate | EncTime | DecTime
M0092 | -0,95% | -3,95% | 103% | 101%
M0090 | -1,50% | -6,88% | 103% | 101%
Full version
Restricted to have the worst case memory band-width within HEVC limit

## Slide 6: The worst case memory vs HEVC
Test | Memory Band-Width
Semi-sum | 133%
Proposed | 133%
Only 2Nx2N CUs use Combination | 133%
+ Combination with bi-pred is dis-allowed for 8x8 | 100%
Average memory access
Test | PureMemory | DDR2 | DDR3 | Mults
SCE_test3.2 | 106% | 105% | 105% | 106%
Proposed | 110% | 108% | 108% | 113%
Only 2Nx2N | 109% | 107% | 108% | 113%
No combination with 8x8 bi-pred | 108% | 106% | 106% | 112%

## Slide 7: Conclusion
Based on presented test results
1,50% average Luma BD-rate gain in SHM1.0
6,88% average Chroma BD-rate gain in SHM1.0
Only 3% Encoding time increment
The worst case memory access within HEVC limit
Only 6-8% average memory band-width increment compare to SHM1.0
No additional reference frame access (such as GRP-like tools)
Samsung suggests adoption of proposed combined prediction into the next version of SHVC test model. Restriction of combined prediction for 2Nx2N Inter CUs only and disallowing combination with bi-pred in smallest CUs guarantees the worst case memory band-width within HEVC limit.