## Slide 1: JCTVC-M0091: Non SCE1-Combined Intra Prediction with low-pass filter
Alexander Alshin
Elena Alshina
Samsung Electronics, Ltd

## Slide 2: Inter-layer texture prediction
Inter layer texture prediction Original signal

## Slide 3: Combined prediction
SCE1, tests 1.1
  ComibedPredEL=PredEL +deltaDC
Proposed
  ComibedPredEL =clip((PredEL +Â·[PredBL - PredEL] ) )
  ComibedPredEL = Â·[PredBL] + (I- Â)·[PredEL]
  Â·[ ] - 2D separable low-pass 5-taps filter:
  { 11, 13, 16, 13, 11}/64

## Slide 4: Performance summary
JCTVC-M0031 (DC correction)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0,5% | -1,3% | -1,2% |  |  | 
Class B | -0,6% | -2,0% | -2,1% | -0,2% | -0,8% | -0,8%
Overall (Test vs Ref) | -0,6% | -1,8% | -1,8% | -0,2% | -0,8% | -0,8%
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0,1% | -0,1% | 0,0% |  |  | 
Class B | -0,2% | -0,1% | -0,2% | -0,1% | 0,0% | -0,1%
Overall (Test vs Ref) | -0,2% | -0,1% | -0,1% | -0,1% | 0,0% | -0,1%

## Slide 5: Conclusion
Based on presented test results
0,4% average Intra Luma BD-rate gain in SHM1.0