## Slide 1: JCTVC-M0096 AHG 9: On enhancement layer CRA
The 13th JCT-VC Meeting
LG Electronics

## Slide 2: Outline
On enhancement layer CRA NAL unit type
  Inter layer prediction is allowed, while inter prediction is disallowed
  CRA NAL units need not be aligned across layer. It means to allow different random access point period across layer when using CRA NAL unit
There might be an issue with random access scenario
  When a CRA picture in higher layer has non-IRAP collocated lower layer picture.
  Non-IRAP collocated picture can use inter prediction.
Proposal: two options are offered to fix this issue.
  Option 1:: Don not allow inter-layer prediction for the CRA and pictures that follow it in decoding order until the picture with collocated IRAP.
  Option 2: Don not allow inter-layer texture prediction but allow inter-layer syntax prediction for the CRA and pictures that follow it in decoding order until the picture with collocated IRAP.

## Slide 3: Problem at non-aligned CRA
picture ‘B’ can use inter-layer prediction but not inter prediction. Therefore, picture ‘B’ can refer to picture ‘b’ in the lower layer.
  However, since picture ‘b’ is not an IRAP, it may refer to other picture, to picture ‘a’ for example.
  In such situation, random access will not work at picture ‘B’ since picture ‘a’ may not be available.
CRA
X
O
B
b
a

## Slide 4: Problem at non-aligned CRA
Any picture following CRA that has corresponding collocated non-IRAP are not safe to use ILP
CRA
Non-IRAP

## Slide 5: Options for solution
Option 1
  When CRA picture has collocated non-IRAP, inter-layer prediction shall not be allowed for the CRA picture and any pictures following it in decoding order until the picture that has collocated IRAP.
CRA
Non-IRAP
x
x
x
x
x
x

## Slide 6: Options for solution
Option 2
  When CRA picture has collocated non-IRAP, inter-layer texture prediction shall not be allowed but inter-layer syntax prediction shall be allowed for the CRA picture and any pictures following it in decoding order until the picture that has collocated IRAP.
CRA
Non-IRAP