## Slide 1: AHG5: Independent chroma transform depth for non 4:2:0 format
J. Kim
JCTVC-M0098

## Slide 2: Introduction
Transform Depth
  Currently in HEVC, chroma components and luma component share one common transform depth.
  Currently in HM, RD costs of chroma components are not included for decision of the transform depth in intra prediction.

## Slide 3: Proposed Method (I)
Independent chroma transform depth
  We propose to use separate transform depth for chroma component
  Chroma transform depth is totally indepedent from luma transform depth
  transform_split_flag for chroma component is coded separately
transform depth | 
luma | chroma
0 | 0
1 | 1
2 | 2
3 | 3
… | …
<Available combinations of transform depths of luma and chroma components>
transform depth |  |  | 
luma | chroma | luma | chroma
0 | 0 | 2 | 0
 | 1 |  | 1
 | 2 |  | 2
 | 3 |  | 3
1 | 0 | 3 | 0
 | 1 |  | 1
 | 2 |  | 2
 | 3 |  | 3
 |  | … | …

## Slide 4: Proposed Method (II)
Partially dependent chroma transform depth
  We propose to use separate transform depth for chroma component
  Chroma transform depth is less than or equal to luma transform depth
  transform_split_flag for chroma component is coded separately but dependant on luma transform depth
    Practically, transform_split_flag for luma component is coded dependently on that for chroma component since derivation of CBF for luma is dependent to CBF for chroma
transform depth | 
luma | chroma
0 | 0
1 | 1
2 | 2
3 | 3
… | …
transform depth |  |  | 
luma | chroma | luma | chroma
0 | 0 | 2 | 0
 |  |  | 1
 |  |  | 2
1 | 0 | 3 | 0
 | 1 |  | 1
 |  |  | 2
 |  |  | 3
 |  | … | …
<Available combinations of transform depths of luma and chroma components>

## Slide 5
Experimental Results in detail (I)
Performance of independent chroma transform depth against HM-Range-extension
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | -0.3% | -0.2% | 0.0% | -0.3% | -0.2% | -0.1% | -0.2% | -0.2%
YCbCr 4:4:4 | -0.1% | -1.2% | -1.1% | 0.0% | -1.0% | -0.7% | -0.1% | -0.8% | -0.6%
YCbCr 4:2:2 | -0.1% | -0.6% | -0.8% | 0.0% | -0.5% | -0.5% | 0.0% | -0.5% | -0.4%
Overall | 0.0% | -0.6% | -0.7% | 0.0% | -0.6% | -0.5% | -0.1% | -0.5% | -0.4%
 | -0.1% | -0.7% | -0.7% | 0.0% | -0.6% | -0.5% | -0.1% | -0.5% | -0.5%
Enc Time[%] | 139% |  |  | 141% |  |  | 143% |  | 
Dec Time[%] | 109% |  |  | 108% |  |  | 106% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | -0.6% | 0.2% | 0.3% | -0.6% | 0.1% | 0.2% |  |  | 
YCbCr 4:4:4 | -0.3% | -0.3% | -0.4% | -0.5% | 0.0% | -0.1% |  |  | 
YCbCr 4:2:2 | -0.3% | -0.1% | -0.7% | -0.3% | -0.1% | -0.3% |  |  | 
Overall | -0.4% | -0.1% | -0.2% | -0.5% | 0.0% | -0.1% |  |  | 
 | -0.4% | 0.0% | -0.3% | -0.5% | -0.6% | 0.0% |  |  | 
Enc Time[%] | 101% |  |  | 103% |  |  |  |  | 
Dec Time[%] | 120% |  |  | 117% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | -0.8% | 0.5% | 0.6% | -0.8% | 0.3% | 0.4% |  |  | 
YCbCr 4:4:4 | -0.5% | 0.5% | 0.4% | -0.7% | 0.4% | 0.5% |  |  | 
YCbCr 4:2:2 | -0.3% | 0.5% | -0.2% | -0.3% | 0.3% | 0.2% |  |  | 
Overall | -0.5% | 0.5% | 0.3% | -0.6% | 0.3% | 0.4% |  |  | 
 | -0.5% | 0.8% | 0.3% | -0.6% | 0.2% | 0.3% |  |  | 
Enc Time[%] | 104% |  |  | 105% |  |  |  |  | 
Dec Time[%] | 125% |  |  | 119% |  |  |  |  | 

## Slide 6
Experimental Results in detail (II)
Performance of partially dependent chroma transform depth against HM-Range-extension
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
YCbCr 4:4:4 | -0.2% | -0.7% | -0.9% | -0.2% | -0.6% | -0.6% | -0.2% | -0.5% | -0.4%
YCbCr 4:2:2 | -0.1% | -0.4% | -0.7% | -0.1% | -0.4% | -0.4% | 0.0% | -0.4% | -0.3%
Overall | -0.1% | -0.4% | -0.6% | -0.1% | -0.4% | -0.4% | -0.1% | -0.3% | -0.3%
 | -0.1% | -0.4% | -0.6% | -0.1% | -0.4% | -0.4% | -0.1% | -0.3% | -0.3%
Enc Time[%] | 109% |  |  | 111% |  |  | 114% |  | 
Dec Time[%] | 108% |  |  | 107% |  |  | 106% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | -1.4% | 1.1% | 0.9% | -1.1% | 1.0% | 1.1% |  |  | 
YCbCr 4:4:4 | -0.9% | 0.6% | 0.2% | -1.3% | 1.0% | 0.7% |  |  | 
YCbCr 4:2:2 | -0.3% | 0.1% | -0.5% | -0.4% | 0.1% | -0.2% |  |  | 
Overall | -0.9% | 0.6% | 0.3% | -0.9% | 0.7% | 0.5% |  |  | 
 | -0.9% | 0.5% | 0.2% | -1.0% | 0.2% | 0.6% |  |  | 
Enc Time[%] | 90% |  |  | 90% |  |  |  |  | 
Dec Time[%] | 122% |  |  | 118% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | -1.8% | 1.6% | 1.6% | -1.3% | 1.2% | 1.7% |  |  | 
YCbCr 4:4:4 | -1.5% | 1.4% | 1.5% | -1.8% | 1.5% | 1.9% |  |  | 
YCbCr 4:2:2 | -0.3% | 0.7% | 0.0% | -0.4% | 0.5% | 0.3% |  |  | 
Overall | -1.2% | 1.3% | 1.0% | -1.2% | 1.1% | 1.3% |  |  | 
 | -1.2% | 1.1% | 1.0% | -1.1% | 1.0% | 1.3% |  |  | 
Enc Time[%] | 93% |  |  | 92% |  |  |  |  | 
Dec Time[%] | 124% |  |  | 118% |  |  |  |  | 

## Slide 7
Experimental Results in detail (III)
Performance of independent chroma transform depth with modified deblocking filter against result (I)
 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
YCbCr 4:4:4 | 0.0% | -0.1% | -0.3% | 0.0% | -0.1% | -0.2% | 0.0% | 0.0% | -0.2%
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Overall | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
 | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1%
Enc Time[%] | 98% |  |  | 98% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 101% |  | 
 | Random Access HE Main-tier |  |  | Random Access HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.0% | -0.2% | -0.1% | 0.0% | -0.1% | -0.1% |  |  | 
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Overall | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | -0.1% |  |  | 
 | 0.0% | 0.1% | -0.1% | 0.0% | 0.1% | -0.1% |  |  | 
Enc Time[%] | 101% |  |  | 100% |  |  |  |  | 
Dec Time[%] | 103% |  |  | 102% |  |  |  |  | 
 | Low delay B HE Main-tier |  |  | Low delay B HE High-tier |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:4:4 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
YCbCr 4:2:2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% |  |  | 
Enc Time[%] | 99% |  |  | 98% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 100% |  |  |  |  | 

## Slide 8: Conclusion
We proposed separating chroma transform depth from luma transform depth for non 4:2:0 format to increase degree of freedom for chroma transform
We also proposed partially dependant chroma transform depth to reduce additional bits and encoding time