## Slide 1: JCTVC-M0105 AHG 9: On position of inter-layer reference pictures
The 13th JCT-VC Meeting
LG Electronics

## Slide 2: Overview
For SHVC RefIdx approach, IL (inter-layer) reference pictures are inserted into RefPicListTempX at the end after short-term and long-term ref pics
JCTVC-L0278 reported that when temporal distance between current and reference pic is far (i.e., current pic in low temporal sub-layer), ILP may be used more often.
Proposal
  Allow dynamic placement of IL ref pics in reference pic lists depending on TemporalId of current picture
  Signal the maximum TemporalId in which for pictures with smaller TemporalId shall insert IL ref pics into ref pics list before short-term and long-term ref pics.

## Slide 3: Positioning IL ref pics based on temporal sub-layer
For pictures with lower TemporalId
  Distance to its inter prediction reference pictures is relatively far
  ILP may be used more often
  Putting IL ref pics in earlier position in reference picture list is beneficial

## Slide 4: Proposed signalling
vps_extension( ) { | Descriptor
… | 
max_sub_layer_ref_layer_at_front_plus1 | u(3)
… | 
} | 
max_sub_layer_ref_layer_at_front_plus1 equals 0 specifies that for picture with nuh_layer_id greater than 0, inter-layer reference pictures shall be inserted into RefPicListTempX after short-term reference pictures and long-term reference pictures. Otherwise, max_sub_layer_ref_layer_at_front_plus1 greater than 0 specifies that for picture with nuh_layer_id greater than 0 and TemporalId less than max_sub_layer_ref_layer_at_front_plus1, inter-layer reference pictures shall be inserted into RefPicListTempX before short-term reference pictures and long-term reference pictures; for picture with nuh_layer_id greater than 0 and TemporalId greater than or equal to max_sub_layer_ref_layer_at_front_plus1, inter-layer reference pictures shall be inserted into RefPicListTempX after short-term reference pictures and long-term reference pictures. The value of max_sub_layer_ref_layer_at_front_plus1 shall never exceed the value of vps_max_sub_layers_minus1 plus 1.

## Slide 5: Proposed signalling
vps_extension( ) { | Descriptor
… | 
max_sub_layer_ref_layer_at_front_plus1 | u(3)
… | 
} | 
max_sub_layer_ref_layer_at_front_plus1
* Equal 0  use current scheme; put IL ref pics after short-term and long-term ref pics
* Between 1 ~ 7
  if TemporalId of current pic < max_sub_layer_ref_layer_at_front_plus1 && nuh_layer_id > 0
    Put IL ref pics before short-term and long-term ref pics
  else if TemporalId of current pic >= max_sub_layer_ref_layer_at_front_plus1 && nuh_layer_id > 0
    Put IL ref pics after short-term and long-term ref pics

## Slide 6: Proposed modification to ref pics list construction

## Slide 7: Proposed modification to ref pics list construction

## Slide 8: Summary and discussion
Inspired by report in L0278
  When temporal distance between current and ref pic is far, ILP may be used more often
  In such case, it should be beneficial to place IL reference pics earlier in ref pic lists.
Proposal:
  Dynamic placement of IL reference pictures in reference picture lists
  Based on TemporalId of current pic
We suggest the JCTVC group to discuss and consider adopting the proposed modification