## Slide 1
JCTVC-M0106
AHG5: Reference sample filtering in intra prediction for extended color format
Junghye Min, Sunil Lee, Chanyul Kim

## Slide 2: Summary
Propose reference sample filtering methods in intra prediction for chroma extended formats
  Apply proposed sample filtering methods for chroma intra prediction
    Methods 1 : additional sample filtering for 4x4 and 8x8 transform units
    Methods 2: Methods1 + strong filtering for large transform units
  performance
    Method 1 : (-0.1%,-0,1%,-0.2%) in AI without additional enc/dec time
    Method 2: (-0.1%,-0.2%, -0.2%) in AI without additional enc/dec time
Additional test was performed with increased number of chroma intra modes.
  Performance
    (-0.1%,-0,3%,-0.4%) in AI without additional enc/dec time

## Slide 3: Introduction -1
Reference sample filtering for intra prediction
  Depending on the transform unit size and intra prediction mode, whether filtered samples are used is determined
HM10.0_RExt2.0
  Sample filtering is applied to chroma intra prediction for 4:4:4 format
  For 4:2:2 format, sample filtering is not used in chroma intra prediction
  Same sample filtering process from luma is applied to chroma component

## Slide 4: Introduction - 2
Motivations
  Chroma component is known to have noises with unnatural patterns
    Chroma component needs strong filtering for reference samples
  To provide optimized designs for chroma intra prediction to improve coding efficiency
Kimono 4:4:4 format

## Slide 5: Reference sample filtering process
Common S/W (same as HM9.0)
diff = min (abs( predMode - HOR_IDX), abs(predMode - VER_IDX));
sizeIndex=getSizeIndex(TuWidth)
filterFlag = diff > m_aucIntraFilter[sizeIndex]? 1:0;
m_aucIntraFilter [] =
{ 10, //4x4
7, //8x8
1, //16x16
0, //32x32
},
 | TU size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 0 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | 2 | 0 | 1 | 1 | 1
 | 3 | 0 | 0 | 1 | 1
 | 4 | 0 | 0 | 1 | 1
 | 5 | 0 | 0 | 1 | 1
 | 6 | 0 | 0 | 1 | 1
 | 7 | 0 | 0 | 1 | 1
 | 8 | 0 | 0 | 1 | 1
 | 9 | 0 | 0 | 0 | 1
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 0 | 1
pred | 12 | 0 | 0 | 1 | 1
mode | 13 | 0 | 0 | 1 | 1
 | 14 | 0 | 0 | 1 | 1
 | 15 | 0 | 0 | 1 | 1
 | 16 | 0 | 0 | 1 | 1
 | 17 | 0 | 0 | 1 | 1
 | 18 | 0 | 1 | 1 | 1
 | 19 | 0 | 0 | 1 | 1
 | 20 | 0 | 0 | 1 | 1
 | 21 | 0 | 0 | 1 | 1
 | 22 | 0 | 0 | 1 | 1
 | 23 | 0 | 0 | 1 | 1
 | 24 | 0 | 0 | 1 | 1
 | 25 | 0 | 0 | 0 | 1
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 0 | 1
 | 28 | 0 | 0 | 1 | 1
 | 29 | 0 | 0 | 1 | 1
 | 30 | 0 | 0 | 1 | 1
 | 31 | 0 | 0 | 1 | 1
 | 32 | 0 | 0 | 1 | 1
 | 33 | 0 | 0 | 1 | 1
 | 34 | 0 | 1 | 1 | 1
Use Filtered samples

## Slide 6: Proposed method 1
Apply filtering for more cases in 4x4 and 8x8 transform units
m_aucIntraFilter [] =
{ 6, //4x4
1, //8x8
0, //16x16
0, //32x32
},
 | block size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 1 | 1 | 1 | 1
 | 1 | 0 | 0 | 0 | 0
 | 2 | 1 | 1 | 1 | 1
 | 3 | 1 | 1 | 1 | 1
 | 4 | 0 | 1 | 1 | 1
 | 5 | 0 | 1 | 1 | 1
 | 6 | 0 | 1 | 1 | 1
 | 7 | 0 | 1 | 1 | 1
 | 8 | 0 | 1 | 1 | 1
 | 9 | 0 | 0 | 1 | 1
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 1 | 1
pred | 12 | 0 | 1 | 1 | 1
mode | 13 | 0 | 1 | 1 | 1
 | 14 | 0 | 1 | 1 | 1
 | 15 | 0 | 1 | 1 | 1
 | 16 | 0 | 1 | 1 | 1
 | 17 | 1 | 1 | 1 | 1
 | 18 | 1 | 1 | 1 | 1
 | 19 | 1 | 1 | 1 | 1
 | 20 | 0 | 1 | 1 | 1
 | 21 | 0 | 1 | 1 | 1
 | 22 | 0 | 1 | 1 | 1
 | 23 | 0 | 1 | 1 | 1
 | 24 | 0 | 1 | 1 | 1
 | 25 | 0 | 0 | 1 | 1
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 1 | 1
 | 28 | 0 | 1 | 1 | 1
 | 29 | 0 | 1 | 1 | 1
 | 30 | 0 | 1 | 1 | 1
 | 31 | 0 | 1 | 1 | 1
 | 32 | 0 | 1 | 1 | 1
 | 33 | 1 | 1 | 1 | 1
 | 34 | 1 | 1 | 1 | 1
Use Filtered samples

## Slide 7: Proposed method 2
Apply strong filter for large transform unit sizes
m_aucIntraFilter [] =
{ 6, //4x4
2, //8x8
1, //16x16
0, //32x32
},
 | block size |  |  |  | 
 |  | 4x4 | 8x8 | 16x16 | 32x32
 | 0 (planar) | 1 | 1 | 2 | 2
 | 1 | 0 | 0 | 0 | 0
 | 2 | 1 | 1 | 2 | 2
 | 3 | 1 | 1 | 2 | 2
 | 4 | 0 | 1 | 2 | 2
 | 5 | 0 | 1 | 2 | 2
 | 6 | 0 | 1 | 2 | 2
 | 7 | 0 | 1 | 2 | 2
 | 8 | 0 | 0 | 2 | 2
 | 9 | 0 | 0 | 0 | 2
 | 10 (horizontal) | 0 | 0 | 0 | 0
intra | 11 | 0 | 0 | 0 | 2
pred | 12 | 0 | 0 | 2 | 2
mode | 13 | 0 | 1 | 2 | 2
 | 14 | 0 | 1 | 2 | 2
 | 15 | 0 | 1 | 2 | 2
 | 16 | 0 | 1 | 2 | 2
 | 17 | 1 | 1 | 2 | 2
 | 18 | 1 | 1 | 2 | 2
 | 19 | 1 | 1 | 2 | 2
 | 20 | 0 | 1 | 2 | 2
 | 21 | 0 | 1 | 2 | 2
 | 22 | 0 | 1 | 2 | 2
 | 23 | 0 | 1 | 2 | 2
 | 24 | 0 | 0 | 2 | 2
 | 25 | 0 | 0 | 0 | 2
 | 26 (vertical) | 0 | 0 | 0 | 0
 | 27 | 0 | 0 | 0 | 2
 | 28 | 0 | 0 | 2 | 2
 | 29 | 0 | 1 | 2 | 2
 | 30 | 0 | 1 | 2 | 2
 | 31 | 0 | 1 | 2 | 2
 | 32 | 0 | 1 | 2 | 2
 | 33 | 1 | 1 | 2 | 2
 | 34 | 1 | 1 | 2 | 2
Use Filtered samples
Use samples from strong filter
c
c
c
c
c
c
c
c
c
c
c
c
3 tap filter
Original
samples
Filtered
samples
c
c
c
c
c
c
3 tap filter
Filtered
Samples
With strong
Filter

## Slide 8: Test results - 1
Chroma formats | Common s/w | Test1 | Test2 | Test3
4:4:4 | Same as luma | Same as luma | Use method 1 | Use method 2
4:2:2 | Not applied | Same as luma | Use method 1 | Use method 2
Sample filtering process for chroma
test 1 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:4:4 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YCbCr 4:2:2 | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
test 2 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1%
YCbCr 4:4:4 | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2%
Overall | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
 | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
test 3 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | -0.2% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
YCbCr 4:4:4 | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1%
YCbCr 4:2:2 | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
Overall | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1%
Enc Time[%] | 101% |  |  | 101% |  |  | 101% |  | 
Dec Time[%] | 101% |  |  | 101% |  |  | 101% |  | 

## Slide 9: Test results - 2
Sample filtering process for chroma with additional intra modes
Anchor | Test4
HM10.0_RExt2.0 with 7 chroma intra modes | Number of chroma intra mode= 7
 | Method1
test 4 | All Intra HE Main-tier |  |  | All Intra HE High-tier |  |  | All Intra HE Super-High-tier |  | 
 | Y | U | V | Y | U | V | Y | U | V
RGB 4:4:4 | -0.1% | -0.2% | -0.3% | -0.1% | -0.1% | -0.3% | -0.1% | -0.1% | -0.1%
YCbCr 4:4:4 | -0.1% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2%
YCbCr 4:2:2 | -0.1% | -0.4% | -0.5% | -0.2% | -0.3% | -0.4% | -0.2% | -0.2% | -0.4%
Overall | -0.1% | -0.3% | -0.4% | -0.1% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2%
 | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.3% | -0.1% | -0.1% | -0.2%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 101% |  | 
Compared with HM10.0_RExt2.0 with 7 chroma intra modes

## Slide 10: Conclusions
Proposed methods provide additional gains in all color components without increase in encoding and decoding time
With increased chroma intra prediction modes, better performance gains are obtained.
Code changes from HM10.0_RExt2.0 are minimal.
We recommend adopting the proposed sampling filtering method for the common s/w with range extension
We would like to thank LG for the crosscheck of this proposal.

## Slide 11
Thank you !