## Slide 1: JCTVC-M0114 Non SCE4: On Interlayer SAO filtering in SHVC
G. Laroche, P. Onno, J. Taquet
E. François, C. Gisquet
13th JCTVC Meeting, Incheon, April 2013
1

## Slide 2: Context of this contribution
A simplification of the Interlayer SAO contribution initially proposed in JCTVC-L0234 and studied in CE4.2.1 experiment (JCTVC-M0265 from Qualcomm).
  SAO Interlayer filtering is applied on the high-frequencies content of the Base Layer

## Slide 3: Principle of this SAO proposal
No pre-filtering process of the base layer
  Change the way the SAO is performed for the Interlayer filtering in SCE4.2.1

## Slide 4: Slight change in SAO
Band Offset remains unchanged
Edge Offset is slightly modified as follows
  The computation of the Edge Index is modified
  It now relies on two neighbors instead of one neighbor in HEVC version 1
  No change for SAO class and SAO offset determination
SAO neighbor for HEVC
version 1
SAO neighbor for this proposal

## Slide 5: Details in the SAO EdgeIndex computation
EdgeIndex in HEVC version 1 is
  EdgeIndex(c) = sign (c - cn2) - sign (cn1- c) +2
EdgeIndex modification
  Keep the principle of CE4.2.1 where SAO is applied on the high-frequency band of the up-sampled base layer
  Introduction of a high pass filter [-1 2 -1] during the Egde determination.
  EdgeIndex(c) = = sign( ((2c-cn1-cn2+2)>>2)-((2cn2-c-cn4+2)>>2) ) - sign( ((2cn1-cn3-c+2)>>2)-((2c-cn1-cn2+2)>>2) )+2

## Slide 6: Experiments results - IntraBL
Reference: SHM1.0
Average BDR performance gain is -0.8%(Y), -0.6%(U), -0.6%(V)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -1.0% | -1.3% | -1.4% |  |  |  |  |  | 
Class B | -0.2% | -0.3% | -0.3% | -0.2% | -0.4% | -0.5% |  |  | 
Overall (Test vs Ref) | -0.4% | -0.6% | -0.6% | -0.2% | -0.4% | -0.5% |  |  | 
Overall (Test vs single layer) | 12.0% | 13.0% | 12.7% | 10.1% | 9.9% | 9.2% |  |  | 
EL only (Test vs Ref) | -0.8% | -1.0% | -1.0% | -0.2% | -0.4% | -0.5% |  |  | 
Enc Time[%] | 100.7% |  |  | 100.9% |  |  |  |  | 
Dec Time[%] | 104.0% |  |  | 105.1% |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.0% | -0.6% | -0.8% |  |  |  | -2.4% | -1.1% | -1.3%
Class B | -0.2% | -0.2% | -0.2% | -0.3% | -0.5% | -0.5% | -1.0% | -0.3% | -0.2%
Overall (Test vs Ref) | -0.5% | -0.3% | -0.4% | -0.3% | -0.5% | -0.5% | -1.4% | -0.6% | -0.5%
Overall (Test vs single layer) | 18.8% | 31.6% | 32.6% | 16.2% | 28.0% | 30.3% | 13.2% | 28.2% | 32.1%
EL only (Test vs Ref) | -0.9% | -0.7% | -0.8% | -0.4% | -0.5% | -0.5% | -2.3% | -1.3% | -1.3%
Enc Time[%] | 101.1% |  |  | 100.7% |  |  | 100.5% |  | 
Dec Time[%] | 106.4% |  |  | 107.0% |  |  | 110.7% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.1% | -0.8% | -0.8% |  |  |  | -3.4% | -1.7% | -1.6%
Class B | -0.5% | -0.5% | -0.4% | -0.8% | -0.9% | -0.9% | -1.7% | -0.6% | -0.4%
Overall (Test vs Ref) | -0.7% | -0.6% | -0.5% | -0.8% | -0.9% | -0.9% | -2.2% | -0.9% | -0.8%
Overall (Test vs single layer) | 25.2% | 35.8% | 37.5% | 21.5% | 32.0% | 34.8% | 19.6% | 33.2% | 38.1%
EL only (Test vs Ref) | -1.1% | -0.9% | -0.9% | -1.0% | -1.1% | -1.1% | -3.1% | -1.8% | -1.6%
Enc Time[%] | 101.0% |  |  | 100.7% |  |  | 101.5% |  | 
Dec Time[%] | 108.8% |  |  | 109.8% |  |  | 113.9% |  | 

## Slide 7: Experiments results - RefIdx
Reference: SHM1.0
Average BDR performance gain is -0.8%(Y), -0.7%(U), -0.6%(V)
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  |  |  |  | 
 | Y | U | V | Y | U | V |  |  | 
Class A | -1.0% | -1.2% | -1.3% |  |  |  |  |  | 
Class B | -0.2% | -0.2% | -0.2% | -0.2% | -0.4% | -0.5% |  |  | 
Overall (Test vs Ref) | -0.4% | -0.5% | -0.5% | -0.2% | -0.4% | -0.5% |  |  | 
Overall (Test vs single layer) | 12.4% | 14.5% | 14.2% | 10.3% | 9.5% | 9.0% |  |  | 
EL only (Test vs Ref) | -0.8% | -0.9% | -1.0% | -0.2% | -0.4% | -0.5% |  |  | 
Enc Time[%] | 100.5% |  |  | 99.8% |  |  |  |  | 
Dec Time[%] | 106.9% |  |  | 107.2% |  |  |  |  | 
 | RA HEVC 2x |  |  | RA HEVC 1.5x |  |  | RA HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.0% | -0.7% | -0.7% |  |  |  | -2.4% | -1.9% | -2.0%
Class B | -0.2% | -0.3% | -0.2% | -0.3% | -0.3% | -0.3% | -1.0% | -0.8% | -0.7%
Overall (Test vs Ref) | -0.4% | -0.4% | -0.3% | -0.3% | -0.3% | -0.3% | -1.4% | -1.1% | -1.1%
Overall (Test vs single layer) | 19.6% | 32.7% | 33.8% | 17.0% | 27.7% | 30.2% | 14.2% | 28.6% | 33.3%
EL only (Test vs Ref) | -0.8% | -0.8% | -0.7% | -0.3% | -0.3% | -0.3% | -2.2% | -1.9% | -1.9%
Enc Time[%] | 100.6% |  |  | 100.6% |  |  | 101.0% |  | 
Dec Time[%] | 107.0% |  |  | 107.2% |  |  | 111.6% |  | 
 | LD-P HEVC 2x |  |  | LD-P HEVC 1.5x |  |  | LD-P HEVC SNR |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A | -1.0% | -0.7% | -0.7% |  |  |  | -3.5% | -2.2% | -2.2%
Class B | -0.5% | -0.5% | -0.2% | -0.8% | -0.8% | -0.8% | -1.7% | -1.3% | -1.0%
Overall (Test vs Ref) | -0.7% | -0.5% | -0.3% | -0.8% | -0.8% | -0.8% | -2.2% | -1.5% | -1.3%
Overall (Test vs single layer) | 25.8% | 37.1% | 38.7% | 22.0% | 31.8% | 34.6% | 20.6% | 32.6% | 37.6%
EL only (Test vs Ref) | -1.0% | -0.9% | -0.7% | -0.9% | -1.0% | -0.9% | -3.2% | -2.5% | -2.3%
Enc Time[%] | 100.7% |  |  | 101.0% |  |  | 100.9% |  | 
Dec Time[%] | 111.2% |  |  | 111.3% |  |  | 114.4% |  | 

## Slide 8: Comparison with CE4.2.1 for IntraBL
CE4.2.1 (M0265)
Reference: SHM1.0
Average BDR performance gain is
  -0.8%(Y), -1.0%(U), -1.0%(V)
Run time
  Enc: 100%
  Dec: 193%
 | BDR |  |  | Run Time | 
 | Y | U | V | ENC | DEC
AI HEVC 2x | 0.0% | -0.4% | -0.4% | 101.1% | 151.4%
AI HEVC 1.5x | -0.4% | -0.6% | -0.7% | 100.9% | 155.5%
RA HEVC 2x | -0.3% | -0.5% | -0.6% | 100.9% | 210.4%
RA HEVC 1.5x | -0.6% | -0.8% | -0.8% | 100.6% | 202.2%
RA HEVC SNR | -1.3% | -0.7% | -0.7% | 100.3% | 221.8%
LD-P HEVC 2x | -0.7% | -1.2% | -1.2% | 101.3% | 198.6%
LD-P HEVC 1.5x | -1.0% | -2.0% | -1.7% | 101.0% | 193.1%
LD-P HEVC SNR | -2.2% | -1.6% | -1.7% | 100.7% | 213.6%
Average | -0.8% | -1.0% | -1.0% | 100.9% | 193.3%
 | BDR |  |  | Run Time | 
 | Y | U | V | ENC | DEC
AI HEVC 2x | -0.4% | -0.6% | -0.6% | 100.7% | 104.0%
AI HEVC 1.5x | -0.2% | -0.4% | -0.5% | 100.9% | 105.1%
RA HEVC 2x | -0.5% | -0.3% | -0.4% | 101.1% | 106.4%
RA HEVC 1.5x | -0.3% | -0.5% | -0.5% | 100.7% | 107.0%
RA HEVC SNR | -1.4% | -0.6% | -0.5% | 100.5% | 110.7%
LD-P HEVC 2x | -0.7% | -0.6% | -0.5% | 101.0% | 108.8%
LD-P HEVC 1.5x | -0.8% | -0.9% | -0.9% | 100.7% | 109.8%
LD-P HEVC SNR | -2.2% | -0.9% | -0.8% | 101.5% | 113.9%
Average | -0.8% | -0.6% | -0.6% | 100.9% | 108.8%
This contribution
Reference: SHM1.0
Average BDR performance gain is
  -0.8%(Y), -0.6%(U), -0.6%(V)
Run time
  Enc: 100%
  Dec: 109%

## Slide 9: Complexity analysis - IntraBL
Average memory access
  By using the complexity assessment module from AhG17.
  No impact for the worse case.
  Memory access in average on the test set of the CTC
  M0265
Average |  |  |  | 
8b/8b | 64b/256b | 64b/512b | Mults | Adds
107% | 103% | 104% | 108% | 108%
Average |  |  |  | 
8b/8b | 64b/256b | 64b/512b | Mults | Adds
117% | 118% | 121% | 109% | 129%

## Slide 10: Complexity analysis - RefIdx
Average memory access
  By using the complexity assessment module from AhG17.
  No impact for the worse case.
  Memory access in average on the test set of the CTC
  M0265
Average |  |  |  | 
8b/8b | 64b/256b | 64b/512b | Mults | Adds
101% | 100% | 100% | 100% | 178%
Average |  |  |  | 
8b/8b | 64b/256b | 64b/512b | Mults | Adds
131% | 131% | 132% | 119% | 163%

## Slide 11: Conclusion
This contribution presents a simplification of the SAO Interlayer technique presented in CE4.2.1
The BDR performance is the same as CE4.2.1
  -0.8%(Y), -0.6%(U), -0.6%(V)
Complexity
  Does not affect the worse case of SHM1.0
  Adds/Mults operations are reduced, as well as memory access on average compared to SCE4.2.1
Recommendation
  Further study this approach in CE related to the Interlayer prediction improvement
Thanks to MediaTek for the cross-check
  JCTVC-M0390