## Slide 1: Non-CE1: Weighted intra prediction
C. Kim, B. Jeon (LG)
JCTVC-M0117
JCTVC-M0117

## Slide 2: Proposed method(1/3)
In this contribution,
  Weighted intra prediction (WIP) that uses reconstructed base layer texture to improve enhancement layer sample predictor.
  In below figure, Dh and DV represent horizontal and vertical distances between P and R respectively.
  As Dh and Dv increase, spatial correlation decreases so that accuracy of P is reduced.
JCTVC-M0117

## Slide 3: Proposed method(2/3)
In this contribution,
  In order to increase accuracy of predictor, a method of using P, which is created by intra prediction of the current layer, and collocated sample B of the base layer at the same time is proposed according to Dh and Dv.
  Below equation shows the process of how to obtain the final prediction value P’x,y .
JCTVC-M0117
PVx,y = (N – y)·Px,y + y·Bx,y
PHx,y = (N – x)·Px,y + x·Bx,y
P’x,y = (PVx,y + PHx,y + N) >> (log2(N) + 1)
B(X,Y)
Collocated base layer sample

## Slide 4: Proposed method(3/3)
‘WIP_flag’ is signaled CU level after the pred_mode.
  If the intra_BL_flag is false and pred_mode is intra and Size is 2Nx2N , WIP_flag is signaled.
  a method of checking rd-cost once the proposed method is applied to the best mode of normal intra prediction
JCTVC-M0117

## Slide 5: Experimental Results
Simulation results reportedly show 0.2% and 0.1% BD-rate savings on average for AI-2x and AI-1.5x, respectively, compared with SHM 1.0 anchors
JCTVC-M0117