## Slide 1: Non-CE 1: Constrained intra prediction at enhancement layer
C. Kim, B. Jeon (LG)
JCTVC-M0123
JCTVC-M0123

## Slide 2: Overall Summary
CIP(constrained intra prediction) at enhancement layer
  if slice type of base layer is Intra,
  Intra BL CU should be used in intra prediction.
Results for AI-2x and AI-1.5x
  Anchor SHM 1.0 (CIP On)
  BD rate savings : 1.3% and 0.2%
  Encoding times : 105.0% and 104.7%
  Decoding times : 106.4% and 102.3%
JCTVC-M0123

## Slide 3: Proposed method
In current SHM 1.0,
  when constrained intra prediction (CIP) is enabled,
  Only intra coded neighboring PUs can be used in intra prediction.
  Intra BL CU cannot be used in intra prediction.
In this contribution,
  If CIP of base layer is enabled,
  an intra BL CU at the enhancement layer that refers to an intra coded CU at the base layer should be used in intra prediction
JCTVC-M0123

## Slide 4: Proposed method
Checking of prediction mode of collocated BL PU
  In SHM 1.0, it will check the prediction modes of the neighboring 4x4 PU
  In case of non-dyadic scalability, an enhancement layer PU may cover inter and intra PUs from base layer.
  To solve this problem, it is checked all Adjacent position.
JCTVC-M0123

## Slide 5: Experimental Results(Intra)
Anchor: SHM 1.0(CIP On)
JCTVC-M0123

## Slide 6: Conclusion
This proposal suggests that when CIP is enabled,
  If CIP of base layer is enabled, an intra BL CU at the enhancement layer that refers to an intra coded CU at the base layer should be used in intra prediction
Simulation results reportedly show 0.1-1.3% bit rate reduction compared with SHM 1.0 anchor(CIP on)
JCTVC-M0123

## Slide 7: Experimental Results(Inter)
Anchor: SHM 1.0(CIP On)
JCTVC-M0123