## Slide 1: JCTVC-M0129 AHG 9: Inter-layer Prediction Indication at Picture Level
The 13th JCT-VC Meeting
LG Electronics

## Slide 2: Overview
Two flags are proposed to be signaled in slice header to indicate the use of inter-layer prediction (ILP)
  ilp_flag – specifies whether or not current picture is used for ILP
  ilp_ref_flag – specifies whether or not current picture is used for inter prediction by other picture(s) whose ilp_flag equals 1.
Benefits of having those two flags:
  Easy to determine whether or not a picture in a non-target layer needs to be delivered / to be decoded
  Enable a single RPS to be used for multiple layers when their temporal structure are the same
  Enable to limit the required DPB size when decoding any target layer

## Slide 3: Case #1 – only highest layer needs to be outputted
TargetDecLayerIdList = {0, 1}
TargetOutputLayerIdList = {1}
Pictures need to be decoded: (00 01) (80 81) (40 41) (21) (11) (31) (61) (51) (71) (160 161) (120 121) (102) (92) (112) (142) (131) (151)

## Slide 4: Case #2 – both layers need to be outputted
TargetDecLayerIdList = {0, 1}
TargetOutputLayerIdList = {0, 1}
Pictures need to be decoded: (00 01) (80 81) (40 41) (20 21) (10 11) (30 31) (60 61) (50 51) (70 71) (160 161) (120 121) (100 101) (90 91) (110 111) (140 141) (130 131) (150 151)

## Slide 5: Proposal -- Signalling
ilp_flag indicates that current slice may be used for inter-layer prediction. It is requirement of the bitstream that the value of this flag shall be the same in all slice segment headers of a coded picture.
ilp_ref_flag indicates that current slice may be referred / used for inter prediction by other picture(s) that are needed for inter-layer prediction. It is requirement of the bitstream that the value of this flag shall be the same in all slice segment headers of a coded picture.
slice_segment_header( ) { | Descriptor
… | 
ilp_flag | u(1)
ilp_ref_flag | u(1)
… | 
} | 

## Slide 6: Proposal – Decoding process
Introduce new list called: TargetOutputLayerIdList
  List of nuh_layer_id whose reconstructed pictures are needed for output / display.
  For SHVC, it may contain only the highest layer id
    E.g., case #1
  May be modified by external means
The following pics not need to be decoded
  Both ilp_flag and ilp_ref_flag are 0
  nuh_layer_id is not included in TargetOutputLayerIdList

## Slide 7: Proposal – Ref pic marking
After decoding of a coded picture at the highest nuh_layer_id, mark reference pic from reference layer as “unused for reference” if:
  It has the same POC with current picture
  Its ilp_flag = 1 and ilp_ref_flag = 0
Motivation:
  Early marking of reference pictures as unused as soon as it is not needed
  Save DPB space

## Slide 8: Proposal – Reference picture list construction
Concept:
  Reference picture list construction should consider the value of ilp_flag and ilp_ref_flag.
Required action:
  Only inter-layer reference picture whose POC equals to POC of current picture and ilp_flag equals 1 shall be included into RefPicSetInterLayer[i]
  If ilp_flag of current picture equals 1, only reference pictures whose ilp_ref_flag equals 1 shall be included into RefPicListTempX
  If ilp_flag of current picture equals 0, no change to current ref pic list construction

## Slide 9: Summary and discussion
Two flags are proposed to described whether or not a picture is needed for ILP by picture in higher layer
  ilp_flag
  ilp_ref_flag
Based on the proposed two flags, some modification are needed:
  Decoding process  pictures that are not needed for ILP should not be decoded
  Reference picture marking process at the end of decoding picture of the highest layer
    Allow early marking picture unused for reference
  Reference picture list construction
We suggest the JCTVC group to discuss and consider adopting the proposed flags and modifications