## Slide 1: JCTVC-M0130 AHG 9: Signalling required DPB size in layer set
The 13th JCT-VC Meeting
LG Electronics

## Slide 2: Overview
Required DPB size for decoding process at a particular layer can be different
  Depending on the use of inter-layer prediction (ILP)
  Pictures that are not needed for ILP can be skipped from decoding, thus, lower requirement for DPB storage
The information is useful for decoder in session negotiation to determine the highest layer the decoder can handle.
Proposed in L0262 and was suggested that perhaps such information should be conveyed in layer set.

## Slide 3: Use-case scenario
Depending on layer set, required DPB size for each layer may be different

## Slide 4: Signalling – Option #1
layer_set_max_dec_pic_buffering_minus1[ i ][ j ] plus 1 specifies the maximum required size of the decoded picture buffer for the CVS in units of picture storage buffers for decoding of pictures with layer id equals j and layer set i is being the target layer set for decoding
vps_extension ( ) { | Descriptor
… | 
for( i = 1; i <= vps_num_layer_sets_minus1; i++ ) | 
for( j = 0; j <= vps_max_layer_id; j++ ) | 
if( layer_id_included_flag[ i ][ j ] ) | 
layer_set_max_dec_pic_buffering_minus1[ i ][ j ] | ue(v)
… | 
} | 

## Slide 5: Signalling – Option #2
layer_set_dec_pic_buffering_info_present_flag equals 1 indicates that the syntax element layer_set_max_dec_pic_buffering[ i ][ j ] is present. Otherwise, layer_set_dec_pic_buffering_info_present_flag equals 0 indicates that the syntax element layer_set_max_dec_pic_buffering[ i ][ j ] is not present
layer_set_max_dec_pic_buffering_minus1[ i ][ j ] – same as in option #1
Have a control flag to indicate whether or not layer_set_max_dec_pic_buffering_minus1 presents
vps_extension ( ) { | Descriptor
… | 
layer_set_dec_pic_buffering_info_present_flag | u(1)
for( i = 1; i <= vps_num_layer_sets_minus1; i++ ) | 
for( j = 0; j <= vps_max_layer_id; j++ ) | 
if(layer_set_dec_pic_buffering_info_present_flag && layer_id_included_flag[ i ][ j ]) | 
layer_set_max_dec_pic_buffering_minus1[ i ][ j ] | ue(v)
… | 
} | 

## Slide 6: Remarks & Conclusion
It is proposed for layer set to signal DPB size of each layer
  i.e., layer_set_max_dec_pic_buffering_minus1[i][j]
This helps decoder to understand how many decoded picture buffers are necessary when it works on a particular layer set
Two signalling methods are offered:
  Option 1: always signal the syntax element layer_set_max_dec_pic_buffering_minus1[i][j] for each layer in layer set
  Option 2: have a control flag to indicate whether or not the layer_set_max_dec_pic_buffering_minus1[i][j] for each layer in layer set presents
Suggest JCTVC group to discuss and consider adopting one of the proposed option.