## Slide 1: JCTVC-M0131 AHG 9: Sub-bitstream extraction for pictures not needed for ILP
The 13th JCT-VC Meeting
LG Electronics

## Slide 2: Overview
For multi-layer HEVC extension, some pictures in certain layers are not necessary to be decoded
  In the layer that is not to be outputted
  Not needed for ILP
Current sub-bitstream extraction process
  Consider TemporalId and list of layerId for target decoding
  Not consider layerId for target output yet
Proposal:
  Add mechanism to remove pictures in non output target layer that are not needed for ILP.
NOTE: related to contribution JCTVC-M0203

## Slide 3: Use-case scenario
The highest temporal sub-layer to be decoded is 3
List of target layer for decoding is {0, 1}
List of maximum sub-layer for ILP in each layer {1, 3}
List of target layer for output {1}

## Slide 4: Proposal
Pictures in layers that are not to be outputted and are not needed for ILP should be removed from bitstream
  Avoid them to be feed into decoder to save resources
Required modification
Inputs to this process are a bitstream, a target highest TemporalId value tIdTarget, and a target layer identifier list layerIdListTarget, and a target layer identifier list layerIdListOutput
Remove all NAL units with nuh_layer_id among the values included in layerIdListTarget but not among the values included in layerIdListOutput; nal_unit_type is not one of intra random access point (IRAP) picture; and max_sublayer_for_ilp_plus1[nuh_layer_id] equals 0
Remove all NAL units with nuh_layer_id among the values included in layerIdListTarget but not among the values included in layerIdListOutput; and TemporalId equals to or greater than max_sublayer_for_ilp_plus1[nuh_layer_id]