## Slide 1: Non SCE1: Inter-layer intra mode prediction
Xuguang Zuo, Lu Yu (Zhejiang University)
Presented by Xuguang Zuo
13th JCT-VC Meeting in Incheon
18-26 Apr., 2013

## Slide 2: Outline
Algorithm description
Experimental results
Conclusions

## Slide 3: Algorithm description
The modes of the left neighbor, above neighbor and BL co-located block of EL block are tagged as ModeLeft, ModeTop and ModeBL.
Chang ModeLeft, ModeTop according to BL blocks when they are IntraBL mode.
Use ModeLeft, ModeTop and ModeBL to derive the MPM list.

## Slide 4: Method 2
Step1: When left or above neighbour is IntraBL mode. if the co-located BL block of EL block is intra mode, the intra mode of the co-located BL block of EL block will be assigned to ModeLeft or ModeTop.

## Slide 5: Method 2
Step2: Derive the MPM list of EL block with ModeLeft, ModeTop and ModeBL:
When ModeBL is intra and is not planar/dc, MPM list derived as follows:
  If all of ModeLeft, ModeTop and ModeBL are the same, signed as MODE3:
MPM[0] = MODE3, MPM[1] = MODE3 + 1, MPM[2] = MODE3 - 1.
  If two of ModeLeft, ModeTop and ModeBL are the same, signed as MODE2, the rest different one is signed as MODE1:
    If MODE2 > 1, then
    MPM[0] = MODE2, MPM[1] = MODE2 + 1 , MPM[2] = MODE2 - 1.
    Otherwise,
    MPM[0] = MODE2, MPM[1] = MODE1,
    MPM[2] = ( MODE1 > 1) ? !MODE2 : vertical
  If ModeLeft, ModeTop and ModeBL are different from each other,
MPM[0] = ModeBL, MPM[1] = ModeLeft, MPM[2] = ModeTop.
Otherwise, derive the MPM list the same way as the base layer.

## Slide 6: Method 1
Step1: When left or above neighbour is IntraBL mode. If the co-located BL block of left or above neighbour is intra coded, the intra mode of the co-located BL block of left or above neighbour will be assigned to ModeLeft or ModeTop.
Step2: The same as method2.

## Slide 7: Experimental Results
Anchor – SHM1
Thank Sony for cross verifying our results (JCTVC-M0357).
Table 1 Summary of simulation results of Method 1 with MDCS on
Table 2 Summary of simulation results of Method 1 with MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.25% | -0.13% | -0.08% |  |  | 
Class B | -0.36% | -0.23% | -0.26% | -0.10% | 0.03% | 0.00%
Overall (Test vs Ref) | -0.33% | -0.21% | -0.21% | -0.10% | 0.03% | 0.00%
Overall (Test vs single layer) | 12.04% | 13.41% | 13.13% | 10.19% | 10.32% | 9.71%
EL only (Test vs Ref) | -0.48% | -0.35% | -0.36% | -0.08% | 0.08% | 0.04%
Enc Time[%] | 107.4% |  |  | 82.3% |  | 
Dec Time[%] | 102.6% |  |  | 100.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.20% | -0.02% | 0.00% |  |  | 
Class B | -0.22% | -0.07% | -0.03% | -0.10% | 0.01% | 0.01%
Overall (Test vs Ref) | -0.22% | -0.06% | -0.03% | -0.10% | 0.01% | 0.01%
Overall (Test vs single layer) | 12.18% | 13.59% | 13.36% | 10.19% | 10.30% | 9.72%
EL only (Test vs Ref) | -0.34% | -0.17% | -0.14% | -0.10% | 0.03% | 0.03%
Enc Time[%] | 131.1% |  |  | 71.4% |  | 
Dec Time[%] | 107.2% |  |  | 100.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 8: Experimental Results
Table 3 Summary of simulation results of Method 2 with MDCS on
Table 4 Summary of simulation results of Method 2 with MDCS off
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.29% | -0.15% | -0.08% |  |  | 
Class B | -0.39% | -0.27% | -0.30% | -0.11% | 0.03% | 0.01%
Overall (Test vs Ref) | -0.36% | -0.23% | -0.23% | -0.11% | 0.03% | 0.01%
Overall (Test vs single layer) | 12.01% | 13.38% | 13.10% | 10.19% | 10.32% | 9.71%
EL only (Test vs Ref) | -0.52% | -0.38% | -0.39% | -0.08% | 0.07% | 0.04%
Enc Time[%] | 87.7% |  |  | 63.6% |  | 
Dec Time[%] | 104.7% |  |  | 99.5% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 
 | AI HEVC 2x |  |  | AI HEVC 1.5x |  | 
 | Y | U | V | Y | U | V
Class A | -0.23% | -0.05% | -0.02% |  |  | 
Class B | -0.25% | -0.10% | -0.07% | -0.11% | 0.01% | 0.02%
Overall (Test vs Ref) | -0.24% | -0.08% | -0.05% | -0.11% | 0.01% | 0.02%
Overall (Test vs single layer) | 12.15% | 13.56% | 13.33% | 10.19% | 10.30% | 9.72%
EL only (Test vs Ref) | -0.37% | -0.20% | -0.17% | -0.10% | 0.03% | 0.04%
Enc Time[%] | 89.1% |  |  | 57.4% |  | 
Dec Time[%] | 103.7% |  |  | 99.6% |  | 
Enc Mem[%] | #DIV/0! |  |  | #DIV/0! |  | 
BL Match | Matched |  |  | Matched |  | 

## Slide 9: Conclusion
In this contribution, MPM list construction using ModeLeft, ModeTop and ModeBL is proposed.
Coding efficiency is improved.

## Slide 10
Thank you!